## Slide 1: Current status of data acquisition electronics at the FLNP, JINR, Dubna
Elena Litvinenko,
Feodosiy Levchanovsky, Valentin Prikhodko, Sergey Kulikov, Valeriy Zhuravlev
FLNP JINR Dubna
litvin@nf.jinr.ru

## Slide 2: Outlook
Long-term program at the FLNP development of a new generation of data acquisition systems for complex of spectrometers of IBR2 reactor
DeLiDAQ-1 lessons (see Thomas Wilpert report)
The latest developments of DAQ electronics at the FLNP
Status of DeLiDAQ-2 development
MPD16 hardware and its usage (here MPD = “Multi Point Detector”)
In addition - a few words about status of new projects at the FLNP Detector Group

## Slide 3: Long-term program at the FLNP
JINR Topical Plan. Theme 04-4-1075-2009/2011->2014
Novel Development and Creation of Equipment for the IBR-2M Spectrometer Complex
S.A. Kulikov, V.I. Prikhodko
Research, development, manufacturing of prototypes and working models of perspective neutron detectors.
Development and creation of new generation of data acquisition and experiment control systems for the IBR-2 spectrometer complex.
Development of new sample environment systems including cryostats and cryomagnetic systems and beam forming systems for the IBR-2 spectrometer complex.

## Slide 4: DeLiDAQ-1 (since 2001)
Project, design and implementation:
  B.Gebauer, K.Shultz, Т.Wilpert, V.I.Prikhodko, F.V.Levchanovsky, A.S.Nikiforov, E.I.Litvinenko
Interface with CARESS (HZB, Berlin):
  L.Rossa, O.-P.Sauer, T.Wilpert, E.I.Litvinenko
The first users at the FLNP:
  A.A.Bogdzel, A.M.Balagurov, T.L.Enik, V.Proglyado, V.G.Simkin, V.N.Shvetzov, A.Churakov
Interface with SONIX+ (FLNP JINR):
  A.S.Kirilov, S.M.Murashkevich, E.I.Litvinenko,V.I.Prikhodko
http://wwwinfo.jinr.ru/~elitvin/DeLiDAQ/

## Slide 5: DeLiDAQ-1 systems at the FLNP
Detector  Preamplifiers  Discriminator  DeLiDAQ-1 < PCI < PC software
PC

## Slide 6: Prerequisites for transfer from DeLiDAQ-1 to DeLiDAQ-2
What is bad?
1. The PCI interface of the board is out of date for a new PC generation;
2. DSP has only one external data bus to process and transfer detector data:
TDC to DSP, DSP to memory and memory to DSP, DSP to PCI bus;
3. Low speed data transfer ability of TDC F1;
4. In spite of FPGA event filtering procedure, the DSP data processing rate is too small.
What tasks have been decided during design of a new DAQ-board?
 two parts – one base board (NIM) and two data communication boards (PC interface), realized as daughter boards;
 USB2.0 - a possibility to connect DAQ-system to any PC’s, including Note-Books (important);
 No DSP, all data processing tasks are performing by FPGA;
 Fiber link connection between computer USB port and DAQ-board for increasing distance and abolishing EMI problem;
 A new simpler (no built-in seek event function) but an order faster TDC GPX (I-mode);
 Four times larger hist. memory – 1Gbyte (256MW x 32bits);
 Improved test generator can issue any pattern of simulating events including overlapped ones;
 Possibility to work in synchrotron radiation experiments (tested in FPGA 2Mevents/sec);
 Low jitter system clock on the base board - 40MHz, 5ppm;
 2 inputs for monitor detectors, “GATE” and “KICK” pulse inputs.

## Slide 7: DeLiDAQ-2 architecture

## Slide 8: Specially developed communication protocol
Serial Communication Protocol:
 Lighten like SFPDP VITA 17.1 protocol (used protocol approach only);
 Bi-directional links;
 Four types of frames supported (RD/WR/FILL memory, RD/WR registers, ACK/NACK/BUSY, idle);
 Dataflow control in both directions (receiving FIFO is full);
 Very low latency;
 Packet size – 512 bytes (natural USB2.0 packet size);
 Powerful 32-bit CRC code data protection (like Ethernet one);
 Repeat previous packet if transmit error (loop back NACK frame);
 Transparent or invisible to user, absent any software.
 Frame structure: packet type or Start_of_Frame, Data Packet, CRC code (SoF = 16 bit, CRC = 32 bit);

## Slide 9
Gate
TOF
From MWPC
Daughter Board
Data
WR
RD
NIM-TTL
TDC-GPX
Anode
X1
X2
Y1
Y2
FPGA
EP1C6Q240C6
Hist.
Memory
1GByte
WE
RAS
CAS
Parallel2Serial
Serial2Parallel
Optical
Converter
Fiber Link
1.25Gb/s
DeLiDAQ-2: recent design and look

## Slide 10
Before and now…

## Slide 11: Modernization of electronics at FLNP – change-over to direct control from PC and unification

## Slide 12: Prerequisites for the establishment of the project MPD16 at the FLNP
Descriptors of event started become bigger than the address field of the memory for histogram
Integral accumulation leads to impossibility to study the reasons of different artifacts at the spectrometers (happened at HRFD and Epsilon)
Performance of personal computer and disk storage capacity began to be adequate to the task of the list mode data accumulation
To provide DAQ for different types of neutron spectrometers at IBR-2M
Number of detector elements <= 256
Mean count rate: 10 4 events*detector elements/seconds
Time accuracy >= 32 nsec
Registration in absolute experimental time >= 106 seconds
Requirements
Realization
Yes
<= 240 (246)
Frequency 62.5 MHz
16 nsec
4.5 * 106 seconds

## Slide 13: MPD16 architecture

## Slide 14: MPD16 features
Mask register at the entrances of the detector elements
Histogram memory 64 Mb for visualization, on-line control, or accumulation in low resolution mode
Individual time bin width for each detector element (if data are accumulated into histogram memory)
Test generator exists
USB2.0 interface (480 Mb/sec). Later will be USB3.0 (5.6 Gb/sec)
Optical fiber up to 100 m between DAQ board and USB adapter
Overall performance 8Mevents/sec or 30Kevents/sec per detector element (if 240 detectors are used)

## Slide 15
Testing of the communication protocol
Electronic blocks MPD16. Data transmission between DAQ and USB via a serial fiber-optic line
The De-Li-DAQ2 block. Data transmission between DAQ and USB via a serial fiber-optic line

## Slide 16
“Multisection ring detector of thermal neutrons for diffraction studies on microsamples in axial geometry”
V.M. Milkov, Ts. Ts. Panteleev, A. A. Bogdzel, A.V. Belushkin, S.A. Kulikov, V.V.Zhuravlev, V.I.Prikhodko, F. V. Levtchanovski
The use of electronics MPD-16 in the FLNP: Multi-section ring detector project

## Slide 17
The use of MPD-16 in the Karpov Institute (Obninsk): Experiment automation system for a neutron powder diffractometer
A.A.Bogdzel, S.Veleshki, A.I.Zhuravlev, V.V.Zhuravlev, F.V.Levchanovskiy, A.S.Kirilov, M.V.Mikhin, T.B.Petukhova, S.M.Murashkevich, V.I.Prikhodko, A.P.Sirotin, A.I.Kalyukanov, L.E.Fykin

## Slide 18
“Boron-10 thin film multi-wire gas detectors for thermal and ultra-cold neutrons”
A. Bogdzel, T. Enik, V. Kruglov
Detector group developments: Boron-10 thin film detectors