## Slide 1: FPGAs in Research - Applications, Technologies and Tools
FPGA Oriented HW/FW Development in FEA DESY
Frantisek Krivan – DESY FEA
Jülich, 04. 12. 2012

## Slide 2: Evolution of FPGA Technology (XILINX)
Spartan3
Virtex5
Kintex7/Zynq
I/O Transfer Rate up to 622Mb/s
Memory support up to 333Mb/s
GTX Transceiver Speed up to 6.5Gb/s
GTX Transceiver Speed up to 3.75Gb/s
PCI Express Gen 1
Transceiver Speed up to 12.5Gb/s
Memory Interface up to 1866Mb/s
AXI4 integration to many IP
PCI Express Gen 2
ZYNQ: Processing System and
Programmable logic in single chip
µTCA - HGF – AMC1
µTCA - DAMC2
PXI – Fast ADC Transient Recorder

## Slide 3: Starting efficiently with a Technology having limited resources ?
Concentrate on key challenges of new technology
  10G
  DDR3
  PCIe Gen2
  AMBA AXI4
Don’t make everything new
  Build up on existing in-house know-how and experiences
Have users and applications for the development
  One can learn much more if a development is really used
Share experience with other groups if possible
  Additional resources
Try to be cost effective
  Development of an improved version of the DAMC2 Board together with KIT –IPE (M. Balzer’s group)

## Slide 4: DAMC2 – Virtex-5
Versatile board
Modular structure
Compatible with DAMC2
For high performance applications
XC7K325T-2FFG900C
HGF-AMC1- Kintex - 7

## Slide 5: Preliminary HGF-AMC1 – Block Diagram

## Slide 6: HGF-AMC1 – Improvements and modifications
PCI Express, Gen 2,
DDR3 Memory, SODIMM
RTM Interface include 2 GTX channels
FMC Interface include 1 GTX channel
SFP+ Interface, 4 channels ( optionally direct 10G Ethernet )
GTX to backplane 4 channels
AMBA®AXI4 conforming interfaces
Power sequencing and monitoring of the Kintex 7
New BPI configuration interface

## Slide 7: Outlook: ZYNQ based developments
from Xilinx documentation

## Slide 8: Advantages of ZYNQ based Board
Commercial modules already on the market
  Simplification of hardware development
Algorithms can be programmed in C/C++ under OS
  Users can much easier maintain their DAQ Systems
Application Firmware and algorithms develop over time
  Today typically a VHDL developer has to update firmware

## Slide 9: ZYNQ based example – Application of commercial modules
Carrier board:
Signals drivers, receivers/transmitters, termination and interfaces connector
Connect signals from commercial module to correspondent interfaces connector
Commercial module:
Support most of the standard interfaces in processor system part
Support of the application design in programmable logic part
Simplification of HARDWARE development by splitting a design to 2 parts:
Combination of the different commercial modules and carrier boards can supply broad spectrum of the customers / applications

## Slide 10: ZYNQ based example – Application of commercial modules
Simplification of the SOFT/FIRMWARE development by splitting a design to 2 parts:
Processor system (PS) - software:
Powerful processing unit
OS integration
Programming in high level languages
Broad spectrum of standard interfaces
Programmable logic (PL) - firmware:
Based on Artix-7/Kintex-7
System monitoring
Written in VHDL Framework
Significant advantage can be relatively independent software development for PS part and firmware development for PL part, including possibility to combine them from different designs

## Slide 11
Thank You