## Slide 1
Development of a FPGA based DAQ for digital SiPM‘s using USB3.0
Holger Nöldgen
10. September 2012 | Holger Nöldgen

## Slide 2
PET-Detectors
A Positron Emission Tomograph (PET) uses the positron decay of radionuclide tracers.
During the annihilation process of a positron two gammas of 511 keV are produced in an angle of 180°.

## Slide 3
PET-Detectors
A PET detector consists of face-to-face placed scintillation detectors measuring coincident γ-particles.
The coincident signals give information about the line of response.
Three informations are required:
Timing information
Energy information
Position on detector (Pixelnumber)

## Slide 4
PET Detecor in Jülich (Plantis)
  Used as a high resolution detector for plant phenotyping, e.g
  for carbon transport within plants using 11CO2 as a radioactive marker
Solute transport in
plants (spica)
11C-distri-bution in a sugar beet

## Slide 5
Philips Digital Silicon Photomultiplier
An evaluation kit for dSiPM (TEK) arrays has been installed at the Central Institute for Electronics of the Forschungszentrum Jülich.
Digital Silicon Photomultiplier (dSiPM) are novel devices, allowing their users to implement them as a fully digital device for photon counting.
Pictures courtesy of Philips Digital Photon Counting

## Slide 6
How dSiPM work
Pictures courtesy of Philips Digital Photon Counting
Analog SiPM: Analog amplifiers are used before the output gets digitized
Digital SiPM: No analog electronics needed, since each photon is counted by the cell electronics

## Slide 7
dSiPM Read-Out Concept
A FPGA will play a central role within the readout chain
A seperate board will provide the proper voltages and logic levels for the tile
As a high speed data-link USB 3.0 will be implemented

## Slide 8
USB 2.0 Development @ ZEL in the past
Avnet Spartan6 LX16 Development Board connected to Cypress FX2 Development Board
cPCI CMC Carrier Board with Cypress USB 2.0 Link

## Slide 9
Differences between USB 2.0 and USB 3.0
Feature | USB 2.0 (Cypress FX2) | USB 3.0 (Cypress FX3)
Data rate | Max. 480 Mbits/s (High Speed) | Max 5.0 Gbits/s (Super Speed)
Data interface | Half-duplex Two-wire differential signaling | Dual-simplex Four-wire differential signaling
Bus transaction protocol | Host directed Polled traffic flow | Host directed Asynchronous notifications
Interface to FPGA | GPIF with 8-Bit @ 48 MHz Slave FIFO Interface | GPIF II with 32-Bit @ 100 MHz Slave FIFO Interface
Cypress FX2 USB Controller has been used in the past.
→ Existing USB 2.0 delevopments can be adapted to USB 3.0

## Slide 10
USB 3.0 Development @ ZEL now

## Slide 11
Cypress FX3 USB Controller [1]
USB 3.0 interface is backward
compatible to USB 2.0
FX3-Chip has internal USB phy
FPGA can be connected to a more simple parallel interface
[4]
[5]

## Slide 12
Cypress FX3 USB Controller [2]
FX3 has internal ARM926 CPU running at 200 MHz
Data transfer inbetween USB interface and GPIF II is set up by CPU code
After setup, data can be exchanged without CPU access (DMA channels)
[3]
[3]

## Slide 13
FX3 System Architecture
FX3 acts as a external coprocessor to provide a USB 3.0 to the FPGA
GPIF II is connected to FPGA I/Os
CPU code is stored on external I²C EEPROM
[2]

## Slide 14
GPIF II Interface
Signal | Usage
D[31:0] | Data bus
A[1:0] | USB endpoint adress
PCLK | GPIF clock (100 MHz)
SLCS | Chip select
SLRD | Read from bus
SLWR | Write to bus
SLOE | Bus output enable
FLAGA-FLAGD | FIFO signals (full, empty)
PKTEND | Write short package
44 FPGA I/O pins needed
[1]
[1]

## Slide 15
GPIF II Read Cycle
Data is clocked out from FIFO by PCLK
CS and ADDR adresses the endpoint buffer
RD is the FIFO read signal
OE enables the bus to be non tri-state and drive the output
FLAGs show status of FIFOs
Latencies !
[2]

## Slide 16
GPIF II Write Cycle
Data is clocked into FIFO by PCLK
CS and ADDR adresses the endpoint buffer
WR is the FIFO write signal
PKTEND indicates short pakate write (direct transfer to USB-Host)
OE disables the bus drive and forces bus to be an input
FLAGs show status of FIFOs
Latencies !
[2]

## Slide 17
GPIF II Software Implementation
GPIF II: A user state machine which can be created by GPIF-Designer tool and implemented into FX3 firmware
GPIF II internally consist of Triggers and Actions
[6]
[6]

## Slide 18
GPIF II Designer Interface Definition

## Slide 19
GPIF II Designer State Machine
After basic definition of user interface, each state can be examined and edited

## Slide 20
GPIF II Designer Timing
The timing tool helps to analyze the behaviour of the GPIF interface and can be used to adapt FPGA VHDL-Code

## Slide 21
FX3 Firmware Development [1]
Cypress provides an application framework to fasten design creation for the FX3 controller
On the host side API libs are provided to use the Cypress device driver
Firmware development is done by Eclipse using ARM-GCC on Windows and Linux
Many example applications are provided to get started
[3]
[3]

## Slide 22
FX3 Firmware Development [2]
A third party RTOS is running on the ARM-CPU and acesses the API libraries.
User code (if needed) can be implemented with the Eclipse IDE
[3]

## Slide 23
References
[1] „AN65974 - Designing with the EZ-USB FX3 Slave FIFO Interface“, Application Note, Cypress Semiconductor, www.cypress.com
[2] „CYUSB301X EZ-USB FX3 Super Speed USB Controller“, Datasheet, Cypress Semiconductor, www.cypress.com
[3] „Cypress FX3 Programmers Manual“
Documentation, Cypress Semiconductor, www.cypress.com
[4] „AN75705 - Getting started with FX3“
Application-Note, Cypress Semiconductor, www.cypress.com
[5] „AN75432 - USB 3.0 EZ-USB FX3 Orientation”, Application Note, Cypress Semiconductor, www.cypress.com
[6] „GPIF II Designer 1.0“
Documentation, Cypress Semiconductor, www.cypress.com

## Slide 24
Thank you!
Matthias Streun
Heinz Loevenich
Hubert Gorke
Günter Kemmerling