## Slide 1
Overview of the PANDA activities/topics at IPE
Michele Caselle and Andreas Kopmann
PANDA kick-off meeting ITIV-IPE Sept. 16th (2021)
Notes: Good afternoon everyone. My name is Andrea Santamaria Garcia, I’m a research associate here at KIT and I will be presenting our artificial intelligence activities for accelerators.

## Slide 2: Briefly overview from 2020 to now
KIT-Expression Of Interest (M. Caselle, A. Kopmann, M. Weber), March 2020
  Hardware development of a “common readout card” for PANDA –DAQ
  Fast track-reconstruction on FPGA based on Machine Learning
Technical Design Report – PANDA Data Acquisition and Event Filtering” (M. Caselle, A Kopmann and S. Chilingaryan), August 2020  Approved
   reference: tdr-daqt_v2.pdf (pag. 25-28 and 40 -41)
BMBF (Acronym: PANDA_MDC_KIT) title: Development of the “Module data concentrator” to establish a high-speed DAQ system for the Micro Vertex Detector of PANDA”
December 2020
Prof. Dr.-Ing. Dr. h. c. Jürgen Becker, Dr.-Ing. Michele Caselle (Coordinator), Dr.-Ing. Andreas Kopmann, Dr.-Ing. Bähr Steffen (KIT - ITIV and IPE)
Approved

## Slide 3: PANDA – Micro-Vertex Detector
The PANDA (antiProton ANnihilation at DArmstadt) experiment will study the strong interaction in annihilation reactions between an antiproton beam and a gas cluster jet target. The detector will comprise different sub-detectors for tracking, particle identification and calorimetry.
The Micro-Vertex Detector (MVD) as the innermost part of the tracking system will enable precise tracking and detection of primary and secondary vertices. It is equipped with both silicon pixel and strip sensors.

## Slide 4: PANDA – Micro-Vertex Detector
MVD – Microvertex Detector

## Slide 5: PANDA – Micro-Vertex Detector
MVD – Microvertex Detector
Microstrip detector
Barrel and Disk Strips

## Slide 6: On-line data path of MVD
Sensors
FEE- ASICs
Local controller ASICs
Electro/optical data links
Off-detector electronics
Slow-control
Compute node in the counting room (experimental area)
MVD detector modules

## Slide 7: On-line data path of MVD
Sensors
FEE- ASICs
Local controller ASICs
Electro/optical data links
Off-detector electronics
Slow-control
Compute node in the counting room (experimental area)
MVD detector modules
Pixel detector will be not integrated (phase 1)

## Slide 8: On-line data path of MVD
Sensors
FEE- ASICs
Local controller ASICs
Electro/optical data links
Off-detector electronics
Slow-control
Compute node in the counting room (experimental area)
MVD detector modules
Pixel detector will be not integrated (phase 1)
Strip detector is vital for (phase 1)

## Slide 9: On-line data path of MVD
FEE- ASICs
Local controller ASICs
Electro/optical data links
Compute node in the counting room (experimental area)
MDC and MMB devices are missing and not covered in PANDA

## Slide 10: On-line data path of MVD
FEE- ASICs
Local controller ASICs
Electro/optical data links
Slow-control
Compute node in the counting room (experimental area)
MVD detector modules
In the BMBF we are proposing the development of both MDC and MMB, which are necessary to complete the data acquisition of the MVD
Great opportunity for ITIV and IPE to work together in the commissioning of the DAQ of the MVD
International partners: Justus-Liebig-Universität Gießen, Forschungszentrum Jülich (FzJü), GSI, CERN and INFN - TO
INFN
Gießen
CERN
FzJü
GSI
MDC and MMB devices are missing and not covered in PANDA

## Slide 11: Module Data Concentrator (MDC) - ASICS
  Developed in UMC 110 nm with rad-hard layout
  Digital logic based on Triplicated Modular Redundancy (TRM) for Single Event Upset mitigation
  First implementation on FPGA to prove the digital behaviour
PASTA
front-end ASICs
Optical link
Hardening by layout:
Enclosed Layout Transistor (ELT)
P+ guarding
P+ Guardring
Rad-hard logic
Gotthard chip developed at KIT

## Slide 12: MVD Multiplexer Board (MMB) – DAQ card
  To be installed within a ATCA or µTCA creates in the counting room location: E20.201
  Must be employed during the test & characterization of the detector module during the detector production, therefore, designed to work as a “standalone” test system
  Possible form factor like AMC (Advanced Mezzanine Cards)
Many detector link
(i.e. 10 detector modules )
To compute node by optical link, i.e. firefly based on RoCE
SODANET implemented at SoC level (ETH)
  Many synergies are possible:
    Hardware development at IPE
    Firmware & SoC to be developed at ITIV

## Slide 13: Proposed DAQ of PANDA
  More complex DAQ scheme with many sub-detectors
  On-line data path covered by off-the-shelf devices  dramatic reduction of custom electronics
  Novel heterogeneous FPGA/GPU architecture based on emerging Ethernet protocols
  High-performance ML inference on modern programmable hardware platforms
Ethernet fabrics
(hundreds Gb/s)
Detectors
…
FPGA
AI
ETH
…
FPGA
AI
ETH
…
FPGA
AI
ETH
MVD Multiplexer Board (MMB)
Ethernet
…
Fast Feedback
HPC
GPUs
AI
Alveo
AI
HighFlex
AI
On-line data path (by commercial devices)
Notes: 1000 / 3  > 300 cards to be produced & tested (installed) + 300 optical fibers (complex optical patch-panel)
31 links -> in one single optical link at 100 Gb/s , we could potentially reduce 30 cards with drastic simplifications of production & test and installation at the exp. area .

## Slide 14: BMBF structure & Milestones
  WP 1 – Development of the MDC ASIC in sub-micrometer CMOS technology
  WP 2 – Development and production of an MVD Multiplexer Board and development of a test procedure and characterization of both pixel and microstrip detectors

## Slide 15: PANDA members & people
Member of PANDA (IPE):
  Staff: M. Caselle, A. Kopmann and S. Chilingaryan
PhDs (IPE):
  PhD student: T. Dritschler
  Olena Manzhura: Development of the DAQ for PANDA
  New PhD: ASIC development of the MDC for the µstrip detector
Student (IPE)
  Greta Heine (physics): fast-track reconstruction by AI (PANDA)
Olena
Manzhura
PhD ?
M. Caselle
A. Kopmann
S. Chilingaryan
T. Dritschler
Greta
Heine

## Slide 16: Fast tracking reconstruction
First implementation based on Unsupervised (K-means) and supervised (recurrent neural network) learning
FT1+FT2
FT3+FT4
FT5+FT6
Forward tracker detectors based on straw tube detectors
Courtesy: Waleed Esmail (Forschungszentrum Jülich) and Weijia Wang

## Slide 17: Fast tracking reconstruction
First implementation based on Unsupervised (K-means) and supervised (recurrent neural network) learning
FT1+FT2
FT3+FT4
FT5+FT6
Forward tracker detectors based on straw tube detectors
Courtesy: Waleed Esmail (Forschungszentrum Jülich) and Weijia Wang
FT1+FT2
FT3+FT4
FT5+FT6
  STEP 2: interpolate the track segments from the different parts of the FTS to form a full track candidate, it is based on a Recurrent Neural Network (RNN)
  STEP 1: Create Track Segments by using K-means clustering algorithm