## Slide 1: Blazar Monitoring with FACT Jens Björn Buß on behalf of the FACT collaboration

## Slide 2: Outline
Feasibility of FACT for monitoring
Maximized observation time with G-APDs
Maximized observation time with automation
Results from 5 years of TeV Blazar monitoring

## Slide 3: Earth-Bound VHE Gamma-Ray Astronomy
Gamma-Rays
Charged
Particles
Notes: Airshower  Cherenkov light
Telescope in the light cone
Image is projection into the Camera plain
Showers as video sequenzes
image parameters for origin and energy

## Slide 4: Monitoring in a Perfect World
Optimal case: 24/7 monitoring without any gaps
Best chance for coincidence with other experiments and messengers
sketch

## Slide 5: Monitoring in Reality
Optimal case: 24/7 Monitoring without any gaps
But in reality: Several limitations
Mrk 501

## Slide 6: Monitoring in Reality
Optimal case: 24/7 Monitoring without any gaps
But in reality: Several limitations  Observations do have gaps
Mrk 501
Notes: Add DWARF

## Slide 7: Monitoring in Reality
Optimal case: 24/7 Monitoring without any gaps
But in reality: Several limitations  Observations do have gaps
Mrk 501
.
FACT
Dedicated Worldwide Agn Research Facility (DWARF)
0
+2
+5,5
+8
-7
??
??
??
X
X
X
Notes: Add DWARF

## Slide 8: The FACT way to address these Limitations
Environment
Light conditions: sun, moon, twilight
Bad weather: clouds, rain, wind
Notes: Several Approaches to address this field of conflict
  Automatization -> Reduce Human interactions and robustness
  Reduce need for special calibration runs -> Self-calibrating system
  Maintainance -> Robust detectors
  Reduce light condition gaps -> Robust Sensors
  Money -> rather inexpensive devices

## Slide 9: The FACT way to address these Limitations
Environment
Light conditions: sun, moon, twilight
Bad weather: clouds, rain, wind
Telescope
Calibrations
Maintenance
Notes: Several Approaches to address this field of conflict
  Automatization -> Reduce Human interactions and robustness
  Reduce need for special calibration runs -> Self-calibrating system
  Maintainance -> Robust detectors
  Reduce light condition gaps -> Robust Sensors
  Money -> rather inexpensive devices

## Slide 10: The FACT way to address these Limitations
Resources
Human interaction
Observation priorities
Money
Environment
Light conditions: sun, moon, twilight
Bad weather: clouds, rain, wind
Telescope
Calibrations
Maintenance
Notes: Several Approaches to address this field of conflict
  Automatization -> Reduce Human interactions and robustness
  Reduce need for special calibration runs -> Self-calibrating system
  Maintainance -> Robust detectors
  Reduce light condition gaps -> Robust Sensors
  Money -> rather inexpensive devices

## Slide 11: The FACT way to address these Limitations
Resources
Human interaction
Observation priorities
Money
Environment
Light conditions: sun, moon, twilight
Bad weather: clouds, rain, wind
Telescope
Calibrations
Maintenance
Automation
Self-calibrating
System
Robust Detectors
Notes: Several Approaches to address this field of conflict
  Automatization -> Reduce Human interactions and robustness
  Reduce need for special calibration runs -> Self-calibrating system
  Maintainance -> Robust detectors
  Reduce light condition gaps -> Robust Sensors
  Money -> rather inexpensive devices

## Slide 12: The FACT way to address these Limitations
Resources
Human interaction
Observation priorities
Money
Environment
Light conditions: sun, moon, twilight
Bad weather: clouds, rain, wind
Telescope
Calibrations
Maintenance
Automation
Self-calibrating
System
Robust Detectors
Notes: Several Approaches to address this field of conflict
  Automatization -> Reduce Human interactions and robustness
  Reduce need for special calibration runs -> Self-calibrating system
  Maintainance -> Robust detectors
  Reduce light condition gaps -> Robust Sensors
  Money -> rather inexpensive devices

## Slide 13: From Tubes to Silicon Devices
Tubes

## Slide 14: From Tubes to Silicon Devices
Tubes
Silicon Devices

## Slide 15: From Tubes to Silicon Devices
Tubes

## Slide 16: From Tubes to Silicon Devices
?
Tubes
Silicon Devices

## Slide 17: G-APDs aka SiPMs
Semi-conductor based
Mechanically and electronically robust
No high voltage needed (U<100V)
Photo-detection efficiency (PDE) comparable to PMTs
Rather inexpensive with decreasing prizes
Extremely robust for bright light conditions

## Slide 18: From Tubes to Silicon Devices
?
Tubes
Silicon Devices

## Slide 19: From Tubes to Silicon Devices
Tubes
Are novel Geiger-mode Avalanche
Photo Diodes (G-APD aka SiPM)
a valid alternative for IACT cameras?
Silicon Devices
?

## Slide 20: From Tubes to Silicon Devices
Tubes
Build a camera and test it → FACT
(First G-APD Cherenkov Telescope)
Silicon Devices

## Slide 21: The FACT Collaboration
2 Countries
4 Institutes
about 25 active Members

## Slide 22: FACT
2200m a.s.l.
First Light: October 2011

## Slide 23: FACT - Goals
Proof of concept for SiPMs in IACTs
Long-term monitoring of TeV Blazars
    Maximize observation time
Notes: Aim is to monitor TeV to have a very dense sample.
Maximize observation time by robotic operation

## Slide 24: Points of Vantage
Automation
Self-calibrating
System
Robust Detectors
Could be done with G-APDs, but are they sufficient for FACT?

## Slide 25: Self-Calibrating System
G-APDs allow for a

## Slide 26: FACT – Uniformity & Stability of Camera
(our) G-APD gain has strong temperature dependency
 adjust voltage to temp. (and DC)  feedback system
check with single pe spectra:
 Dark noise + crosstalk allow calibration without any external device
Sum over
all pixels
and ΔT~25oC
excellent
uniformity
& stability
[JINST 9 P10012]
>1400 pixel
1 pixel
(5ms data)
gain
‘crosstalk’
1pe 2pe 3pe
gain = charge contribution of 1 photon

## Slide 27: Feedback System
No dedicated Light-Flasher runs needed!
FACT Light Flasher

## Slide 28: Robust Detectors
Reducing the Gap

## Slide 29: Ratescans– Stability with changing Light Conditions
+ calima
Trigger rate independent of moon, temperature and age of sensors
Due to this stability:
identify bad atmospheric conditions
from Ratescans
[33rd ICRC, 709]
For given sky position: Trigger should always see same rate of cosmic rays
FACT Preliminary

## Slide 30
M.L. Knoetig et al., FACT - Long-term stability and observations during strong Moon light
June 23rd 2013
brightest
full moon
of the year
[33rd ICRC, 695]
#No Filters
Notes: Gain independent from light conditions (feedback
system).
• Showers visible even while pointing to full
moon (no filters used).

## Slide 31: Reliability: Aging of Sensors?
FACT Preliminary

## Slide 32: Reliability: Aging of Sensors?
integrating over time, divide by dark-night DC (5μA) for each sensor:
 collected same charge as in >17’000 hours dark night observations
dark noise: ~0.5μA (laboratory)
 collected same charge as in ~20 years continuous op. in laboratory
No signs for aging
Despite huge amount of charge
FACT Preliminary
FACT Preliminary

## Slide 33: Automation
From on-site shifter to shifter-on-call

## Slide 34: Towards Robotic Operation
2011 – 2012
Local Operation

## Slide 35: Towards Robotic Operation
2011 – 2012
Local Operation
Since late 2012
Remote Operation

## Slide 36: Towards Robotic Operation
2011 – 2012
Local Operation
Since 2016
Automatic Operation & System Monitoring
Since late 2012
Remote Operation
http://www.fact-project.org/smartfact
Operation via smartphone

## Slide 37: Towards Robotic Operation
2011 – 2012
Local Operation
Since 2016
Automatic Operation & System Monitoring
Since late 2012
Remote Operation
http://www.fact-project.org/smartfact
Operation via smartphone
Currently Testing
Shifter-On-Call

## Slide 38: Data Taking Efficiency
95% Efficiency for good Weather
data-taking efficiency: 100% = time between astronomical twilights
When weather permits, we reach now a physics data-taking efficiency ~95%, rest mainly for telescope repositioning
Notes: Exceeding 95 % for good weather.
• Reduced dependency on light conditions.
• Maximized duty cycle
(robotic operation).
• Automized system monitoring
(Shifter Notifications).
Preliminary QLA results publicly available with short latency

## Slide 39: Crab Analysis
Are G-APDs sufficient for an IACT?
[NASA]

## Slide 40: Crab Energy Spectrum
SiPMs are well-suited for IACTs!
Energy range: 300 GeV – 10 TeV
Crab Spectrum in agreement with other IACTs
F. Temme et al., FACT - First Energy Spectrum from a SiPM Cherenkov Telescope, [34th ICRC, 707]
Note: 𝜽 used in
background suppression
Notes: Unfolded energy spectrum of the Crab Nebula

## Slide 41: SiPMs are Robust and Stable
Remote and automatic operation possible
High data taking efficiency
Stable telescope performance
Gamma sources detectable

## Slide 42: SiPMs are Robust and Stable
Remote and automatic operation possible
High data taking efficiency
Stable telescope performance
Gamma sources detectable
FACT is an ideal monitoring telescope

## Slide 43: Monitoring of Bright TeV Blazars

## Slide 44: Long-term Monitoring at VHE
FACT monitoring:
All data ~410h
FACT
Mrk 501 (2013) 1­hour­ binning

## Slide 45: Long-term Monitoring at VHE
FACT monitoring:
All data ~410h
Std. VHE monitoring:
Moon < 65%
Less than 1h every ~ 3rd night
  ~ 32h
FACT
standard VHE monitoring
Mrk 501 (2013) 1­hour­ binning

## Slide 46: Long-term Monitoring at VHE
FACT
standard VHE monitoring
Mrk 501 (2013) 1­hour­ binning
FACT monitoring:
All data ~410h
Std. VHE monitoring:
Moon < 65%
Less than 1h every ~ 3rd night
  ~ 32h

## Slide 47: Long-term Monitoring at VHE
Std. VHE monitoring:
Moon < 65%
Less than 1h every ~ 3rd night
  ~ 32h
FACT
standard VHE monitoring
Mrk 501 (2013) 1­hour­ binning
FACT monitoring:
All data ~410h
FACT monitoring strategy
unbiased data sample

## Slide 48: Observed Sources
Other sources
Crab Nebula (Calibration)
1H0323+342
Some spare observation time for:
Follow-up of alerts
  multi-wavelength, e.g. flare in optical
  multi-messenger, e.g. neutrino
Standard monitoring: Brightest TeV blazars
Mrk 421
Mrk 501
1ES 1959+650
1ES 2344+51.4

## Slide 49: Observed Sources
Status from December 2012 to December 2016:
Sources with > 100 h observation time
Source | # Runs | Time / h
Mrk 501 | 25367 | 1731.01
Crab | 18188 | 1481.71
Mrk 421 | 19187 | 1396.37
1ES 2344+51.4 | 15153 | 993.19
1ES 1959+650 | 15182 | 966.15
1H0323+342 | 6454 | 389.32
Notes: Redu the plots

## Slide 50: Low Latency Results – Quick Look Analysis
Low latency processing
excess rates within ~10min
Quick flare alerts
MWL observations
ToO observations
Results publicaly available
public access to QLA results: http://www.fact-project.org/monitoring

## Slide 51: More than 5 Years of Monitoring – The Markarians
Mrk 421
~1400h
Mrk 501
~1800h
Long-term monitoring of bright variable TeV sources
FACT Preliminary
FACT Preliminary
several short duration flares
even durations of one night
Mrk 421
2 flare alerts
1 Atel with HAWC and Swift-XRT
Mrk 501
6 flare alerts
Notes: Mrk421 Flare 2015 noch rein
We send a ToO

## Slide 52: More than 5 Years of Monitoring – The Markarians
Mrk 421
~1400h
Mrk 501
~1800h
Long-term monitoring of bright variable TeV sources
FACT Preliminary
FACT Preliminary
several short duration flares
even durations of one night
Mrk 421
2 flare alerts
1 Atel with HAWC and Swift-XRT
Mrk 501
6 flare alerts
Notes: Mrk421 Flare 2015 noch rein
We send a ToO

## Slide 53: More than 5 Years of Monitoring – The Markarians
Mrk 421
~1400h
Mrk 501
~1800h
Long-term monitoring of bright variable TeV sources
FACT Preliminary
FACT Preliminary
several short duration flares
even durations of one night
Mrk 421
2 flare alerts
1 Atel with HAWC and Swift-XRT
Mrk 501
6 flare alerts
Notes: Mrk421 Flare 2015 noch rein
We send a ToO

## Slide 54: More than 5 Years of Monitoring – 1ES 1959+650
Atel 9010
Atel 9139
Atel 9148
hardly visible low state
significant
brightening
bright flares
FACT Preliminary
Atel 9239
Atel 9203
Long-term behavior
Flaring activity
2016
April 2016 – now

## Slide 55: More than 5 Years of Monitoring – 1ES 1959+650
Atel 9010
Atel 9139
Atel 9148
hardly visible low state
significant
brightening
bright flares
FACT Preliminary
Atel 9239
Atel 9203
Long-term behavior
Flaring activity
2016
April 2016 – now
30 flare alerts
5 Atels

## Slide 56: Atel – 1ES 1959+650 Flare
FACT detected and reported brightest TeV flare of 1ES 1959
Wednesday 12:35 - 12:55
Amit SHUKLA
Multi-waveband study of TeV blazar 1ES1959+650 during a high state in 2016

## Slide 57: Atels & Flare Alerts
#9239: FACT: FACT measures new maximum flux from the HBL 1ES 1959+650 at TeV energies
#9203: FACT, MAGIC: FACT and MAGIC measure an increased gamma-ray flux from the HBL 1ES 1959+650
#9148: FACT, MAGIC, VERITAS, Fermi-LAT, Swift-XRT: Further increase of gamma-ray emission from the HBL 1ES 1959+650
#9139: FACT: FACT measures increased gamma-ray flux from the high-energy peaked BL Lac object 1ES 1959+650 since five nights
#9137: FACT, HAWC, Swift-XRT: Enhanced and increasing activity in gamma rays and X-rays from the HBL Mrk421
#9010: Fermi-LAT, FACT, MAGIC, VERITAS: Fermi-LAT, FACT, MAGIC and VERITAS detection of increasing gamma-ray activity from the high-energy peaked BL Lac object 1ES 1959+650
Source | Alerts | Atels
Mrk 501 | 6 | -
Mrk 421 | 2 | 1
1ES 1959+650 | 30 | 5
1ES 2344+51.4 | 2 | -
Sum | 40 | 6
Source | Alerts | Atels
Mrk 501 | 6 | -
Mrk 421 | 2 | 1
1ES 1959+650 | 30 | 5
1ES 2344+51.4 | 2 | -
Sum | 40 | 6
+ 2 gcn-circulars
Notes: Timeline of ATELs
GCN wieder rein +

## Slide 58: Conclusion
G-APDs are excellent sensors for IACTs
  Excellent single Pe resolution
  Calibration without dedicated flasher
  Robust at bright light conditions e.g. Moon
  No indication for aging effects
  Crab analysis agrees with other IACTs
Automation: 95% data taking efficiency possible
Provide low-latency results (QLA)
Several notifications: flare alerts and ATELs sent
Dense light curves for Mrk 421, Mrk 501 and 1ES 1959+650

## Slide 59: Conclusion
G-APDs are excellent sensors for IACTs
  Excellent single Pe resolution
  Calibration without dedicated flasher
  Robust at bright light conditions e.g. Moon
  No indication for aging effects
  Crab analysis agrees with other IACTs
Automation: 95% data taking efficiency possible
Provide low-latency results (QLA)
Several notifications: flare alerts and ATELs sent
Dense light curves for Mrk 421, Mrk 501 and 1ES 1959+650
FACT is ideal for long-term monitoring

## Slide 60: Conclusion
G-APDs are excellent sensors for IACTs
  Excellent single Pe resolution
  Calibration without dedicated flasher
  Robust at bright light conditions e.g. Moon
  No indication for aging effects
  Crab analysis agrees with other IACTs
Automation: 95% data taking efficiency possible
Provide low-latency results (QLA)
Several notifications: flare alerts and ATELs sent
Dense light curves for Mrk 421, Mrk 501 and 1ES 1959+650
FACT is ideal for long-term monitoring
.
FACT
Dedicated Worldwide Agn Research Facility (DWARF)
0
+2
+5,5
+8
-7
??
??
??
X
X
X
Next?

## Slide 61: Send Notifications
Source | # Alerts | # atels
Mrk 501 | 6 | -
Mrk 421 | 2 | 1
1ES 1959+650 | 30 | 5
1ES 2344+51.4 | 2 | -
Sum | 40 | 6

## Slide 62: Mrk 421 from Radio to TeV Energies
FACT
800 days
2-20 keV
2-10 keV
15 GHz
GeV
15-50 keV

## Slide 63: Pulseshape

## Slide 64
.
FACT
Dedicated Worldwide Agn Research Facility (DWARF)
0
+2
+5,5
+8
-7
??
??
??
X
X
X

## Slide 65: Feedback System
Voltage Supply
Temperature
Sensor
Control Circuit
Iout → USiPM
Nomial Voltage Calculation
PC
USiPM
Iout
Uset
TSiPM
USiPM
Uout
SiPM

## Slide 66: Data Rate
Chart: 
| 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0
Volume [TB] | 4.3 | 37 | 74 | 64 | 89 | 80
Num Files [k Files] | 3.615 | 29.203 | 52.676 | 50.271 | 53.615 | 47.644
Ratio [GB/File] | 1.1895 | 1.267 | 1.4048 | 1.2731 | 1.66 | 1.6791

## Slide 67: Spannungsabhängigkeit des Gain
Temperaturabhängigkeit
über Spannung korrigieren
Preliminary

## Slide 68: Different Temperature Conditions
Stable Signal Amplitude (Feedback System)
Notes: Gain independent from temperature variations
(feedback system)

## Slide 69: MWL and ToO Activities
Target-of Opportunity Campaigns
  2013: XMM-Newton / Swift
  2015: INTEGRAL / Swift
  Ongoing in 2016: INTEGRAL, Swift and XMM-Newton
  Granted for 2017:
    INTEGRAL, Swift
    AstroSAT
Multi-Wavelength Observations
  Multi-Messenger: AMON Network
  MWL campaigns
  Observations triggered by FACT alerts
38 alerts since March 2014
Successful ToO Dec 2015
6 Atels in 2016
HAP Workshop Non-thermal Universe, Erlangen, 2016 Daniela Dorner
@ 17:30h
Notes: 12/9/16
69
69

## Slide 70: Multivariate Energy Reconstruction
Bias:
Mean
Resolution:
Standard deviation
Notes: Random Forest Regression used for energy estimation
Magic Resolution 15 to 20%
Bias comparable

## Slide 71: FACT – G-APD Camera
1440 pixels
6 weeks, 3 FTE
1: glue G-APD to cone
2: glue cones to front window
3: solder connector cables to G-APDs
4: install baffle plate
completed sensor plane

## Slide 72
1440
pixels
\

## Slide 73: FACT – First Light
FACT

## Slide 74: Comparison MAGIC & FACT
Mrk 501 – Flares May/June 2012
Magic light curve and FACT excess rate curve in good agreement

## Slide 75: FACT – Night Sky Background
Today’s G-APD are much better
adapted to the needs of IACTs
Cherenkov sun ~ moon NSB(dark)
integrated spectra
solid: G-APD
dotted: PMT
G-APD: Hamam.
S10362-33-50C
PMT: Hamamatsu
R10408
G-APD: SensL
TSV

## Slide 76: Outlook…
p
plus projects for future
MST and LST cameras
post-FACT: many
SiPM-based
CTA projects.
& CTs
outside
CTA
SST-1M
ASTRI
GCT
SCT
Actual SiPM much better than those used in FACT
 expect significantly better performances
FACT
FAMOUS