## Slide 1
MMB

## Slide 3: Component Side 1
Keepout area
Recommended area for hot-swap switch
MMC
SODIMM
ZYNQ
US+
PLL
LTM46
44
LTM4620
FireFly
FireFly
FireFly
FireFly
FireFly
LTM4620
LTM4620
LTM4620

## Slide 4: Component Side 2
MMC
ZYNQ
US+
PLL
LTM46
44
LTM4620
FireFly
FireFly
FireFly
FireFly
FireFly
SODIMM
LTM4620
LTM4620
LTM4620
Keepout area

## Slide 6: ZYNQ UltraScale+ XCZU11EG-1FFVC1760
1760
C
11

## Slide 7: Recommended Operating Conditions (PS)
Symbol | Description | Min (V) | Typ (V) | Max (V)
VCC_PSINTFP | PS full-power domain supply voltage | 0.808 | 0.850 | 0.892
VCC_PSINTLP | PS low-power domain supply voltage | 0.808 | 0.850 | 0.892
VCC_PSAUX | PS auxiliary supply voltage | 1.710 | 1.800 | 1.890
VCC_PSINTFP_DDR | PS DDR controller and PHY supply voltage | 0.808 | 0.850 | 0.892
VCC_PSADC | PS SYSMON ADC supply voltage relative to GND_PSADC | 1.710 | 1.800 | 1.890
VCC_PSPLL | PS PLL supply voltage | 1.164 | 1.200 | 1.236
VPS_MGTRAVCC | PS-GTR supply voltage | 0.825 | 0.850 | 0.875
VPS_MGTRAVTT | PS-GTR termination voltage | 1.746 | 1.800 | 1.854
VCCO_PSDDR | PS DDR I/O supply voltage | 1.06 | - | 1.575
VCC_PSDDR_PLL | PS DDR PLL supply voltage | 1.710 | 1.800 | 1.890
VCCO_PSIO | PS I/O supply | 1.710 | - | 3.465
VPSIN | PS I/O input voltage | –0.200 | - | VCCO_PSIO + 0.200
 | PS DDR I/O input voltage | –0.200 | - | VCCO_PSDDR + 0.200
VCC_PSBATT | PS battery-backed RAM and battery-backed real-time clock (RTC) supply voltage | 1.200 | - | 1.500
(DS925, p. 4)

## Slide 8: Recommended Operating Conditions (PL)
Symbol | Description | Min (V) | Typ (V) | Max (V)
VCCINT | PL internal supply voltage | 0.825 | 0.850 | 0.876
VCCINT_IO | PL internal supply voltage for the I/O banks | 0.825 | 0.850 | 0.876
VCCBRAM | Block RAM supply voltage | 0.825 | 0.850 | 0.876
VCCAUX | Auxiliary supply voltage | 1.746 | 1.800 | 1.854
VCCO | Supply voltage for HD I/O banks | 1.140 | - | 3.400
 | Supply voltage for HP I/O banks | 0.950 | - | 1.900
VCCAUX_IO | Auxiliary I/O supply voltage | 1.746 | 1.800 | 1.854
VIN | I/O input voltage | –0.200 | - | VCCO + 0.200
VMGTAVCC | Analog supply voltage for the GTH or GTY transceiver | 0.873 | 0.900 | 0.927
VMGTAVTT | Analog supply voltage for the GTH or GTY transmitter and receiver termination circuits | 1.06 | - | 1.575
VMGTVCCAUX | Auxiliary analog QPLL voltage supply for the transceivers | 1.746 | 1.800 | 1.854
VMGTAVTTRCAL | Analog supply voltage for the resistor calibration circuit of the GTH or GTY transceiver column | 1.164 | 1.200 | 1.236
VCCADC | PS DDR I/O input voltage | 1.746 | 1.800 | 1.854
VREFP | PL System Monitor externally supplied reference voltage relative to GNDADC | 1.200 | 1.250 | 1.300
(DS925)

## Slide 9: Quiescent Supply Current (VCCINT = 0.85V)
VCCINT rail would typically require most amount of current
Maximum current draw for VCCINT for XCZU11EG-1FFVC1760: 70 A
Symbol | Description | I (mA)
ICCINTQ | Quiescent VCCINT supply current | 1699
ICCINT_IOQ | Quiescent VCCINT_IO supply current | 115
ICCOQ | Quiescent VCCO supply current | 1
ICCAUXQ | Quiescent VCCAUX supply current | 255
ICCAUX_IOQ | Quiescent VCCAUX_IO supply current | 56
ICCBRAMQ | Quiescent VCCBRAM supply current | 22
 |  | 2.148
(DS925, p. 11 - 15)
(UG583, p. 33)

## Slide 10: Power Supply Consolidation

## Slide 11
(UG583, p. 29)

## Slide 12: FireFly Power (1)

## Slide 13: FireFly Power (2)

## Slide 14: PLL Power (1)

## Slide 15: PLL Power (2)

## Slide 16: Power Supplies (1)
LTM4620 (two outputs):
  Input: 4.5 .. 16 V
  Output: 0.6 .. 2.5 V
  Current: 13 A/Output; 26 A when combined outputs
LTM4644 (four outputs):
  Input: 4 .. 14 V; with external bias: 2.375 .. 14 V
  Output: 0.6 .. 5.5 V
  Current: 4 A/Output; up to 16 A when combined outputs

## Slide 17: Power Supplies (2)
LTM4650 (two outputs, used in HighFlex2):
  Input: 4.5 .. 15 V
  Output: 0.6 .. 1.8 V
  Current: 25 A/Output; 50 A when combined outputs
MAX8686:
  Input: 4.5 .. 20 V
  Output: 0.7 .. 5.5 V
  Current: 25 A per phase

## Slide 18
(UG583, p. 20)