## Slide 1: Micro Channel Cooling for ultra light silicon detectors.
M. Deveaux

## Slide 2
Purpose of the concept
Our project: The CBM experiment
A heavy ion fixed target experiment
Location: GSI/FAIR – Darmstadt
8 subdetector systems (2x silicon)
>400 scientists, 57 institutes
CBM is designed to become the fastest
heavy ion experiment buildt so far:
10 MHz Au+Au collisions.

## Slide 3
Weak point: MVD
CBM is designed to become the fastest
heavy ion experiment buildt so far:
10 MHz Au+Au collisions.
The MVD is at present limited to 100 kHz.
On the long run: Room for improvement
The CBM-MVD
Sensors have to be operated in vacuum.
Accelerating them needs adding power.
Adding power adds material for cooling.
=> Optimizing requires

## Slide 4
MIMOSIS-1, 60µm thick
MIMOSIS-1
In synergy with:
CMOS Monolithic Active Pixel Sensors
Use CMOS Monolithic Active Pixel Sensors (MIMOSIS-1):
5µm/5µs resolution
27x30 µm² pixel pitch
50µm thick
20 MHz/cm² (80 MHz/cm² peak).
Power dissipation:
50 – 100 mW/cm²
Sensors have dead area.
Needs two layers of silicon
Team:
PICSEL Group IPHC Strasbourg
AG Stroth, Goethe University
Detektorlabor, GSI

## Slide 5
Integration concept of the MVD
M. Deveaux
17
Discri
Sensor
Discri
Sensor
GBTx data
concentrator
LV-re-
gulator
MVD Prototype (mock up)

## Slide 6
Cooling options so far
Sensors on CVD-Diamond:
+ Highly heat conductive
+ Very stiff
+ “Easy” to handle
- High price
Sensors on TPG-graphite:
+ Highly heat conductive
+ Cheap
o Needs wrapping
- Difficult to handle
- Mechanically fragile

## Slide 7: Detector integration: state of the art
PRESTO:
Prototype of a quarter station incl. sensors (MIMOSA-26),
cables, support etc.
Material budget is dominated by:
Cables
Cooling
=> Need to increase efficiency of both
Discri
Sensor (3x)
Discri
Sensor
Discri
Sensor
Cable (2x)
Cable (2x)
Cable (2x)
In synergy with:

## Slide 8
What is the challenge?
Video (DVD)
MIMOSA-5
MIMOSTAR-3
MIMOSA-26
FSBB
MIMOSIS-1
ALPIDE
Gen. 1
Gen. 2
Gen. 3
Year
Data stream: >20 Gbps internal, 2.4 Gbps external
A further acceleration of sensors would require higher data streams:
~ 2 Tbps internal, 240 Gbps external (already compressed, corresponds to computer RAM).
Needs cables and cooling in vacuum.

## Slide 9
What could be done?
CO2 Channel
Metal 1
Metal 2
Bonding pad
Sensor
Sensor
SiO2
Si
~ 0.2 X0
0.05X0
0.05X0
Use highly
doped Si as additional ground plate
Hold sensors with cooling support
Evacuate heat with micro-channels (e.g. liquid CO2)
Integrate cables
into support
Bond sensors to
support

## Slide 10
Open scientific questions
CO2 Channel
Metal 1
Metal 2
Bonding pad
Sensor
Sensor
SiO2
Si
~ 0.2 X0
0.05X0
0.05X0
Design of micro channels Handling of (liquid CO2)
Design rules,
thickness of metall layers (thicker=better)
thickness of isolators (5V, 100V?)
HF-properties of traces
Feasibility of Bonding
Design of the
inlet
Operation and test

## Slide 11
Anodic wafer bonding
Creation of micro – channels (simple example):
Put lithography mask.
Edge e.g. (111) wafers with KOH (Potassiom Hydroxide)
Result: Open channels
Rather triangular if KOH is used.
Well structured if plasma etching is used.

## Slide 12
Anodic wafer bonding
Connect to wafers (e.g. Si + Glass).
Needs high voltage: ~ 1 kV
Needs high temperature: >400°C
Needs pressure
Structured objects should be bonded in vacuum
=> Wafers bond by electro-chemical reaction.
Outcome:
Double wafer with buried channels.
Possibly still too thick for the application
No inlets yet.
Important note:
Conditions not compatible with the use of structured wafers => Can't use sensor wafers.

## Slide 13
Thinning and opening of inlets
Channels still closed, need inlets/outlets.
Inlets added by etching.
Reduce thickness by etching.

## Slide 14
Connect tube adapters
Tube adapter
Placing the tube adapter in a reliable way is an art of its own.
So far: State of the art. Processes were validated at CERN.

## Slide 15
Add traces and sensors
Cu-traces
Add and bond sensors
Add traces with lithographic methods.
Challenge: Need relatively thick Cu-layers to reach reasonably low R
Add sensors by glueing and wire bonding.
Challenge:
Need to place sensors at both sides
=> Complicated holding structures needed.

## Slide 16
What was learned from a first attempt
Starting from 2013 – Attempt do to something together with CiS.
Idea: Build device based on lithography for silicon strip detectors.
Discontinued do to missing funding and insufficient human ressources.
Lessons learned:
Wafer size is limited (4", 6"?) => Difficult to build sizeable devices.
Transporting power though lithographic traces is difficult (ohmic losses)
  Restrict to data (?).
This is complex, need experience in
  Sensor operation.
  Sensor integration (bonding etc.).
  CO2 – cooling systems.
  Fluid dynamics (design of cooling channels).
  Connecting micro channels to macroscopic channels.

## Slide 17
Summary and conclusion
High performance pixel sensor systems need highest data transport capability.
Sizeable power for data transport.
Highly efficient and ultra-light cooling systems.
Ultra light cabling.
Idea:
Integrate cooling micro channels and micro cables into one silicon device.
Status:
First attempt done together with CiS failed due to missing ressources.