## Slide 1
Life Cycle Assessment of Geothermal Heating & Cooling Systems
European Geothermal Workshop 2019
Astu Sam Pratiwi
Prof. Evelina Trutnevyte
UNIGE Renewable Energy Systems
10 October 2019
Notes: Life cycle asse

## Slide 2: Life Cycle Analysis for Environment Sustainability
Wells
Opera-tion
End of Life
Cons-truction

## Slide 3: Life Cycle Analysis for Environment Sustainability
Wells
Opera-tion
End of Life
Fuel
Transport
Electricity
Steel
Cement
Cons-truction

## Slide 4: Heating Demand in Geneva
Fossil fuel dominates the demand
Geneva 2030 targets:
  40% greenhouse gas reduction (from 1990)
  10% of fossil fuel substitution by renewable energy
Adapted from Narula et al., 2019 and Quiquerez et al., 2020

## Slide 5: Geothermal Potential in Geneva
Geothermal energy as renewable source potential
Potentially supplies 75% of Geneva heat demand by 2030 (Groupe de travail PGG, 2011)
Switzerland has the highest density of ground source heat pumps
But less knowledge for deeper systems
Adapted from https://geothermie-schweiz.ch
< 100 °C
shallow
deep
medium depth

## Slide 6: GEothermie 2020
Subsurface characterization for shallow and medium depth
Support the district heating expansion in Geneva
Adapted from https://geothermie-schweiz.ch
< 100 °C
shallow
deep
medium depth

## Slide 7: Scenarios of GEothermie 2020
Pilot wells for medium depth
744 m
30°C
1100 m
-
1500 m
-
?
-
Several scenarios for surface applications
Multifamily /
tertiary building
District heating with heat pump
District heating without heat pump

## Slide 8: Scenarios of GEothermie 2020

## Slide 9: Scenarios of GEothermie 2020
Environmental performance

## Slide 10: Literature study

## Slide 11: Literature study – LCA for geothermal heating systems
Peer-reviewed environmental studies on geothermal heating applications worldwide
Chart: Number of Literature Studies
| Ground-source Heat Pump | Groundwater Heat Pump + Medium Enthalpy | High Enthalpy Heating | High Enthalpy Power + Cogeneration
LCA Studies | 0 | 4 | 1 | 41
Non-LCA Studies | 0 | 7 | 1
LCA Studies | 14
Non-LCA Studies | 6
Number of Plants | 178 | 281 | 1 | 113

## Slide 12: Literature study – LCA for geothermal heating systems
29 studies
  quantified environmental performance
22 studies
used LCA methodologies
Chart: Number of Literature Studies
| Ground-source Heat Pump | Groundwater Heat Pump + Medium Enthalpy | High Enthalpy Heating | High Enthalpy Power + Cogeneration
LCA Studies | 0 | 4 | 1 | 41
Non-LCA Studies | 0 | 7 | 1
LCA Studies | 14
Non-LCA Studies | 6
Number of Plants | 178 | 281 | 1 | 113

## Slide 13: Literature study – LCA for geothermal heating systems
Chart: Number of Literature Studies
| Ground-source Heat Pump | Groundwater Heat Pump + Medium Enthalpy | High Enthalpy Heating | High Enthalpy Power + Cogeneration
LCA Studies | 0 | 4 | 1 | 41
Non-LCA Studies | 0 | 7 | 1
LCA Studies | 14
Non-LCA Studies | 6
Number of Plants | 178 | 281 | 1 | 113
gap
Source for the status of geothermal plants: EGEC, 2018
29 studies
  quantified environmental performance
22 studies
used LCA methodologies

## Slide 14: Literature study – LCA for geothermal heating systems
Chart: Number of Literature Studies
| Ground-source Heat Pump | Groundwater Heat Pump + Medium Enthalpy | High Enthalpy Heating | High Enthalpy Power + Cogeneration
LCA Studies | 0 | 4 | 1 | 41
Non-LCA Studies | 0 | 7 | 1
LCA Studies | 14
Non-LCA Studies | 6
Number of Plants | 178 | 281 | 1 | 113
gap
GEothermie 2020
29 studies
  quantified environmental performance
22 studies
used LCA methodologies

## Slide 15: Literature study – reported impacts
3 most reported impact categories
Ground-source Heat Pumps:
Less homogeneous results
Sensitive to COP and electricity mix
Groundwater Systems:
More homogenous result
More studies are needed

## Slide 16: Literature study – reported impacts
3 most reported impact categories
Ground-source Heat Pumps:
Less homogeneous results
Sensitive to COP and electricity mix
Groundwater Systems:
More homogenous result
More studies are needed

## Slide 17: Literature study – reported impacts
3 most reported impact categories
Ground-source Heat Pumps:
Less homogeneous results
Sensitive to COP and electricity mix
Groundwater Systems:
More homogenous result
More studies are needed

## Slide 18: Preliminary case studies

## Slide 19: Preliminary case studies

## Slide 20: Preliminary case studies
 |  | Scenario IA-1 |  | Scenario IA-2 |  | Scenario I B
Diameter |  | 0.18 m |  | 1 m |  | 1 m
Depth |  | 10 m |  | 30 m |  | 60 m
N. Well |  | 2 |  | 2 |  | 3
Flowrate |  | 5.5 l/s |  | 30 l/s |  | 16 l/s
Cooling |  | Yes |  | Yes |  | No

## Slide 21: Preliminary Results
Global Warming:
8.9 – 14.3 kgCO2/MWh
Fossil Fuel:
62 – 92 MJ/ MWh
Acidification:
0.02 – 0.22 kgSO2/ MWh
Case studies

## Slide 22: Preliminary Results – Global warming potential
Chart: 
| Scenario IB | Scenario IA-2 | Scenario IA-1
Drilling | 245608.3459 | 51642.7723 | 11584.6919
Construction | 281298.1546 | 81823.2794 | 51573.1773
Operation | 414885.7382 | 805919.7786 | 187065.1084
End of Life | 3146.3578 | 40413.2791 | 6976.5829
Note:
  Hydro electricity
  30 years of lifetime

## Slide 23: Preliminary Results
Depletion of abiotic resources
Water depletion
Air Pollution
Climate Change
Fossil Fuel Depletion
lower impacts
higher impacts

## Slide 24: Preliminary Results
Depletion of abiotic resources
Water depletion
Air Pollution
Climate Change
Fossil Fuel Depletion
Use of metallic material
Hydro electricity

## Slide 25: Conclusion
More LCAs are needed for geothermal heating and cooling involving groundwater extraction
Existing literature shows that impacts of ground source heat pump are less homogenous than groundwater systems, and not always lower than individual oil boilers.
Preliminary finding shows
  the difference in impact contribution between individual and district heating.
  lower impacts on global warming from geothermal and higher impacts on metal and water depletion.

## Slide 26: Thank You !
Astu Sam Pratiwi
UNIGE Renewable Energy Systems
astu.pratiwi@unige.ch