## Slide 1
Michele Caselle, Timo Dritschler, Kai Lukas Unger, Vladimir Sidorenko, Lars Eisenblätter, Olena Manzhura, Suren Chilingaryan, Andreas Kopmann
PANDA DAQ for beam test
Beam test Meeting
23 –February 2023
KIT

## Slide 2
Introduction
Beam test setup “Hardware side” (Michele)
Beam test setup “low-level Driver – Software” (Timo)
Round table discussion
Conclusion & Next steps
AOB
Lunch
Visit the KIT clean room (detector technologies)
Feedback final remarks from Giessen (if present)
PANDA beam test – Meeting (Giessen-KIT)
Agenda

## Slide 3
PANDA DAQ for beam test
First version of FPGA firmware that integrated the control/readout of ToASt(s) by the MDC architecture
The first architecture is based on HighFlex v.1 with MDC architecture on FPGA
Readout based on PCIe Gen 3, compatible to any PCs
Data throughput up to 120 Gb/s suitable to readout multiple ToASt(s) simultaneously as a detector module scenario
ToASt
ToASt
ToASt
…
Strip Detector
Detector card
FPGA (HighFlex v1) card
DDR3
PC DAQ/control
User register
GPU-Direct KIT-DMA
Data
PCIe Programmed IO (PIO)
Cmd/Cnfg
MDC
(Module data Concentrator)

## Slide 4
PANDA DAQ for beam test (HW components)
First version of HW setup, development platform
TOASt ASIC on detector card
HighFlex readout card with MDC proto

## Slide 5
Status of the Module Data Concentrator ASIC
Radiation-tolerant ASIC local controller of the microstrip detector modules
First version of MDC (FPGA) developed, all necessary logic blocks “ready” to be tested with ToASt
MDC architecture implemented
Designed to readout up to 12 ToASt
Dynamic configuration of the number of ToASt and high-speed links
No-active links are kept in low-power mode
Intelligent multiplexing logic to balance the data occupancy between the serial links
Milestone: designing the first prototype of “baby-MDC in UMC 110nm, within 2022

## Slide 6
Module Data Concentrator (Data Format)
MDC data format and real-time data consistency check
Header
SYNC
SYNC
Data
SYNC
Data
…
Trailer
32 bits
ToASt frame (25.6 µs)
CRC
ToASt
(data format)
MDC
(channel)
Header
Data
Data
…
Trailer
CRC
SYNC packets  to check the communication between TX_ch channel (ToASt) and MDC
Only HEADER, DATA and TRAILER transmitted
MDC
(Data format)
Header
Data
Data
…
Trailer
Header
Data
Data
…
Trailer
Header MDC
…
Trailer MDC
ToASt 0
ToASt N
CRC
CRC
128 packets
Frame number alignment  performed on MDC and packed in the MDC Header
CRC data check and correction  performed on the FPGA/ZYNQ (off-detector electronics)
MDC Header and Trailer (32 bits) free to any further metadata to be sent to off-detector acquisition
To DAQ

## Slide 7
Additional requirements for beam test
Signal requirements for beam test and platform development
External clock at 80 MHz
External reset epoch counter for off-line data analysis
External data acquisition (frame acquisition)  to be defined both the single-shot and continuous acquisition modes
MDC
(Data format)
Header
Data
Data
…
Trailer
Header
Data
Data
…
Trailer
Header MDC
…
Trailer MDC
ToASt 0
ToASt N
CRC
CRC
HEADER MDC = {8'hAA, Epoch_counter, FRAME_NUM}
TRAILER MDC = {32'h5_BEEF_BEEF}
MDC header (opcode)
Epoch counter
Available for additional off-line meta-data
Event number generated from the ToASt

## Slide 8: Epoch counter and reset
Counter @ 160 MHz
When an external or internal acquisition command is asserted, the epoch counter is copied in the MDC HEADER field
Ext Reset
@ 160 MHz
Epoch counter
External/internal acq. cmd
Epoch counter
(timestamp)

## Slide 9
HW-SW interface
ToASt driver installed as PCIe interface
A set of shell scripts prepared to control the system
The script are example to learn how to develop more sophisticated GUI/ routines
To check the dma status
Reload the driver
Reset and config the ToASt
Test pulse command and readout procedure
Readout data (streaming)

## Slide 10
Reset and configuration (ToASt)
PW-On-reset  global-Reset  configuration (Global and channel regs)
16 Global registers
8 regions divided in 8 channels each

## Slide 11
Status registers and errors (DAQ + ToASt)
Status / Errors are ready only registers
Control_register
 cmds
Status DAQ and FPGA infras.
Status of ToASt & MDC
Status link TX_0 (ToASt)
Status link TX_1 (ToASt)
Number of test pulses

## Slide 12
Control register (DAQ + ToASt)
Command register for (reset, configuration, acquisition modes)
Data from DDR3  to DMA  to PC<
Enable test pulse procedure (FPGA)
Enable readout (streaming)
Internal data check (infrastructure-only)
Intern./extern. clock source
FPGA, MDC and ToASt resets

## Slide 14
Global and channel configurations
Global and channel configuration are the same of the ToASt (defined by Ganni)
seq | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  |  | 
 |  |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  | 
chip sel B | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0xD600 |  | 
GCR0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x4100 |  | 
WR | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0x5030 |  | 
GCR0 (0x0) | 0 | 1 | 0 | 1 |  | detector pol. | leading edge only | single THR mode |  | frame couter reset | TX_1 EN | TX_0 EN |  |  | timestamp_Gray mode | timestamp EN |  |  | 
default |  |  |  |  |  | 1 | 0 | 0 |  | 0 | 1 | 1 |  |  | 1 | 1 | 0x5433 |  | 
GCR1 (0x1) | 0 | 1 | 0 | 1 |  | CfgTX inversion | TX_1_inversion | TX_0_inversion | CfgTx output current ctrl |  |  |  | TX_1 and TX_0 output current ctrl |  |  |  |  |  | 
default |  |  |  |  |  | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0x5088 |  | 
GCR2 (0x2) | 0 | 1 | 0 | 1 |  |  | CSA load I bias |  |  |  |  | CSA gain boost Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0x5125 |  | 
GCR3 (0x3) | 0 | 1 | 0 | 1 |  |  | CSA gain boost Vbias |  |  |  |  | CSA source follwer Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0x51F0 |  | 
GCR4 (0x4) | 0 | 1 | 0 | 1 |  |  | Preamp feedback pMOS Ibias |  |  |  |  | Preamp feedback nMOS Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0x529F |  | 
GCR5 (0x5) | 0 | 1 | 0 | 1 |  |  | Preamp Ishift |  |  |  |  | PTA Ibuf |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0x53FF |  | 
GCR6 (0x6) | 0 | 1 | 0 | 1 | PTA control |  | PTA pMOS Ibias |  |  |  |  | PTA nMOS Ibias |  |  |  |  |  |  | 
default |  |  |  |  | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0x51DF |  | 
GCR7 (0x7) | 0 | 1 | 0 | 1 |  |  | CB Ibias 1 |  |  |  |  | CB Ibias 2 |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0x530D |  | 
GCR8 (0x8) | 0 | 1 | 0 | 1 |  |  | CB Vbias |  |  |  |  | ToT Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0x52D4 |  | 
GCR9 (0x9) | 0 | 1 | 0 | 1 |  |  | BLR Ibias |  |  |  |  | BLR Vcas |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0x5246 |  | 
GCR10 (0xA) | 0 | 1 | 0 | 1 |  |  | HC Ibias 1 |  |  |  |  | HC Ibias 2 |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0x5318 |  | 
GCR11 (0xB) | 0 | 1 | 0 | 1 |  | HC Ibias 3 |  |  |  |  | Baseline Vbias |  |  |  |  |  |  |  | 
default |  |  |  |  |  | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0x56A8 |  | 
GCR12 (0xC) | 0 | 1 | 0 | 1 |  |  | TThr bias |  |  |  |  | EThr bias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0x5129 |  | 
GCR13 (0xD) | 0 | 1 | 0 | 1 |  |  | ToT Ifb DAC Ilsb |  |  |  |  | ToT Ifb DAC Imin |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0x51B5 |  | 
GCR14 (0xE) | 0 | 1 | 0 | 1 |  |  |  |  | calibration EN | Ib calibration |  |  |  |  |  |  |  |  | 
default |  |  |  |  |  |  |  |  | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0x5071 | here CAL EN | 0x50F1
GCR15 (0xF) | 0 | 1 | 0 | 1 |  |  |  |  | Reg Dis 7 | Reg Dis 6 | Reg Dis 5 | Reg Dis 4 | Reg Dis 3 | Reg Dis 2 | Reg Dis 1 | Reg Dis 0 |  |  | 
default |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x5000 |  | 
Channel configuration register |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Select channel | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Region (R2, R1, R0) |  |  | 0 | Channel (C2,C1,C0) |  |  | A0 |  |  | 
 |  |  |  |  | 0 | 0 | 0 | 0 |  |  |  | 0 |  |  |  |  | ch --> 7:0 | reg --> 7:0 | 
Reg A0 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  |  | 
0 | 0 | 1 | 0 | 1 |  |  |  |  | Channel mask | Delay enable | CAL ENABLE | ToT discharge current calibration DAC |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0x38 | cal_en | 0x5018
1 | 0 | 1 | 0 | 1 | Energy threshold DAC range | Energy threshold DAC |  |  |  |  | Time threshold DAC range | Time threshold DAC |  |  |  |  |  |  | 
 |  |  |  |  | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0xD36 |  | 

## Slide 15
ToASt
ToASt
ToASt
…
MDC ToASt configuration module
ToAst configuration and “error protection” architecture
MDC
Downlink from LpGBT (output elinks)
Uplink transmit data from the lpGBT to the counting room
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
-----
Register read (conf data)
No operation (idle)
Implemented on ToASt (Gianni)
MDC conf FIFO
LpGBT interface
FSM_CFG_check
FSM_TX_CFG
FSM_RX_CFG

## Slide 16
ToASt
ToASt
ToASt
…
MDC ToASt configuration module
ToAst configuration and “error protection” architecture
MDC
Downlink from LpGBT (output elinks)
Uplink transmit data from the lpGBT to the counting room
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
-----
Register read (conf data)
No operation (idle)
Implemented on ToASt (Gianni)
MDC conf FIFO
LpGBT interface
FSM_CFG_check
FSM_TX_CFG
FSM_RX_CFG
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect

## Slide 17
ToASt
ToASt
ToASt
…
MDC ToASt configuration module
ToAst configuration and “error protection” architecture
MDC
Downlink from LpGBT (output elinks)
Uplink transmit data from the lpGBT to the counting room
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
-----
Register read (conf data)
No operation (idle)
Implemented on ToASt (Gianni)
MDC conf FIFO
LpGBT interface
FSM_CFG_check
FSM_TX_CFG
FSM_RX_CFG
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect

## Slide 18
ToASt
ToASt
ToASt
…
MDC ToASt configuration module
ToAst configuration and “error protection” architecture
MDC
Downlink from LpGBT (output elinks)
Uplink transmit data from the lpGBT to the counting room
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
-----
Register read (conf data)
No operation (idle)
Implemented on ToASt (Gianni)
MDC conf FIFO
LpGBT interface
FSM_CFG_check
FSM_TX_CFG
FSM_RX_CFG
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
Sequence VALID
Sequence NOT VALID

## Slide 19
ToASt
ToASt
ToASt
…
MDC ToASt configuration module
ToAst configuration and “error protection” architecture
MDC
Downlink from LpGBT (output elinks)
Uplink transmit data from the lpGBT to the counting room
Implemented on ToASt (Gianni)
MDC conf FIFO
LpGBT interface
FSM_CFG_check
FSM_TX_CFG
FSM_RX_CFG
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
Sequence VALID
CfgTx
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
-----
Register read (conf data)
No operation (idle)

## Slide 20
ToASt
ToASt
ToASt
…
MDC ToASt configuration module
ToAst configuration and “error protection” architecture
MDC
Downlink from LpGBT (output elinks)
Uplink transmit data from the lpGBT to the counting room
Implemented on ToASt (Gianni)
MDC conf FIFO
LpGBT interface
FSM_CFG_check
FSM_TX_CFG
FSM_RX_CFG
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
….
Chip Deselect
CfgRx
Every write operation is completed by a readback
COMPARE
Chip Select
Register select (ch/glob)
Register write (conf data)
….
Register select (ch/glob)
Register write (conf data)
Register read (conf data)
COMPARE
….
Chip Deselect

## Slide 21
ToASt
SERDES
FSM align
bitslip
FSM
Control
Async.
FIFO
FSM
Readout
lock
ToASt
SERDES
FSM align
bitslip
FSM
Control
Async.
FIFO
32 x 64
FSM
Readout
lock
ToASt
SERDES
FSM align
bitslip
FSM
Control
Async.
FIFO
FSM
Readout
lock
… x 12 ToASt
MUX
intelligent Round-Robin controller
Main FSM
Frame alignment check
Trailer check
5 MHz
80 MHz
@ 80 MHz
Async.
FIFO
32 x 1024
To external DDR3 device
40 MHz
320 MHz
Test Pulse
ToASt Configuration & Control FSM

## Slide 22
User Bank Register on FPGA infrastructure
Serial_CFG_interface_V2
User registers
add: 9064
add: from 6000
Direct ToASt configuration
By Sequencer generator
CFG_SequenceGen
MUX
Sequencer will automatically generates the configuration sequence
Downlink_GBT_Data_seq
Downlink_GBT_Data_reg
Downlink_GBT_Data
Sync_FIFO
FSM_SHIFT
TX
SERIAL_OUT
FSM_RX_CFG
Cfg_TX
Cfg_RX
CfgRx_int_reg
DATA_RX_CFG
ToASt
MDC
ReadBack to User

## Slide 23
Address by PCIe | Global Register | Defaults value | Description
6000 | GCR_0 | 0x433 | Tx_0 and TX_1 enable for each ToASt, Detector polarity =1 (electrons)
6004 | GCR_1 | 0x088 | 
6008 | GCR_2 | 0x125 | 
600C | GCR_3 | 0x1f0 | 
6010 | GCR_4 | 0x29f | 
6014 | GCR_5 | 0x3ff | 
6018 | GCR_6 | 0x1df | 
601C | GCR_7 | 0x30d | 
6020 | GCR_8 | 0x2d4 | 
6024 | GCR_9 | 0x246 | 
6028 | GCR_10 | 0x318 | 
602C | GCR_11 | 0x6a8 | 
6030 | GCR_12 | 0x129 | 
6034 | GCR_13 | 0x1b5 | 
6038 | GCR_14 | 0x071 | Calibration enable = 0 (please set 0xF1 to enable the test pulse)
603C | GCR_15 | 0x000 | No region disabled

## Slide 24
Address by PCIe | Channel register | Defaults value | Description
6040 | Region 0 - Channel 0 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6044 | Region 0 - Channel 0 Reg 1 | 0xd36 | 
6048 | Region 0 - Channel 1 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
604C | Region 0 - Channel 1 Reg 1 | 0xd36 | 
6050 | Region 0 - Channel 2 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6054 | Region 0 - Channel 2 Reg 1 | 0xd36 | 
6058 | Region 0 - Channel 3 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
605C | Region 0 - Channel 3 Reg 1 | 0xd36 | 
6060 | Region 0 - Channel 4 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6064 | Region 0 - Channel 4 Reg 1 | 0xd36 | 
6068 | Region 0 - Channel 5 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
606C | Region 0 - Channel 5 Reg 1 | 0xd36 | 
6070 | Region 0 - Channel 6 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6074 | Region 0 - Channel 6 Reg 1 | 0xd36 | 
6078 | Region 0 - Channel 7 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
607C | Region 0 - Channel 7 Reg 1 | 0xd36 | 

## Slide 25
Address by PCIe | Region
6040 | Region 0
6080 | Region 1
60C0 | Region 2
6100 | Region 3
6140 | Region 4
6180 | Region 5
61C0 | Region 6
6200 | Region 7