## Slide 1
Michele Caselle, Timo Dritschler, Kai Lukas Unger, Vladimir Sidorenko, Lars Eisenblätter, Olena Manzhura, Suren Chilingaryan, Andreas Kopmann
Status of the DAQ system
periodical meeting
29 –March 2023

## Slide 2
PANDA DAQ for beam test
First version of FPGA firmware that integrated the control/readout of ToASt(s) by the MDC architecture
The first architecture is based on HighFlex v.1 with MDC architecture on FPGA
Readout based on PCIe Gen 3, compatible to any PCs
Data throughput up to 120 Gb/s suitable to readout multiple ToASt(s) simultaneously as a detector module scenario
ToASt
ToASt
ToASt
…
Strip Detector
Detector card
FPGA (HighFlex v1) card
DDR3
PC DAQ/control
User register
GPU-Direct KIT-DMA
Data
PCIe Programmed IO (PIO)
Cmd/Cnfg
MDC
(Module data Concentrator)

## Slide 5
PANDA DAQ for beam test (HW components)
First version of HW setup, development platform

## Slide 6
Global and channel configurations
Global and channel configuration are the same of the ToASt (defined by Ganni)
seq | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  |  | 
 |  |  |  |  |  | B |  |  |  |  |  |  |  |  |  |  |  |  | 
chip sel B | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0xD600 |  | 
GCR0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x4100 |  | 
WR | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0x5030 |  | 
GCR0 (0x0) | 0 | 1 | 0 | 1 |  | detector pol. | leading edge only | single THR mode |  | frame couter reset | TX_1 EN | TX_0 EN |  |  | timestamp_Gray mode | timestamp EN |  |  | 
default |  |  |  |  |  | 1 | 0 | 0 |  | 0 | 1 | 1 |  |  | 1 | 1 | 0x5433 |  | 
GCR1 (0x1) | 0 | 1 | 0 | 1 |  | CfgTX inversion | TX_1_inversion | TX_0_inversion | CfgTx output current ctrl |  |  |  | TX_1 and TX_0 output current ctrl |  |  |  |  |  | 
default |  |  |  |  |  | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0x5088 |  | 
GCR2 (0x2) | 0 | 1 | 0 | 1 |  |  | CSA load I bias |  |  |  |  | CSA gain boost Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0x5125 |  | 
GCR3 (0x3) | 0 | 1 | 0 | 1 |  |  | CSA gain boost Vbias |  |  |  |  | CSA source follwer Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0x51F0 |  | 
GCR4 (0x4) | 0 | 1 | 0 | 1 |  |  | Preamp feedback pMOS Ibias |  |  |  |  | Preamp feedback nMOS Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0x529F |  | 
GCR5 (0x5) | 0 | 1 | 0 | 1 |  |  | Preamp Ishift |  |  |  |  | PTA Ibuf |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0x53FF |  | 
GCR6 (0x6) | 0 | 1 | 0 | 1 | PTA control |  | PTA pMOS Ibias |  |  |  |  | PTA nMOS Ibias |  |  |  |  |  |  | 
default |  |  |  |  | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0x51DF |  | 
GCR7 (0x7) | 0 | 1 | 0 | 1 |  |  | CB Ibias 1 |  |  |  |  | CB Ibias 2 |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0x530D |  | 
GCR8 (0x8) | 0 | 1 | 0 | 1 |  |  | CB Vbias |  |  |  |  | ToT Ibias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0x52D4 |  | 
GCR9 (0x9) | 0 | 1 | 0 | 1 |  |  | BLR Ibias |  |  |  |  | BLR Vcas |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0x5246 |  | 
GCR10 (0xA) | 0 | 1 | 0 | 1 |  |  | HC Ibias 1 |  |  |  |  | HC Ibias 2 |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0x5318 |  | 
GCR11 (0xB) | 0 | 1 | 0 | 1 |  | HC Ibias 3 |  |  |  |  | Baseline Vbias |  |  |  |  |  |  |  | 
default |  |  |  |  |  | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0x56A8 |  | 
GCR12 (0xC) | 0 | 1 | 0 | 1 |  |  | TThr bias |  |  |  |  | EThr bias |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0x5129 |  | 
GCR13 (0xD) | 0 | 1 | 0 | 1 |  |  | ToT Ifb DAC Ilsb |  |  |  |  | ToT Ifb DAC Imin |  |  |  |  |  |  | 
default |  |  |  |  |  |  | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0x51B5 |  | 
GCR14 (0xE) | 0 | 1 | 0 | 1 |  |  |  |  | calibration EN | Ib calibration |  |  |  |  |  |  |  |  | 
default |  |  |  |  |  |  |  |  | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0x5071 | here CAL EN | 0x50F1
GCR15 (0xF) | 0 | 1 | 0 | 1 |  |  |  |  | Reg Dis 7 | Reg Dis 6 | Reg Dis 5 | Reg Dis 4 | Reg Dis 3 | Reg Dis 2 | Reg Dis 1 | Reg Dis 0 |  |  | 
default |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x5000 |  | 
Channel configuration register |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Select channel | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Region (R2, R1, R0) |  |  | 0 | Channel (C2,C1,C0) |  |  | A0 |  |  | 
 |  |  |  |  | 0 | 0 | 0 | 0 |  |  |  | 0 |  |  |  |  | ch --> 7:0 | reg --> 7:0 | 
Reg A0 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  |  | 
0 | 0 | 1 | 0 | 1 |  |  |  |  | Channel mask | Delay enable | CAL ENABLE | ToT discharge current calibration DAC |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0x38 | cal_en | 0x5018
1 | 0 | 1 | 0 | 1 | Energy threshold DAC range | Energy threshold DAC |  |  |  |  | Time threshold DAC range | Time threshold DAC |  |  |  |  |  |  | 
 |  |  |  |  | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0xD36 |  | 

## Slide 7
User Bank Register on FPGA infrastructure
Serial_CFG_interface_V2
User registers
add: 9064
add: from 6000
Direct ToASt configuration
By Sequencer generator
CFG_SequenceGen
MUX
Sequencer will automatically generates the configuration sequence
Downlink_GBT_Data_seq
Downlink_GBT_Data_reg
Downlink_GBT_Data
Sync_FIFO
FSM_SHIFT
TX
SERIAL_OUT
FSM_RX_CFG
Cfg_TX
Cfg_RX
CfgRx_int_reg
DATA_RX_CFG
ToASt
MDC
ReadBack to User

## Slide 8
Address by PCIe | Global Register | Defaults value | Description
6000 | GCR_0 | 0x433 | Tx_0 and TX_1 enable for each ToASt, Detector polarity =1 (electrons)
6004 | GCR_1 | 0x088 | 
6008 | GCR_2 | 0x125 | 
600C | GCR_3 | 0x1f0 | 
6010 | GCR_4 | 0x29f | 
6014 | GCR_5 | 0x3ff | 
6018 | GCR_6 | 0x1df | 
601C | GCR_7 | 0x30d | 
6020 | GCR_8 | 0x2d4 | 
6024 | GCR_9 | 0x246 | 
6028 | GCR_10 | 0x318 | 
602C | GCR_11 | 0x6a8 | 
6030 | GCR_12 | 0x129 | 
6034 | GCR_13 | 0x1b5 | 
6038 | GCR_14 | 0x071 | Calibration enable = 0 (please set 0xF1 to enable the test pulse)
603C | GCR_15 | 0x000 | No region disabled

## Slide 9
Address by PCIe | Channel register | Defaults value | Description
6040 | Region 0 - Channel 0 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6044 | Region 0 - Channel 0 Reg 1 | 0xd36 | 
6048 | Region 0 - Channel 1 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
604C | Region 0 - Channel 1 Reg 1 | 0xd36 | 
6050 | Region 0 - Channel 2 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6054 | Region 0 - Channel 2 Reg 1 | 0xd36 | 
6058 | Region 0 - Channel 3 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
605C | Region 0 - Channel 3 Reg 1 | 0xd36 | 
6060 | Region 0 - Channel 4 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6064 | Region 0 - Channel 4 Reg 1 | 0xd36 | 
6068 | Region 0 - Channel 5 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
606C | Region 0 - Channel 5 Reg 1 | 0xd36 | 
6070 | Region 0 - Channel 6 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
6074 | Region 0 - Channel 6 Reg 1 | 0xd36 | 
6078 | Region 0 - Channel 7 Reg 0 | 0x038 | Set 0x18 to enable the test pulse on this channel
607C | Region 0 - Channel 7 Reg 1 | 0xd36 | 

## Slide 10
Address by PCIe | Region
6040 | Region 0
6080 | Region 1
60C0 | Region 2
6100 | Region 3
6140 | Region 4
6180 | Region 5
61C0 | Region 6
6200 | Region 7

## Slide 11
ToASt
SERDES
FSM
CH
Channel
FIFO
FSM
Readout
FSM align
bitslip
lock
Reset 0
Idle
1
HEAD_DATA 2
ERROR 3
ERROR FIFO FULL 4
FIFO_FULL
start_Readout_ToASt & (DataOut_32[31:28] == 4'b1010)
(!start_Readout_ToASt)
If the sequence HEADERSYNCDATA_TRAILER are wrong
Reset 0
Idle 1
READY 2
ERROR 5
Trailer_found_sync_5
Start Readout 3
Stop Readout 4
start_read_fifo (from Main_FSM_Readout)
Fifo_ready = 1
Rd_data_en = 1
Move to fsm_data_read_start
DATA_COUNT_tmp counts the number of data received between HEADER and TRAILER
When all data have been readout and sent to MAIN_FSM
Clock = DATA_CLOCK = 80 MHz
Reset = IORESET
Clock = CLK_DIV = 5 MHz
Reset = IORESET
WR_FIFO <= #dly 1'b1;
Write_Data_FIFO <= #dly DataOut_32;

## Slide 12
FSM
Readout
FSM
Readout
FSM
Readout
MUX
Main FSM
Async.
FIFO
32 x 1024
Reset 0
Idle 1
Header_MDC 2
ERROR F
FIFO_READY_OR
Channel Select link 0 4
Readout link 0 5
start_read_fifo = 1
Clock = DATA_CLOCK = 80 MHz
Reset = MDC_RESET
Channel Select link 1 5
Readout link 1 6
Trailer_MDC 7
FIFO_FULL
Link not locked
Readout till ToASt_Trailer

## Slide 13
LpGBT_pll
Clock_LpGBT (320 MHz)
Clock_PCie (80 MHz)
Clock_EXT (80 MHz)
MDC
Clock_buffer_logic (pll)
clk_elink (320 MHz)
clock_ToASt (160 Mhz)
clock_cfg (80 MHz)
clock_readout (80 MHz)
clk_div_elink (10 MHz)
CLK_DIV (5 MHz)
Serial_CFG_interface_V2
BUFR (/2)

## Slide 14
PLLs architecture
Clock_from_PCIe_to_80MHz
User_clk (250 MHz)
clk_LpGBT
internal_clock_80MHz
Ext_clock_buf (80 MHz)
ClockIn_GBT_p (320 MHz)
clock_dist_MDC (PLL)
clock_ToASt
To ToASt (160 MHz)
BUFR
BUFG

## Slide 15
External pins on FPGA
Ext_clk
Slow trigger
Fast trigger
BB31  GPIO_DIP_SW7
AY30  GPIO_DIP_SW5
BA32  GPIO_DIP_SW3
AY33  GPIO_DIP_SW1
spare