## Slide 1: The journey to multi bunch emittance control
More than just feedback
Alun Morgan, Dmitrii Rabusov

## Slide 2: What do we do now
Feedback loop using pinhole cameras as detector and skew quadrupole magnets as actuators
Beam
Pinhole camera
Emittance calculation
Feedback calculation
Desired emittance
Pinhole camera
Feedback actuator (skew quadrupole magnets)
Beam
1 of 15

## Slide 3: Why not just keep doing that?
We will not have the flexibility to use the skew quadrupole magnets due to the impact on off axis injection
Operating modes in Diamond-II may require per bunch size manipulation. (e.g. hybrid bunch)
Additional Diamond-II
considerations
It cannot stabilise horizontal and vertical emittance simultaneously as it is coupling control based.
Small reduction in dynamic aperture​
Suffers from hysteresis
  performance degrades over time
Feedback loop limited to a few Hz due to pinhole camera update rate.
Limitations of existing system
2 of 15

## Slide 4: Why use side band excitation with the MBF?
There are some differences in behaviour which need to be accounted for before it can be used in operation.
No new hardware required in the storage ring.
This allows the emittance control to be applied to all or a subset of bunches as operations require.
It has less impact on lifetime and injection efficiency compared to the existing skew quadrupole approach
Sideband excitation
Additional MBF bonuses
Emittance Control for Diamond-II​
Ian Martin, Alun Morgan, Shaun Preston
9th Low Emittance Rings Workshop​
CERN, 13th-16th February 2024​
3 of 15

## Slide 5: What is the new approach?
Keep the existing emittance monitoring but replace the actuator of the feedback.
Beam
Pinhole camera
Emittance calculation
Feedback calculation
Desired emittance
Pinhole camera
Feedback actuator
Beam
Part of the control loop replaced an oscillator controlled by and part of the multi bunch feedback system.
A new feedback controller algorithm is required
4 of 15

## Slide 6: Tune tracking
  In Diamond we need to use tune tracking to make sideband excitation practical
Excitation at fixed frequency and amplitude
Tune and sidebands jitter in frequency
Frequency jitter is converted into a variation in effectiveness and so beam size variation
5 of 15
We may not need this in Diamond-II due to the 3rd harmonic cavity.

## Slide 7: Tune tracking limitations
6 of 15
Machine change has broken the tune tracking twice since 2020
Unable to identify the causes
2023 unexpected phase shift
2020 multivalued solutions
The past
Developed improved locking scheme
Retuned the entire system

## Slide 8: MBF emittance feedback development
Initial proof of concept done in 2020 by Guenther
Largely manual but looked promising.
Various issues identified in operating alongside standard operation,
for example:
Making sure the target bunch is filled
The need to turn off the feedback on the few bunches either side of the tracking bunch
Basically, it allowed us to define the problem much more clearly.
Emittance
MBF actuator
ID gap
MBF feedback
No feedback
Magnet feedback
7 of 15

## Slide 9: Development of a new MBF vertical emittance feedback algorithm
Scalar controller
Dynamic controller
Emittance measurement
r
ε
εF
Existing skew quadrupole base algorithm
MBF based algorithm (tested September 2022)
εerror
Emittance measurement
εTarget
ε
Scalar controller
εerror
Operational proof of concept
No dynamic adjustment of parameters so currently it takes too long to stabilise after ID changes.
Much of the controller is related to the magnet dynamics and so needs to be redeveloped to use the MBF system instead
8 of 15

## Slide 10: Testing the simple emittance control
Response rate when changes occur:
Next step is to use proper systems analysis to develop a full feedback model
No feedback | 0.030pm rad
Magnet based system | 0.037pm rad
MBF system | 0.060pm rad
Standard deviation over a few mins in the stable state:
Magnet based system | 8 s / pm rad
MBF system | 29 s / pm rad
9 of 15

## Slide 11
Broader considerations
The MBF system will become machine critical in more ways.
MBF focussed
Assessing and developing new operational uses of the MBF system.​
  PPRE​
  Bunch cleaning​
  Emittance feedback​
Integrating all the different operating modes to work together in various combinations.​
Accelerator focussed
Improving our assessment of the working point stability.
Identifying the impact of various machine settings.
Improving our understanding of the impact of MBF setting changes.
10 of 15
Notes: I will touch on the broader studies which impact the sideband excitation scheme only.

## Slide 12: Broader studies – Pulse Picking by Resonant Excitation for use with 'timing users'
An alternative to hybrid fill.
  Feasibility study in collaboration with one of our beam lines
Investigations into operating Pulse Picking by Resonant Excitation (PPRE) in the vertical plane
doi: 10.18429/JACoW-IPAC2023-MOPM037
S. Wilkes, A. Morgan, G. Karras, I. Martin, M. Warren
Lifetime without Compromise
doi: 10.18429/JACoW-IPAC2023-MOPM036
S. Wilkes
Machine measurement
Beamline measurement
11 of 15

## Slide 13
Emittance feedback for the Diamond-II storage ring using resonant excitation
doi:10.18429/JACoW- IPAC2022 - TUPOMS035
S. T. Preston∗ , T. Olsson, B. Singh
Including the impedance causes a broadening and shifting of the sidebands as well as showing the asymmetry similar to the measured data.
Broader studies – settings optimisation
12 of 15
Measured impact of chromaticity and bunch charge
The Asymmetry of the peaks and the sensitivity with excitation harmonic
indicates that long-range wakefields have a significant impact. ​
Measurements for emittance feedback based on resonant excitation at Daimond light source
doi:10.18429/JACoW-IBIC2022-WEP37
S. T. Preston∗ , T. Olsson, A. Morgan† , L. Bobb
Simulation
Measurement

## Slide 14: Broader studies – further investigation of excitation harmonic modes
Full fill
Single bunch
Tune excitation with equivalent charge per bunch.
Dependencies investigated so far
Fill pattern
Excitation amplitude
Beam current
Signal integrated over the beam depends on excitation mode
13 of 15

## Slide 15: Broader studies – Measuring the effects of MBF bandwidth on feedback robustness
tune scans at I = 150 mA around the current working point
Shorter filter
Wider bandwidth
Longer filter
Narrower bandwidth
14 of 15

## Slide 16: Future work and questions
Develop an improved feedback algorithm
Simulation
  Understand the effects of a 3rd harmonic cavity
  Include both short and long range wakefields
Measurement studies
  Single bunch operation - To better separate the effect of long and short range wakefields.
  Find a more optimal accelerator setup with minimal sideband driven centroid motion
  Can this residual centroid motion be mitigated by the multi-bunch feedback ?
Questions
Experience with 3rd harmonic cavity
Experience with ramped / booster operation
Experience with Amplifiers
Where does the noise floor variation with excitation mode come from?
15 of 15
Noise measurements