## Slide 1
Precision measurement of vibrational transition in HT
Valentin Hermann

## Slide 2: How well do we understand molecules?
O
H
H
H
H

## Slide 3: What is „understanding a molecule“?
„Good understanding“ = accurate model of the energy levels in molecule

## Slide 4: What is „understanding a molecule“?
„Good understanding“ = accurate model of the energy levels in molecule
E = EBO + Ead + Enad + Erel + EQED + ?*
Includes:
Molecular QED theory
Fundamental constants
Potentially new physics

## Slide 5: What is „understanding a molecule“?
Simplest molecule to test depth of „understanding“?:
Molecular hydrogen!
H
H

## Slide 6: Energy levels in the hydrogen molecule
Calculated and measured with high precision
Competition: theory vs. experiment
Species: H2, HD and D2
mass: nuclear spin:
Limited advancements in theory![1,2]
[1] J. Komasa, M. Puchalski, and K. Pachucki, Phys. Rev. A 102 (2020)
[2] C. Delaunay, J.-P. Karr, T. Kitahara, J.C.J. Koelemeij, Y. Soreq, and J. Zupan
Phys. Rev. Lett. 130, 121801 (2023)

## Slide 7: The solution: Tritium!
3 additional molecules to test! (HT, DT, T2)
Mass of 3u and fermionic
Best spectroscopy data ~15 MHz accuracy[1,2] (vs. HD: ~60 kHz[3])
Test object for New Physics[4]
! Radioactive
! Radiochemical active
[1] M Schlösser et al., J. Phys. B: At. Mol. Opt. Phys. 50 214004 (2017)
[2] K.-F. Lai, VH, et al., PCCP, 22, 8973-8987 (2020)
[3] F.M.J. Cozijn, VH, et al., Phys. Rev. A 105, 062823 (2022)
[4] W.G. Hollik, M. Linster, M. Tabet, Eur. Phys. J. C 80, 661 (2020)
H
T
D
T
T
T
Combined expertise of high-res. spectroscopy and tritium technology needed!

## Slide 8
Precision measurement of vibrational transition in HT
Valentin Hermann , Benedict Rothmund, Magnus Schlösser
Frank M.J Cozijn, Meissa L. Diouf, Wim Ubachs
“Precision Measurement of Vibrational Quanta in Tritium Hydride (HT)”,
F.M.J. Cozijn, M.L. Diouf, W. Ubachs, V. Hermann, M. Schlösser, accepted by PRL (2024)

## Slide 9: The Technique: Noise-Immune Cavity-Enhanced Optical-Heterodyne Molecular Spectroscopy (NICE-OHMS)

## Slide 10: Cavity enhanced spectroscopy
FWHM≈1.5 GHz
High-reflective mirrors R=99.996%
Finesse of 80000
26 mW Input 400W Peff
! Wavelength needs to fit free spectral range (FSR)
! Extremely stable conditions required
Enhancement by optical resonator

## Slide 11: Saturation spectroscopy
Lamb-dip in Doppler broadened profile:
Saturation of molecules with v=0
1/1000 linewidth

## Slide 12: Saturation spectroscopy
Lamb-dip in Doppler broadened profile:
Saturation of molecules with v=0
1/1000 linewidth
Only ~10 ppm absorption!

## Slide 13: How to extract NICE-OHMS signal?
Light matter interaction
Dispersion
Absorption

## Slide 14: How to extract NICE-OHMS signal?
Light matter interaction
Dispersion
Dispersion measurement?

## Slide 15: Frequency modulation spectroscopy (FM) in the cavity
+
=
Electro-optical modulator (EOM) produces sidebands with ν0±νm
νm fits FSR of cavity
Sidebands are 180° phase-shifted
Dispersion changes cause imbalance in sidebands
Phase sensitive detection

## Slide 16: Wavelenght modulation in NICE-OHMS
Additional low-frequency dither (modulation)
  Derivative detection symmetric line shape
  Further noise suppression
  Eliminates background drifts
  Any order possible(1f, 2f, 3f)
1f:
2f:

## Slide 17: Typical Result: 1f signal in H2O
Single scan of residual water
1f of dispersive signal symmetric line shape
High SNR

## Slide 18: The Experimental Setup:

## Slide 19: The optical setup @Amsterdam

## Slide 20: The Tritium setup @Amsterdam
1 GBq activity of H:T mixture (~20 mbar*cm³)
Fully tritium compatible, enclosed setup
Non-evaporable Getter (NEG) as vacuum pump
Tritium storage and pressure regulation from 0.005 Pa - 5 Pa using special NEG
Cavity and tritium infrastructure in second evacuated containment for noise reduction

## Slide 21: The Tritium setup
1 GBq activity of H:T mixture (~20 mbar*cm³)
Fully tritium compatible, enclosed setup
Non-evaporable Getter (NEG) as vacuum pump
Tritium storage and pressure regulation from 0.005 Pa - 5 Pa using special NEG
Cavity and tritium infrastructure in second evacuated containment for noise reduction

## Slide 22: The Tritium setup
1 GBq activity of H:T mixture (~20 mbar*cm³)
Fully tritium compatible, enclosed setup
Non-evaporable Getter (NEG) as vacuum pump
Tritium storage and pressure regulation from 0.005 Pa - 5 Pa using special NEG
Cavity and tritium infrastructure in second evacuated containment for noise reduction
Tritium storage and pressure regulation?

## Slide 23: Tritium storage & pressure regulation using NEGs
Zirconium-based non-evaporable getters (NEGs) from SAES (type St171)
Irreversible binding of (non-noble) gases when heated
Reversible binding of hydrogen when cold
Desorption of hydrogen following Sievert‘s law
log(peq) = 3.6 + 2log(Cgetter) – 5200/T [1]
Temperature of getter  Hydrogen pressure
[1] www.saesgetters.com/sites/default/files/St 171 - 172_Sintered Porous Getters_1.pdf

## Slide 24: Tritium storage & pressure regulation using NEGs
Zirconium-based non-evaporable getters (NEGs) from SAES (type St171)
Irreversible binding of (non-noble) gases when heated
Reversible binding of hydrogen when cold
Desorption of hydrogen following Sievert‘s law
log(peq) = 3.6 + 2log(Cgetter) – 5200/T [1]
And for tritium?
[1] www.saesgetters.com/sites/default/files/St 171 - 172_Sintered Porous Getters_1.pdf

## Slide 25: Sorption tests with tritium and mixture
Desorption tests with H2, D2, T2 and H2:HT:T2 mixture (H:T = 1:1)
Loading amount equivalent to 1 GBq HT activity
Reference volume ~60 cm3
Temperature read-out from getter resistivity

## Slide 26: Sorption tests with tritium and mixture
Desorption successful for all gas (mixtures)
Loads of uncertainties
Possible isotope effect? Calculation shows: Changes on scale not relevant for HT spectroscopy
Proven reversible tritium storage!

## Slide 27: The Results:

## Slide 28: Measured lines: R(0)
R(0), R(1) and P(1) measured ν= 02
R(0) (1f signal)
(Hidden)

## Slide 29: Measured lines: R(0)
R(0), R(1) and P(1) measured ν= 02
R(0)
(Hidden for instance)
H2O (1f signal)

## Slide 30: Measured lines: R(0)
R(0), R(1) and P(1) measured ν= 02
R(0) (1f signal)
(Hidden)
Dispersive line shape
(like for HD)

## Slide 31: Measured lines: R(0)
R(0), R(1) and P(1) measured ν= 02
R(0) (1f signal)
Hyperfine splitting enables assignment

## Slide 32: Measured lines: R(1)
R(0), R(1) and P(1) measured ν= 02
R(1) (1f signal)

## Slide 33: Measured lines: P(1)
R(0), R(1) and P(1) measured ν= 02
P(1) (1f signal)

## Slide 34: Measured lines: Comparison to theory
All positions 1.8 MHz off theory (~2 σ)
[1]“Precision Measurement of Vibrational Quanta in Tritium Hydride (HT)”,
F.M.J. Cozijn, M.L. Diouf, W. Ubachs, V. Hermann, M. Schlösser, accepted by PRL (2024)
[2] H2SPECTRE ver. 7.4 Fortran source code, University of
323 Warsaw, Poland (2022).
v=02 | Freq.[1] / MHz | Diff. to theory[2] / MHz
R(0) | 203 396 426. 692 (21) | 1.8 (1.1)
R(1) | 205 380 033. 644 (22) | 1.8 (1.0)
P(1) | 198 824 820. 600 (100) | 1.9 (1.1)
Most accurate spectroscopy of a molecule with tritium!

## Slide 35: Summary: NICE-OHMS on HT
Technical achievements
Successful tritium sample preparation and resorption using NEG
Using only 20 mbar*cm3 HT
Target parameters achieved
No degradation observed
Over 6 weeks continuous measurements
Spectroscopic achievements
v=02: R(0), R(1) & P(1)
Line shape not yet fully understood
Isolated hyperfine component observed
Lamb-dip for low power at isolated hyperfine  Line assignment
Accuracy of 21-100 kHz (rel. 10-10 / <1/10 theory)
Deviation to theory of ~2σ

## Slide 36
Magnus Schlösser
Benedict Rothmund
Frank M. Cozjin
Meissa Diouf
Wim Ubachs
Access Program of Laserlab–Europe (Grants No. 654148 and No. 871124)