## Slide 1: Explainability in Reinforcement Learning: An Application for Powertrain Control
Catherine Laflamme, PhD

## Slide 2: Reinforcement Learning
AlphaZero (2017):
  General-purpose game-playing AI.
  Chess, shogi, and Go at a superhuman level.
  Training solely through self-play, without any prior knowledge of the games.
Success Stories

## Slide 3: RL in Industry Applications
Job Shop Scheduling
Planning in Matrix Production
Routing
Energy Management Systems

## Slide 4: RL in Industry Applications
Where and when RL can be beneficial?
  How big does my state space and action space need to be for RL to beat heuristics?
  How does stochasticity impact results?
Challenges

## Slide 5: RL in Industry Applications
Where and when RL can be beneficial?
  How big does my state space and action space need to be for RL to beat heuristics?
  How does stochasticity impact results?
Simulations
  Creating simulations / digital twins is hard!
  Even when you have the simulation, there is the real-world gap.
Challenges

## Slide 6: RL in Industry Applications
Where and when RL can be beneficial?
  How big does my state space and action space need to be for RL to beat heuristics?
  How does stochasticity impact results?
Simulations
  Creating simulations / digital twins is hard!
  Even when you have the simulation, there is the real-world gap.
Implementing a function approximator is hard for companies to do!
  Lack of transparency/explainability.
  Lack of standard processes.
Challenges

## Slide 7: RL in Industry Applications
Where and when RL can be beneficial?
  How big does my state space and action space need to be for RL to beat heuristics?
  How does stochasticity impact results?
Simulations
  Creating simulations / digital twins is hard!
  Even when you have the simulation, there is the real-world gap.
Implementing a function approximator is hard for companies to do!
  Lack of transparency/explainability.
  Lack of standard processes.
Challenges

## Slide 8: RL in Industry Applications
Can we still benefit from an RL Agent without having to implement a neural network?
Research Question

## Slide 9: Explainability in Reinforcement Learning
Gear shifting logic for an automatic drive vehicle.
Just a good, well understood use case to demonstrate feasibility.
Start boring 
Powertrain Control Use Case

## Slide 10: Explainability in Reinforcement Learning
Gear shifting logic for an automatic drive vehicle.
Just a good, well understood use case to demonstrate feasibility.
Start boring 
Powertrain Control Use Case
RL Agent

## Slide 11: Explainability in Reinforcement Learning
Full vehicle model with internal combustion engine, transmission, powertrain control algorithms.
Used for powertrain matching analysis and component selection, control and diagnostic algorithm design, and hardware-in-the-loop testing
Matlab: Conventional Vehicle Reference Application
https://www.mathworks.com/help/autoblks/ug/conventional-vehicle-reference-application.html

## Slide 12: Explainability in Reinforcement Learning
Matlab: Conventional Vehicle Reference Application
Driving Cycle:
Reference Velocity to be followed

## Slide 13: Explainability in Reinforcement Learning
Matlab: Conventional Vehicle Reference Application
Driver:
Driver generates normalized acceleration and braking commands.

## Slide 14: Explainability in Reinforcement Learning
Matlab: Conventional Vehicle Reference Application
Control Unit: Implements a powertrain control module (PCM) containing a transmission control module (TCM) and engine control module (ECM)

## Slide 15: Explainability in Reinforcement Learning
Matlab: Conventional Vehicle Reference Application
TransSwitch: External input for transmission control model. Allows for external input of gear.

## Slide 16: Explainability in Reinforcement Learning
Goal:
Can we replace this gear shifting logic with an explainable RL-based policy?

## Slide 17: Explainability in Reinforcement Learning
Matlab optimised controller
Inputs:
  Vehicle Speed
  Pedal Position
  Current Gear
Benchmark

## Slide 18: Explainability in Reinforcement Learning
Matlab optimised controller
Inputs:
  Vehicle Speed
  Pedal Position
  Current Gear
Benchmark
State Space

## Slide 19: Explainability in Reinforcement Learning
Fuel Economy
  Total distance / total fuel accumulated for the complete driving cycle.
Evaluation

## Slide 20: Explainability in Reinforcement Learning
Fuel Economy
  Total distance / total fuel accumulated for the complete driving cycle.
Evaluation
Higher is better!

## Slide 21: Explainability in Reinforcement Learning
Velocity Following
Evaluation

## Slide 22: Explainability in Reinforcement Learning
European Union Commission. "Speed trace tolerances". European Union Commission Regulation. 32017R1151, Sec 1.2.6.6, June 1, 2017.
Speed Faults

## Slide 23: Explainability in Reinforcement Learning
European Union Commission. "Speed trace tolerances". European Union Commission Regulation. 32017R1151, Sec 1.2.6.6, June 1, 2017.
Velocity Following

## Slide 24: Explainability in Reinforcement Learning
Benchmark
 | Fuel Economy | # Faults
Matlab | 38.76 | 8

## Slide 25: Explainability in Reinforcement Learning
Driving Cycles

## Slide 26: Explainability in Reinforcement Learning
Gymnasium Environment
Compile Matlab simulation into a *.dll file.
  Can be called in Python via a step() function.
  Includes our reward function

## Slide 27: Explainability in Reinforcement Learning
Gymnasium Environment
Compile Matlab simulation into a *.dll file.
  Can be called in Python via a step() function.
  Includes our reward function
Free parameter

## Slide 28: Explainability in Reinforcement Learning
Stable Baslines implementation
Gymnasium environments are compatible with stable baselines.
Stable Baselines3 is “a set of reliable implementations of reinforcement learning algorithms in PyTorch.”
PPO:

## Slide 29: Explainability in Reinforcement Learning
Hyperparameter Tuning with Weights and Biases

## Slide 30: Explainability in Reinforcement Learning
Results RL Agent
 | Fuel Economy | # Faults
Matlab | 38.76 | 8

## Slide 31: Explainability in Reinforcement Learning
Results RL Agent
 | Fuel Economy | # Faults
Matlab | 38.76 | 8
Summary: Many „good“ neural network policies. Can we use them to form a lookup table?

## Slide 32: Explainability in Reinforcement Learning
Note: We did attempt to train a Q-table from scratch.
  How to discretize continuous variables?
  Very inefficient training
Never obtained a policy better than the benchmark.
Q-Table Attempt

## Slide 33: Explainability in Reinforcement Learning
Method
Train RL Agent
Sample the policy network
  (small state space -> can sample uniformly.)
Train a decision trees with standard supervised learning
  Fix depth of decision tree
Evaluate the decision tree as a lookup-table policy

## Slide 34: Explainability in Reinforcement Learning
Performance on Driving Cycle „FTP“

## Slide 35: Explainability in Reinforcement Learning
Testing on Different Driving Cycles

## Slide 36: Explainability in Reinforcement Learning
Testing on Different Driving Cycles

## Slide 37: Explainability in Reinforcement Learning
Testing on Different Driving Cycles

## Slide 38: Explainability in Reinforcement Learning
Testing on Different Driving Cycles
Smallest DT that outperforms benchmark (in FE and #Faults) on all cycles: depth = 5

## Slide 39: Explainability in Reinforcement Learning
Example Result
Agent | Fuel Economy | # Faults
RL | 46.502527 | 8
DT (Depth 3) | 40.878837 | 0
Matlab Benchmark | 38.762721 | 8
Vehicle Speed [km/h] | 20.45 | 39.55
Engine Speed [rpm] | 2090.91 | 3484.85 | 3545.45 | 3666.67
Pedal Position [0-1] | 0.50
DT (Depth 3, Nodes 15)

## Slide 40: Explainability in Reinforcement Learning
Results

## Slide 41: Explainability in Reinforcement Learning
Conclusions
Sampling a neural network policy could be a method to create a user-friendly and explainable policy for small state spaces.
Larger state spaces (where uniform sampling is not possible) could be possible but not studied here.
Despite small tables, still improved performance compared to benchmarks.

## Slide 42
Thank you!