## Slide 1: Automatic Setup of Controlled Longitudinal Emittance Blow-Up
>> Considerations on RL Feasibility <<
N. Bruchon

## Slide 2: Outline
Introduction to blow-up
  Importance for longitudinal stability
  Blow-up settings
Purpose of RL application
  Definition of State, Actions, Reward
  Critical issues
Solutions with other approaches
  Discussion
Conclusions

## Slide 3: Outline
Introduction to blow-up
  Importance for longitudinal stability
  Blow-up settings
Purpose of RL application
  Definition of State, Actions, Reward
  Critical issues
Solutions with other approaches
  Discussion
Conclusions

## Slide 4: Introduction
Bunch length shrinks during acceleration
  Smaller bunch length may result in unstable beam at extraction
Injection of bandwidth limited noise into the phase loop
  Purpose: diffuse particles in the bunch core, without touching the tails
  Effect: improve beam stability

## Slide 5: Blow-Up in a Nutshell
Synchrotron frequency
Emittance
Noise bandwidth
Profile
Longitudinal
Phase Space
Particles diffuse in the bunch to increase longitudinal emittance:
  Reduced line density peak current
  Increased bunch length
Courtesy of D. Quartullo
Notes: Maybe in back up

## Slide 6: Blow-Up Functions to Optimize
Amplitude, :
  Defined in rms degrees of the 200 MHz RF system
  Too low-amplitude noise signal may be ineffective
  Too high amplitude can negatively affect the bunch distribution
  Zero amplitude means that no blow-up is applied
Frequency band:
  Defined by cutoff frequencies that follow variation of small-amplitude synchrotron frequency,
  Ratios called margins defined by normalizing those values with respect to
    Margin low,
    Margin low,
  The aim of the blow-up is to impact the bunch core exclusively, without increasing the tail population of the particle distribution, which would risk generating losses

## Slide 7: Blow-Up Functions to Optimize
Blow-up interval:
  Time interval along the cycle during which the blow-up is applied
  Defined when RF voltages and synchronous phase are nearly constant
  Limited also by other manipulations

## Slide 8: Outline
Introduction to blow-up
  Importance for longitudinal stability
  Blow-up settings
Purpose of RL application
  Definition of State, Actions, Reward
  Critical issues
Solutions with other approaches
  Discussion
Conclusions

## Slide 9: Purpose
Optimal blow-up settings are essential to ensure longitudinal stability
Automatize the Setup!
  Replace the manual procedure
  Reduce required beam time for optimization
  Results comparability thanks to objective function
Why Reinforcement Learning?
  A trained agent should efficiently solve the problem

## Slide 10: Schematic View
Raw Data Analysis
LHC Software Architecture
Blow-up Noise Generator
Beam Measurements
RL Agent
Environment
Action
Reward
State

## Slide 11: Measurements/Observations
Longitudinal profiles from detectors installed in the SPS
Multi turn acquisitions:
  Data refresh every 20ms
Single bunch
Multi bunch
Analysis software to extract features:
  Peak, Width, FWHM, μ, σ, bunch length, …
Multiple bunches  extract features for each bunch
LHC-beam type consists of bunches
Uniform features are desired across all bunches
Single bunch
Multi bunch

## Slide 12: State
Represent environment: raw data and/or extracted features
  Bunch length is the most critical one
  Additional information about bunches may be useful (shape, intensity, …)
Multi turn acquisitions: when observation must be taken?
Few observations are sufficient but…
information during blow-up is missing
What about adding intermediate points?
Better knowledge and control of the beam aspects taken into account!
WARNING: do not exaggerate with the state dimensions  the problem will become unmanageable soon!

## Slide 13: Action
Variation of settings value
Manually: constant settings
Over multiple points:
  Adapt settings to each interval independently
  More accurate time dependent setup:
    Amplitude could go to zero in some intervals.
    Freq. band could increase or reduce in intervals.
  Better control leads to better results
  Limit actions to avoid losses or ineffective blow-up
Variation of the AMPLITUDE
Variation of the MARGINS

## Slide 14: Reward
The reward must be a scalar
Custom function to calculate it relying on observations
Define the most relevant features with which calculate the blow-up effects
General targets:
  Reach desired bunch length
  Guarantee longitudinal stability
  Ensure uniform bunches
  Control the bunch length evolution.
  Avoid losses
…

## Slide 15: Bunch Length RMSE – Reward example
Multi bunch beam  bunch lengths:
  Error vector:
    Desired bunch length: , constant for all sub-interval observations
  Filtered error vector:
    With tolerance band defined by :

## Slide 16: Critical Issues
Training an RL agent requires data:
  from the real system
  from a simulator
Data efficiency is mandatory:
  Training should rely on as little data as possible
Data collection should not take long time:
  Fast creation of dataset

## Slide 17: Real World Data
Single LHC cycle () in the SPS super-cycle ()
State is collected at the end of the cycle
  Single sample every
samples  hours
without considering eventual issues along the acceleration chain
Relying on real data requires too much machine time  Unfeasible!

## Slide 18: Simulated Data
Beam Longitudinal Dynamics (BLonD):
  CERN simulation suite for longitudinal particle tracking in synchrotrons.
It generates the blow-up effects on the longitudinal profiles:
  “raw data” to analyse
It can replace the real machine and provide data according to blow-up settings
Issues on the calculation time!
Single cycle with uniform settings hours
Grid search (simulations in parallel) with uniform settings days
BLonD

## Slide 19: A dead end…
Too long time to collect enough data for training RL agent
  Only uniform settings were considered, exponential growth of problem complexity with intermediate points…
Software for optimal blow-up was required as soon as possible
 Generic optimizers to replace RL solutions

## Slide 20: Outline
Introduction to blow-up
  Importance for longitudinal stability
  Blow-up settings
Purpose of RL application
  Definition of State, Actions, Reward
  Critical issues
Optimization loop
  Alternative approaches
  Discussion
Conclusions

## Slide 21
GeOFF & COI
sps-blowup
┣━ sps_blowup
┃ ┣━ __init__.py
┃ ┣━ _baseenv.py
┃ ┣━ _machine.py
┃ ┣━ _realprofiles.py
┃ ┗━ _analysis.py
┣━ setup.py
┗━ README.md
SPS blow-up optimization
Blow-up parameters
SET
GET
Raw Data Analysis
LHC Software Architecture
Blow-up Noise Generator
Beam Measurements
Environment
Beam info

## Slide 22: Integration in the CERN Optimization Framework
Generic Optimization Frontend
and Framework (GeOFF)
“… graphical application for generic numerical optimisation and reinforcement learning on CERN accelerators.
It bundles:
Interfaces to the machines and simulations thereof
Numerical optimisers and reinforcement learners that can use these interfaces.”
Common Optimization Interfaces (COI)
“… facilitate using numerical optimization and reinforcement learning (RL) on the same optimization problems. This makes it possible to unify both approaches into a generic optimization application in the CERN Control Center.”
Inheritance diagram of the core interfaces

## Slide 23: Configuring the Tool
Parameter Group: RF BEAM CONTROL Property: SpsLowLevelRF/LongitudinalBlowUp
Interval
Amplitude
Margin high
Margin low
Check parameters in LSA
  Select the noise settings to optimize and set their min-max range
    Amplitude, margin low, margin high
  Set the number of sub-intervals, the start time and end time
  Set the number of bunches in the circulating beam
  Set the target bunch length
Run the optimization in GeOFF
  Select the Machine: SPS
  Select the User
  Environment: SPS-BlowUp-Real-v0
Push Start and… sit back and relax!

## Slide 24: Results
Scan of and on two sub-intervals
Target bunch length: ns---
Int. per bunch: ppb - # bunches:
Bayesian optimization
Scan of and on three sub-intervals
Target bunch length: ns
Scan of , and on two sub-intervals
Target bunch length: 1 ns
Intensity per bunch: ppb - # bunches:
Generic optimization (BOBYQA)

## Slide 25: Discussion
Trade-off: optimization time and bunch length constant
More sub-intervals mean more iterations
More sub-intervals ensure flatter bunch length
Acceptable results with two and three sub-intervals
Single sub-interval: faster, suitable if a constant bunch length is not required
Four sub-intervals: longer time required for limited improvement in bunch length
Bayesian optimization
  Dataset for exploration by grid search
  Fixed number of steps for optimization
Drawback: increased number of steps
  Need of mitigation strategies (e.g., reuse previous data, define convergence criteria, …)

## Slide 26: Outline
Introduction to blow-up
  Importance for longitudinal stability
  Blow-up settings
Purpose of RL application
  Definition of State, Actions, Reward
  Critical issues
Solutions with other approaches
  Discussion
Conclusions

## Slide 27: Conclusions
An operational tool to automatically setup the controlled longitudinal emittance blow-up for high-intensity multi-bunch LHC beams was developed
  Integration in LSA and the CERN optimization framework
  Simple objective function is based on RMSE
  Sequential setup by splitting blow-up duration in sub-intervals
Blow-up setup successful for high intensity proton LHC beams
  Promising results with Bayesian optimization, improve sample-efficiency
Released software supports the extension to RL methods
  Faster way to simulate data
  Improve sample-efficiency

## Slide 28: Automatic Setup of Controlled Longitudinal Emittance Blow-Up
>> Considerations on RL Feasibility <<
N. Bruchon

## Slide 29: Blow-up Past Presentations/Publications
ML and data analysis discussions:
  03/03/2022
ML Community Forum meetings:
  29/04/2022
  30/11/2022
IPAC 22:
  TUPOST42 (proceedings)
  09/06/2022 (poster)
SPS MPC:
  06/06/2023
ICALEPCS 23:
  07/12/2023 (flash presentation)
Blow-Up parameters during the online optimization Beam process: HIRADMT2 Hiradmat_4Inj_FB11100_FT500_Q20_2021_V1
0.35
0.2551
0.6375
0.64
02:56:36
03:06:17
Parameters:
Amplitude
Margin low
Nov. 2021
Configurations
Data on the LHCPILOT Cycle
Summer 2022
ML: Machine Learning

## Slide 30: Common Optimization Interfaces
CERN ML Project:
  Numerical Optimization - Machine Learning (ML) - Reinforcement Learning (RL)
  for operations in the CERN accelerator complex.
CERNML-COI:
  Common Optimization Interfaces (COI) to apply CERN ML solutions on the same problems.
  Unification of all approaches into a generic optimization application in the CERN Control Center.
CERNML-COI-UTILS:
  Provides utility functions and classes that make it easier to work with the COI.
  Improvable keeping the COI stable.
Generic Optimisation Frontend and Framework (GeOFF):
  This is the graphical application for generic numerical optimisation and reinforcement learning on CERN accelerators.
ENVIRONMENT:
  Statement of the problem to be managed by the generic optimizers.
  It should be encapsulated in an appropriate structure and follow some rules.

## Slide 31: Some Existing Environments
Optimization of the steering for ISOLDE:
  Problem of steering optimization for ISOLDE. The goal is to steer the ion beam via electrostatic elements such as to maximize the intensity measured by a downstream Faraday cup.
Optimization of the LEIR Transfer Line:
  Problem of alignment in the ETL transfer line towards LEIR. The goal is to adjust the current over time of the BHN10 kicker so that the first injection in a cycle has maximum injection efficiency, and all subsequent injections in a cycle land in the same orbit as the first one.
Optimization of the Tune in the SPS:
  Problem of tune optimization in the SPS. The goal is to manipulate the horizontal and vertical tune at two times within a cycle so that it maximizes the transmission. The transmission is defined as the beam intensity at the beginning of slow extraction divided by the beam intensity at the end of injection.
Optimization of the ZS Alignment in the SPS:
  Problem of ZS alignment in the SPS. The goal is to move 9 anodes in such a manner that during slow extraction, the beam passes the electromagnetic septum and does not hit the beamline walls.
Optimization of the Blow-Up in the SPS:
  Problem of Blow-Up setup in the SPS. The goal is to reach a desired longitudinal emittance by controlling the amplitude and the frequency margins of the noise injected in the phase.

## Slide 32: GeOFF
Supercycle
Optimization
Visualization
Num. Opt.
Machine
Cycles
Tabs
Environment
Algorithm
Train RL Agent
Run RL Agent

## Slide 33: LSA Integration: Functions
Advantages of the LHC Software Architecture:
  Keep in the database settings of all managed device/properties
  Every change in control value (trim) is registered
    Trim history and rollback
Use of LSA for all tools settings
Optimizable functions:
Amplitude
Margin Low
Margin High

## Slide 34: LSA Integration: Discrete Settings
Parameter Group: RF BEAM CONTROL EXPERT Property: SpsLowLevelRF/LongitudinalBlowUp
Parameter Group: RF BEAM CONTROL Property: SpsLowLevelRF/LongitudinalBlowUp
(*) Test parameters for user LHC2
(*)
(*)
Interval
Amplitude
Margin high
Margin low

## Slide 35: Amplitude Scan in the SPS
Blow-up interval: 19085 – 23585 [ms]; Num. sub-intervals: 4
  Skeleton Points: 17585, 19085, 20585, 22085 [ms]
  Observation Points: 19085, 20585, 22085, 23585 [ms]
Parameters: Amplitude
  Amplitude Range: [0, 1]
Scan
Scan
Scan
Scan
sub
sub
sub
sub
Algorithm: BOBYQA

## Slide 36: Results in the SPS
Target bunch length:
  Tolerance: ±5% 
Problem solved in 31 iterations (Num. sub-intervals: 4).
Amplitude scan
Objective function
Bunch lengths
Scan
Scan
Scan
Scan
Scan
Scan
Scan
Scan
Scan
Scan
Scan
Scan
Scan : 0, 8
Scan : 9, 16
Scan : 17, 26
Scan : 27, 31
Iterations per sub-interval

## Slide 37: Results Portability
Blow-up optimized for single batch, 06-10-2022.
Intensity per bunch: 1.2 e11 p/b
Average bunch length per extraction: 1.76 ns
  Average bunch length at injection: 2.68 ns
Results on 5 batches without optimizing, 13-10-2022.
Intensity per bunch: 1.5 e11 p/b
Average bunch length per extraction: 1.81 ns
  Average bunch length at injection: 2.82 ns
Scraping EXERCISE

## Slide 38: LSA Function Trim
Amplitude Optimization
Interval per interval research of the optimal amplitude to keep the bunch length constant.