## Slide 1: Adaptive X-ray Fluorescence Imaging
Daniel Ratner
February, 2024

## Slide 2: X-ray Fluorescence Imaging
Image courtesy Horiba
X-ray Fluorescence Imaging (XRF):
Relatively new imaging method measures quantitative elemental maps
Scan x-ray probe (with variable resolution) around the sample
Fluorescence proportional to composition
Courtesy TU Delft et al
Famous example #1: Van Gogh study of the potato-eaters
Map composition to pigment
Recover picture underneath in color!

## Slide 3: X-ray Fluorescence Imaging
Hall, Bergmann, Morton, et al.
Famous example #2: Archimedes Palimpsest
Archimedes text from the Medieval period was erased, copied over, and then further tampered in the 20th century
XRF identifies original writing by elemental composition
Recovered only example of a lost Archimedes text on “early calculus”!

## Slide 4: X-ray Fluorescence Imaging
Close-up of quills
Phosphorous scan
Famous example #3: Thermopolis Archaeopteryx
Phosphorous scan reveals bone details, including first images of quills (albeit still at low resolution)
Uwe
Bergmann

## Slide 5: X-ray Fluorescence Imaging
Close-up of quills
Phosphorous scan
Famous example #3: Thermopolis Archaeopteryx
Phosphorous scan reveals bone details, including first images of quills (albeit still at low resolution)
Uwe
Bergmann
Image is VERY sparse… hours of scanning and less than 1% of pixels capture quill region!

## Slide 6: X-ray Fluorescence Imaging
Sign of early life?
Sparse structures appear in Zinc map
Possible early life signature?
Calcium
Zinc
Sam Webb

## Slide 7: Adaptive XRF for Sparse Samples
Sam Webb
Ground truth
Key in on high value regions
Loop 1
Loop 2
Loop 3
Rough (human) approach for adaptive sampling:
Low resolution scans identify rough areas of interest
Increasing resolution focuses on most interesting/uncertain regions
Final reconstruction combines all measurements

## Slide 8: RL or BO?
Reinforcement learning
Advantages
Incorporate rich priors with pre-trained deep NN
Easy implementation of high-dimensional inputs and outputs
Fast executing at inference
Disadvantages
Very data hungry (effectively requires simulation)
Requires retraining when distribution changes
Expensive to train
Bayesian optimization (GP)
Advantages
Can handle small data sets
Relatively robust to changing conditions
No need for pre-training in a simulation environment
Disadvantages
Expensive to operate at inference
Poor scaling with big data
Poor scaling to high dimensional inputs/outputs
Priors relatively weak
Caveat: BO with NNs blurs these distinctions

## Slide 9: RL for XRF
Action: Select aperture, position, exposure
Interaction with Environment: Acquire data
State: Acquisition parameters and data returned to agent
Reward: Final reconstruction quality (e.g. RMS error) and acquisition time penalty
Sam Webb
Ground truth
Key in on high value regions
Loop 1
Loop 2
Loop 3
Translating to an RL problem:
https://en.wikipedia.org/wiki/Reinforcement_learning
Two styles of actions:
Exposure map
Trajectory control

## Slide 10: RL for XRF
Simplify problem:
Force measurements to monotonically increase resolution
Force measurements to scan every pixel (no path planning)
   Policy chooses an exposure map
Loss function minimizes RMS error and total exposure time
Purely convolutional architecture  allow arbitrary image shapes
Drawbacks:
Training constrained by image reconstruction (needed for reward)
Small network trained with a GA
Preliminary simulation studies of simple system
Jean Betterton et al., ICRA, 2020

## Slide 11: RL for XRF
First studies by Jean Betterton (Stanford):
Jean Betterton et al., ICRA, 2020
Examples on a synthetic checkerboard pattern and real fossil data
(Both run in simulation environment)

## Slide 12: XRF Scanning schematic: Deep learning version
Measurements
Low resolution
Mid resolution
High resolution
Exposure
Uniform raster
Reconstruction
Policy
NN
NN
Policy
Sample
Loss
Note: This is just a PINN!

## Slide 13: XRF Deep RL: Toy example
Adaptive policy, Avg exposure = 1, avg loss = 0.055
Sample #1

## Slide 14: XRF Deep RL: Toy example
Upshot: better loss (0.19 vs. 0.22) with 8x shorter exposure (0.12 vs 1) compared to uniform sampling
Adaptive, Err=0.055
Exposure = 1
Adaptive, Err=0.19
Exposure = 0.12
Raster, Err=0.22
Exposure = 1
Ground truth

## Slide 15: Experimental configuration
SSRL hard x-ray, wiggler-based beam line
Sample size up to 300 mm x 1000 mm
Supports XRF/XAS techniques, as well as XRD
Hexapod optics platform for rapid encoded switching between beam sizes
Dedicated beam line allows expanded science program
  Rapid screening for remote access
  Large scale soil core pilot program
  Large scale animal tissue screening
Experiments to happen at SSRL BL 7-2
Sam Webb

## Slide 16: Experimental configuration
Custom optic holder & hexapod allows for the ability to easily change between optics
“Pie slice” for macro-imaging beam lines allows switching between several different types of optics – capillaries, pinholes, SIGRAYs
Critical capability to enable adaptive scanning methods with ability to change between encoded beam focus positions.
New optics allows automated, adaptive switching of focus
Sam Webb

## Slide 17: XRF Deep RL: Realistic samples
New project just funded for deep-learning RL on XRF
Tobias Boltz, Sam Webb
Example of realistic sample (still in simulation environment)

## Slide 18: XRF Deep RL: Realistic samples
New project just funded for deep-learning RL on XRF
Tobias Boltz, Sam Webb
Factor of ~3-5 speed-up
To improve we will try:
Sparser samples
Stronger priors
More specific loss functions (ignore low-signal regions)
Trajectory control (instead of exposure map) may be necessary

## Slide 19: XRF Deep RL: First experimental test
First experimental test failed. Some possible issues:
Tobias Boltz, Sam Webb
Zig-zag pattern highlights challenge of matching simulation to experiment
NN reconstruction seems to be bottleneck
 Next experiment (March) will use statistical reconstruction
Priors too weak. Networks should match specific tasks

## Slide 20: RL vs. BO Comparison
Reinforcement learning
Advantages
Incorporate rich priors with pre-trained deep NN
Easy implementation of high-dimensional inputs and outputs
Fast executing at inference
Disadvantages
Very data hungry (effectively requires simulation)
Requires retraining when distribution changes
Expensive to train
Bayesian optimization (GP)
Advantages
Can handle small data sets
Relatively robust to changing conditions
No need for pre-training in a simulation environment
Disadvantages
Expensive to operate at inference
Poor scaling with big data
Poor scaling to high dimensional inputs/outputs
Priors relatively weak
Caveat: BO with NNs blurs these distinctions

## Slide 21: Ghost Imaging / Compressive Sensing for X-rays
Radiation, a
Target, x
b = [ 5037,
4783,
4891, … ]
Bucket measures total transmission
Reconstructed Target, x*
=
b
x
a
Ghost imaging / single pixel camera / compressive sensing:
Non-adaptive approach
Random probe in sparse representation

## Slide 22: Random sampling vs. Adaptive Experiments
Toy problem: search for single sparse signal out of n pixels
Assume complete freedom to shape probe
Adaptive approach:
Binary search
 log2(n) measurements

## Slide 23: Random sampling vs. Adaptive Experiments
Toy problem: search for single sparse signal out of n pixels
Assume complete freedom to shape probe
Adaptive approach:
Compressive sensing/ Ghost imaging approach:
Randomly probe sample and solve by optimization
Binary search
 log2(n) measurements
C log(n) measurements
With C ~ small number
In what situations can adaptive experiments outperform compressive sensing?

## Slide 24: Conclusion
Thanks to Jean Betterton, Tobias Boltz, Mykel Kochenderfer, Willie Neiswanger, and Sam Webb
RL promising for X-ray imaging of certain sparse use cases
Matching simulations to experimental setup is challenging
Benefits still not sufficient to justify effort… research into competing methods ongoing in parallel
Conclusions so far: