## Slide 1: Experiences with SIRIUS Booster
Fernando Henrique de Sá
On behalf of the LNLS Accelerator Physics Group
Injectors for Storage Ring Based Light Sources
Karlsruhe, 6-8 of March 2024

## Slide 2
CNPEM campus
SIRIUS design parameters
Energy 3.0 GeV
Circumference 518.4 m
Emittance 250 pm.rad
Current (top-up) 350 mA
Green-field facility
Construction: 2012 – 2020
Cost: US$ 500M (∼85% spent in Brazil)
1st regular users call: Nov. 2022
10 beamlines in operation
100 mA in top-mode mode, uniform fill
Phase-1 (end of 2024): 14 beamlines
Campinas
Brazil
SIRIUS – 4GSR in Operation
Brazilian Center for Research in Energy and Materials (CNPEM)

## Slide 3
CARNAÚBA
(nanoprobe)
CATERETÊ
(CDI/XPCS)
EMA
(Extreme Cond.)
IMBUIA
(nano & m FTIR)
MANACA
(MX)
SABIÁ
(XMCD/PEEM)
IPÊ
(RIXS/ XPS)
SAPÊ
(ARPES)
PAINEIRA
(XPD)
SAPUCAIA
(SAXS)
QUATI
(XAFS)
JATOBÁ
(PDF)
CEDRO
(SRCD)
MOGNO
(mCT)
OPERATION
https://www.lnls.cnpem.br/beamlines/
83 submitted
20 approved
67 submitted
41 approved
41 submitted
24 approved
45 submitted
26 approved
82 submitted
33 approved
Third Cycle of Proposals (1S 2024)
Total: 422 submitted / 225 approved
From Brazil: 376 submitted / 198 approved
Form abroad: 46 submitted / 27 approved
18 submitted
15 approved
46 submitted
36 approved
40 submitted
30 approved
Fast track
Fast track
INSTALLATION
CONSTRUCTION
SIRIUS Beamlines – Phase 1
Courtesy: Harry Westfahl

## Slide 4: Storage Ring Injection
Low emittance booster required!

## Slide 5: Booster Design

## Slide 6: Lattice Design
Dipoles with defocusing quadrupole and sextupole components;
Large spaces between magnets:
  enough room for RF cavity and injection/extraction systems;
Symmetric lattice, without non-dispersive straigth sections:
  simpler, cheaper and with uniform distance to storage ring;
Compact magnets:
  supported by girders attached to inner walls of tunnel;

## Slide 7: Linear Optics
Optimized for low emittance → low momentum compaction;
Nominal linear optics with 50 dipoles and 50 QFs;
Nominal chromaticity adjusted to 0.5 with 25 SF sexts and dipoles;
Tune and chromaticity correction with 25 QD quads and 10 SD sexts;
Orbit Correction with 50 BPMs, 25 CH and 25 CV magnets;
BPMs are not placed close to peaks of optical funcions;
Circumference | 496.8 m
Harm. Number | 828
Tunes | (19.20, 7.31)
Chromaticities | (0.5, 0.5)
Nat. Chrom. | (-33.7, -13.9)
Mom. Compaction | 7.2x10-4
Nat. Emitt.@3GeV | 3.5 nm.rad
Nat. En. Spread@3GeV | 0.09 %
Nat. Bun. Len.@3GeV | 11.2 mm

## Slide 8: Orbit Correction and Dynamic Aperture
Error | Dipole | Quad. | Sext.
Alignment x, y | 160 um |  | 
Rotation Roll | 0.8 mrad |  | 
Excitation | 0.15 % (grad. 2.4 %) | 0.3 % | 0.3 %
Mult. Normal | ~4x10-4 |  | 
Mult. Skew | ~1x10-4 |  | 
Simulations with realistic errors;
Low residual orbit;
Good dynamic aperture and momentum aperture;

## Slide 9: Injection System
Linac beam @ 150 MeV: εx,y = 170 nm.rad, σδ = 0.5%;
Geometry requires strong septum (21.5°) and kicker (19.3 mrad);
Optics (β, α, η, η’) at end of TL matched to booster optics;
Booster horizontal acceptance:
  4-σ of beam size;
  1 mm of orbit distortion;
  4.5 mm of transverse oscillations
  1.5% of energy oscillation;
Three screens were considered to help checking optics matching;
100% of ramp efficiency in commissioning simulations.

## Slide 10: Ejection System
Optics at beggining of TL matched to optical functions of booster (including dispersion and its derivative);
Weaker ejection kicker (~2.1 mrad) and septa (~3.6°);

## Slide 11: Commissioning

## Slide 12
Booster and SR sharing same tunnel
Commissioning concurrently with the installation of the SR:
  Intermitent commissioning schedules;
  Facilities not well conditioned yet -> poor temperature stability;
  Installation activities delaying commissioning:
    Magnets and BPM cables inversion;
    Mal-functioning power supplies;
    SR permanent magnet temporarilly stored close to booster;
Interference of SR power supplies on booster and TLs orbit:
  SR magnets cable positions optimized to minimize magnetic field on booster under nominal operation currents for all PSs;
  Only few SR PSs on -> no beam on booster;
  Even with all SR PSs on, the booster orbit changes in comparison to when they are off;
Interference of booster ramping on storage ring orbit:
  Mainly on the horizontal plane;
  Created by the dipoles;
  Effectively attenuated by SR fast orbit feedback.

## Slide 13
Septa Issues
Strong effect of eddy current:
  Peak of magnetic field displaced in relation to peak of current;
  Strong quadrupole at injection septum → re-matching of TL;
  Injection at 1/3 Hz due to temperature rise when pulsing at 2 Hz;
Initially there was a large effect on orbit due to leak fields;
Max. Field
Injection

## Slide 14
Orbit Issues
Energy deviation variation along ramp:
  low momentum compaction + variation of velocity → energy deviation variation;
  Easy to miss in design stage:
    slippage factor ≈ momentum compaction even at low energies;
    For the SIRIUS booster 1/γ2 ~ 1.3x10-5 @150MeV, while α = 7.2×10-4
  The orbit correction system ineffective:
    booster and the SR have the same master RF oscillator;
  Booster realigned to correct energy deviation at low energy: improve ramp eff.;
Large residual horizontal orbit due to small number of HCMs:
  Not predicted by simulations from design stage;
  Similar orbit signature along ramp;
  Possibly related to sorting of magnets installation order (correlated errors);
  Ongoing studies to add corrector magnets and/or realign some magnets.

## Slide 15
Optics Characterization
Orbit response matrix measured along all ramp;
LOCO fitting at some points (without using dispersion data);
Tunes and beta-beating predicted by model:
  Large beta-beating, but results are ok for a booster;
Dispersion measured at low energies:
  Difference to LOCO fitted model is not alarming;

## Slide 16
Transverse Emittance Exchange (TEE)
P. Kuske and F. Kramer, “Transverse Emittance Exchange for Improved Injection Efficiency”, in Proc. IPAC’16, Busan, Korea, May 2016, pp. 2028–2031. doi:10.18429/JACoW-IPAC2016-WEOAA01

## Slide 17: Current and Future Operation

## Slide 18
Current Operation in Top-up Mode
Current operation performance:
  Top-up mode: single-shot every 3 min;
  Average injected current per pulse: 0.220 mA;
  Control of injected current with Egun bias voltage.
Ocasionally BO vert. orbit changes between 2 states (flip-flop):
  Correction signature imply field distributed along the ring;
  Generally happens after machine maintenances;
19:00
09:00
11:00
13:00
15:00
17:00
07:00
100.2
100.3
Current [mA]
99.9
99.8
99.7
99.6
100.0
100.1
100.0 ± 0.3 mA

## Slide 19
Future Requirements for Operation
In August 2024 SC RF cavities will be installed in the SR:
  Stored current will probably increase to 200mA;
  Lifetime is expected to be about half of present value;
  Same injection scheme -> ~0.9mA per pulse;
Multi-bunch needs optimization at high currents:
  Linac was specified so that BO would ramp 1.7mA;
  Today, maximum current delivered is ~1.1mA;
Single-bunch injection:
  Important to provide top-up operation with arbitrary fillings;
  Not ready for operation. Very low efficiency (<10%);
  Optimization also required for LINAC;

## Slide 20
Summary
A low-cost small emittance booster was designed:
  Symmetric lattice and small number of magnet families and PSs;
  Simple scheme for tune and chromaticity correction;
  The number of corrector magnets was too small;
  Small momentum compaction is an issue.
In 2019 the booster commissioning was intervealed with the SR installation:
  Intermitent scheduling. Main objective was to start SR commissioning ASAP;
  Difficulty to perform detailed characterizations;
From 2020 to last year a large effort was applied to the SR:
  Increase of operation current, top-up;
  Orbit stability, "transparent SR Injection", IDs installation and commissioning;
  Little time dedicated to booster optimization;
Booster performance meets current requirements;
Work required to reach future operation demands:
  Improvement of orbit correction;
  Optimization of single-bunch mode;
  Improvement of multi-bunch ramp efficiency at high currents;
  Investigation of solutions to septa heating issues;

## Slide 21: Thank you for your attention!
Thanks to Murilo Alves and all my colleagues that helped putting this presentation together.