## Slide 1: ALS-U Injector(s)
Christoph Steier
ALS-U Accelerator Physics and Commissioning Manager
iFAST Injector Workshop, March 7, 2024

## Slide 2: Outline
Introduction: ALS-U
Swap-Out Injection
New accumulator + booster modifications
R&D results on injection elements for swap-out
Accumulator status (installation in progress)
Summary

## Slide 3: ALS-U Project
ALS-U will deliver a world-leading light source that provides users with bright, high-coherent-flux soft x-rays
  High-level Goals:
  Achieve an increase in brightness and coherent flux of soft x-rays (@1 keV) of at least 2 orders of magnitude beyond today’s ALS capabilities
  Develop a set of experimental capabilities that will enable leadership in soft x-ray science
  Provide infrared and hard x-ray capabilities comparable to present-day ALS
Today’s ALS
Future ALS
Electron Beam Profile
3BA
9BA

## Slide 4: ALS-U Scope
Linac
(existing)
Booster Ring
(existing)
ATS and STA
transfer lines
  New 2.0 GeV 9BA storage ring in existing cave optimized for low emittance and high soft x-ray brightness and coherent flux
  New 2.0 GeV Accumulator Ring for full energy swap-out injection and bunch train recovery
  New full-length undulators optimized for high coherent flux
  The Accumulator Ring is being installed and will be commissioned early in order to minimize the risk and duration of one-year dark period; Storage Ring, ATS+STA will be installed during dark period
BTA injection line

## Slide 5: More than two order of magnitude brightness improvement, 69 pm emittance, diffraction limited to ~ 1.5 keV
9 Bend achromat lattice with reverse bends and high field Hbends in 3 sectors for hard x-rays
Small, optimized beta functions in straights
~2.5% dynamic momentum aperture in arcs
On-axis injection (swap-out) needed
Storage Ring | Design
Energy | 2.0 GeV
εx (full coupling) | 69 pm
εy (full coupling) | 69 pm
Δp/p | 0.98 x 10-3
σx/y @ ID | 12 μm/14 μm
σx/y @ Bend sources | 7 μm/10 μm
Bunch Length (FWHM) | 110 ps
Current | 500 mA
Lifetime | ~1 h
Improvements: Emittance, undulator length, undulator technology+gap, smaller βx: Overall: >100x @ 1 keV
C. Sun

## Slide 6: Swap-Out Injection

## Slide 7: Performance enabling ALS-U feature – Bunch train swap-out
Stored Beam
Injected Beam
Fast Kicker
Stored Beam
Injected Beam
  Swap-out enables:
  lattices with smaller dynamic apertures  higher brightness
  Small round apertures  improved undulator performance
Off-axis injection + accumulation
On-axis swap-out injection
(initially proposed by M. Borland)
requires larger
apertures
can use smaller
apertures
Allows for small (~6mm) round apertures
Delta/Apple-X undulator
Permits higher performance polarizing undulators
Allows lattices with stronger focusing + higher brightness
S. Omolayo
E. Wallen

## Slide 8: Injector Requirements for Swap-Out
Hard requirements:
  Sufficient charge per bunch
  Sufficiently small emittance
  Stable pulse to pulse (charge, position, angle, energy, …)
Desired
  Cost + space optimized
  Minimized beam losses – ALARA
  Minimum perturbations on user photon beams - transients
For ALS, booster is fairly small – hard to achieve sufficiently small emittance
Booster also makes charge recovery from SR difficult
Accumulator ring comes with inherent stability of a storage ring
Selected full energy accumulator with bunch-train swap out

## Slide 9: Accumulator location in SR tunnel is optimal solution
Advantages:
  Easing lattice design for
  Much shorter transfer lines from/to Storage Ring
  Minimal alteration of floor plan and shielding
    Evaluated access issues with building code official and fire marshal
    Finished study of seismic issue.
Potential Challenges:
  Somewhat crowded tunnel space
  Supports are non-trivial
    Both challenges were overcome in ALS-U design and accumulator construction

## Slide 10: ALS-U Operation/Fill Modes
Advantages of bunch train swap-out with recovery
  minimizes number of lost/dumped electrons
  reduces demands on injector
  made swap-out-kicker development easier
ALS-U expected lifetime ~1 h @ 500 mA
  Need to replace 0.09 nC/s
  Booster routinely delivers 1 nC/s
Planned Swap-out Timing:
  Between SR swap-out injections the AR train is filled from the BR in Top-Off mode.
  AR injection between 1 and 4 BR bunches per shot, at up to 1Hz.
  Do not need to top-off every bunch in single swap-out, could spread over multiple swap-out cycles if necessary
To achieve 1% current stability, swap-out would need to happen every 36 seconds (500 mA)
  User experience at ALS shows ALS minimum of 12 seconds between injections is acceptable
Can maintain bunch-to-bunch current variation around 10%, similar to ALS
Storage-ring bunches transferred to accumulator
Accumulator bunches transferred to storage ring
New ALS storage ring
New accumulator ring
Fast kicker magnets

## Slide 11: New Accumulator and Booster modifications

## Slide 12: AR Parameters
emittance for ~100% injection efficiency into the SR
<50 mA average current beam (1/11 of SR)
  1 train of 25 or 26-bunches
Enables swap-out every ~30 s
  Modest lifetime requirement for accumulator
Top-off injection to replenish SR train in between swap outs
  Accept (relatively large) beam from existing ALS gun/Linac/booster
  >95% injection efficiency (from booster)
Fit into ALS tunnel against inner shielding wall, leave serviceable corridor between AR and SR
Small AR magnet apertures to minimize magnet size, weight
AR has same rf frequency as the SR
  AR circumference is “quantized”

## Slide 13: Accumulator uses Triple-Bend-Achromat lattice
Scaled-down and optimized version of ALS TBA (circumference ~14m shorter)
  12 sectors
Lattice optimization done w/ genetic algorithm (MOGA)
  1.8 nm emittance
  Finite dispersion in straights
Straight magnetic-axis, combined-function bends
Magnet apertures significantly narrower than in ALS
  Optimizing weight, power consumption and cost
3 Bends (combined function, defocusing gradient)
Quadrupoles (QF,QFA, QD)
Sextupoles (w/ correctors)
  1 skew-quad corrector
  6 dipole correctors (two of them fast)
6 BPMs
C. Sun

## Slide 14
Error Sources considered (using simulated commissioning toolkit – SC):
  Systematic multipoles errors
  Random multipole errors
  Mechanical, assembly imperfections
  Magnet misalignments
Achieve dynamic and momentum aperture close to physical apertures – predict rapid commissioning
Impact of differential circumference variations (AR/SR) is small
Extensive simulations determined magnet and other error tolerances
Dynamic Momentum Aperture with errors is larger than RF acceptance
T. Hellert

## Slide 15: Booster Upgrades
Linac+Booster have previously been refurbished
  Power supplies, controls, timing, vacuum instrumentation, …
Accumulator (with bunch train recovery) relaxes requirements on injector
Charge and emittance from Booster sufficient for ALS-U
ALS-U upgrades are limited to expanding booster energy to 2.0 GeV
  Dipole power supply
  RF cavity power coupler

## Slide 16: R&D results

## Slide 17: Swap-out kicker concept was demonstrated at ALS with beam, full-scale prototype is currently in fabrication
2m long
W. Waldron

## Slide 18: R&D pulser and stripline kicker beam tested over full year in ALS
Stored Beam
Injected Beam
Fast Kicker
On-axis swap-out injection
(initially proposed by M. Borland)
can use smaller
apertures
  Successful swap-out technology demonstration on ALS:
  6 mm full (vertical) gap stripline kicker installed in ALS in 2017
    In user operations for several years
  Verified impedance and thermal design
  Kicked single bunch, mapping the time structure and reproducibility of pulser
In house design for kicker and pulser
Beam based characterization of rise/fall-time and reproducibility
W. Waldron
C. Swenson, C. Pappas, S. De Santis, C. Steier

## Slide 19: Accumulator progress

## Slide 20: Accumulator Manufacturing and Installation
Design work is complete, integration and installation plan are mature
Received majority of mechanical hardware (for example vacuum, magnets, supports fully received)
Prestaging output close to target rate, handoffs to removal and installation work well, good collaboration for installation support
Starting electrical installations (rack baseplates, RF HPA); AR AC distribution was previously installed
Completed full project cycle: Design, Integration, Manufacturing, Testing, Assembly, Installation Support -> basis of SR plan
Integrated testing and commissioning planned for 2025
Accumulator rafts, dipoles, vacuum chambers, and straight: installed several full sectors and started vacuum integration
Electronics racks at off-site storage
MPS chassis
PS Rack
RF HPA
RF Cavities

## Slide 21: Summary
ALS-U will reach diffraction limit for soft x-rays (69 pm emittance)
Lattice optimization aided by choice of on-axis swap-out injection
Swap-out needed injector upgrades – optimum choice was full energy accumulator with bunch train swap-out
Accumulator manufacturing and installation is well advanced, commissioning in 2025
ALS-U upgrade will be complete afterwards during one year darktime starting in 2026

## Slide 22: Acknowledgements
ALS-U is very large project, but for the topics of this talk:
Leads for swap-out R&D:
  Will Waldron, Stefano de Santis, Chuck Swenson, Christoph Steier
Accumulator Design:
  Physics Lead(s): Marco Venturini, Christoph Steier
  Mechanical: Steve Virostek
  Electrical: Will Waldron

## Slide 23: Backup Slides

## Slide 24: Science Case for ALS-U
Soft x-ray light, which has the appropriate energy to interact strongly with the electrons that determine the chemical, electronic, and magnetic properties of materials, and
High coherent flux delivered in a nearly continuous wave, which is necessary to resolve nanometer-scale features and interactions and which allows real-time observation of chemical processes as they evolve and materials as they function.

## Slide 25
Baseline is mature and stable, and reaches soft x-ray diffraction limit up to 1.5 keV
Major design choices have remained throughout R&D and design phases – 9 bend achromat, bunch trains swap out, accumulator, HBends
Bunch train swap-out using demonstrated kicker/pulser technology
Small aperture NEG coating
High Field PM bend magnets

## Slide 26
ALS-U: nine-bend achromat with reverse bends
ALS today: triple-bend achromat
Nine-bend achromat lattice reaches the soft x-ray diffraction limit up to 1.5 keV
Large increase in coherent fraction due to lower emittance and smaller b-functions
75

## Slide 27
High Field Bend Magnets
Reverse Bends
Performance enhancing lattice features: Reverse bends & high-field bend magnets
3 of 12 Sectors
2 magnets each
10 focusing quadrupoles per sector radially offset (~1 mm)
Reverse bends further reduce emittance
  ~1 mm offset of 10 QF per sector
High Field Bend Magnets allow generation of hard x-rays on intermediate energy ring
  3.2 T Permanent Magnet dipoles
high field bend

## Slide 28: ALS-U Integrated CAD model includes all mechanical scope of Project

## Slide 29: Injection / Extraction
AR
(commissioning)
SR

## Slide 30: Injection from the Booster (top-off) is based on a three pulsed-dipole kicker (3DK) scheme
Sector-12 straight
Sector-1 straight
Sector-2 straight
stored beam
Injected beam (from booster)
Main kicker
2nd pre-kicker
1st pre-kicker
Kickers are placed in three separate sectors (12, 1, and 2)
  1st and 2nd pre-kickers only affect the stored beam. The main kicker deflects both stored and injected beam.
  Pulsed thin + thick septum in sector 1 straight
For best injection efficiency the stored beam is left with a small, finite oscillation-amplitude past the main kicker
SEPTUM

## Slide 31: Simulations show injection efficiency > 95% over all lattice error realizations
3DK optimally set (by scan) based on lattice error realization
  No losses on the stored beam
These simulation do not include 3-4% possible additional degradation due to collective effects
  Likely to be less once wakes are included in full 3DK setting optimization
With additional losses through BTA (BTA magnet errors, beam jitter) injection efficiency estimated to above 90% for the largest majority of error realizations
Study of tolerance to thin-septum leakage fields
(on top of all other error sources)
specified tolerance
for leakage fields

## Slide 32: ALS-U Summary
CD-0
9/2016
CD-1
9/2018
CD-3A
12/2019
CD-2
4/2021
CD-3
FY23
CD-4 (Early Finish)
FY28
Scope:
New 2-GeV, high-brightness storage ring fed by a new full-energy accumulator ring and transfer lines in the existing ALS storage-ring tunnel
2 new full-length undulators
Suite of 2 new and 2 upgraded world-leading undulator beamlines
High-field bends and realignment of bend-magnet beamlines
Seismic and shielding upgrades of SR tunnel
Cost:
TPC of $590M (CD-2 approval 4/2021)
Schedule:
CD-3A approved 12/2019 for the early installation and commissioning of the accumulator ring and BTA prior to dark time
CD-2 approved 4/2021
CD-3 approved 11/2022
AR commissioning starts late 2025
Dark Period is FY26 (start 6/2026)
Early finish is early FY28 , >1 year of float to late finish
dark
time
Today