## Slide 1: Transverse beam instabilities in the SOLEIL II booster
Watanyu Foosang
watanyu.foosang@synchrotron-soleil.fr
Accelerator physics group
Synchrotron SOLEIL
I.FAST Workshop on Injectors for Storage Ring Based Light Sources
6-8 March 2024, KIT, Karlsruhe

## Slide 2: Outline
Introduction
Why study collective effects in the new booster
Booster model
Ramp model
Case study from the present booster
SOLEIL II booster model
SOLEIL II impedance model
Energy-dependent collective effects study
Transverse Single-Bunch Instabilities (TSBI)
Transverse Coupled-Bunch Instability (TCBI)
Conclusion and outlook
Design of the SOLEIL II booster
Previous talk of P. Schreiber

## Slide 3: Introduction

## Slide 4: Why study collective effects in the new booster
The new 7BA-4BA lattice of the SOLEIL II storage ring results in a much smaller dynamic aperture (DA) compared to the present ring.
The booster which serves as an injector to the SR also needs an upgrade to produce low emittance beam to be injected into the new DA.
The lattice design has evolved from simple FODO cells to 16BA lattice with stronger dipole field, quadrupole and sextupole gradients.
Emittance at extraction
Present booster
SOLEIL II booster
Close to the natural emittance of the present storage ring
(3.9 nm rad)
140 nm rad
5.2 nm rad
27 times smaller

## Slide 5: Why study collective effects in the new booster
To allow for the stronger magnets, the average vaccum chamber dimension will be reduced.
This immediately raised concern over the impedance, especially the resistive-wall (RW) type since
RW instability (RWI) growth time
Vaccum chamber radius
32 mm
22 mm
48 mm
52 mm
18 mm
52 mm
Present SOLEIL booster
SOLEIL II booster
Standard vacuum chamber sizes (to scale)

## Slide 6: Why study collective effects in the new booster
RWI growth time [1] :
Synchrotron radiation damping time :
To asses the importance of the resistive-wall instability (RWI), we calculated its growth time at the injection enegy and compared it to the synchrotron radiation damping time.
Stable beam when
[1] R. Nagaoka and K. L. F. Bane, J Synchrotron Rad 21, 937–960 (2014), https://doi.org/10.1107/S1600577514015215
Parameter | Estimated value | Stability condition | Condition satisfied
 | 1.4 ms | > 142 ms (beam passage time) | ❌
 | 31 s | < 1.4 ms ( | ❌
Threshold current | 0.6 A | > 6 mA (nominal current) | ❌
Parameter | Estimated value | Stability condition | Condition satisfied
 | 1.4 ms | > 142 ms (beam passage time) | ❌
 | 31 s |  | ❌
Threshold current |  | > 6 mA (nominal current) | ❌
Where is beam energy
Obtained by substituting in Eq. (1)
(1)
(2)

## Slide 7: Why study collective effects in the new booster
Particle vertical oscillation amplitude along the SOLEIL II booster ramp
Analytical RWI growth time and SR damping time along the ramp
Excited beam
Damped beam
Then, a simple exponential model was used to calculate the oscillation amplitude of a particle with energy ramp to take into account the energy dependence of and
where
It was found that the particle oscillation amplitude exhibited a large inflation along the ramp due to a competition between and .
This worrying result had brought us to a more sophisticated model by doing particle tracking simulation with energy ramp.
150 MeV
2.75 GeV
150 MeV
2.75 GeV

## Slide 8: Booster model

## Slide 9: Ramp model
Energy gain per turn
Energy loss per turn
Synchronous phase
Radiation damping time
Natural energy spread
Natural emittance
Start
Define equilibrium parameters at injection energy 150 MeV e.g.
Set and
Calculate then calculate
Calculate eq. parameters by scaling from the injection point, e.g.
End
Yes
No
Equilibrium parameters variation along the ramp
As shown previously that beam energy plays a significant role in estimating the beam instability since and , it is important to vary beam energy while doing particle tracking
Track particles with collective effects

## Slide 10: Ramp model
Equilibrium parameters along the ramp in SOLEIL II booster
Vrf max = 3 MV
Vrf inj = 164 keV
Dipole field and RF voltage ramp in SOLEIL II booster

## Slide 11: Case of the present booster
What else do I need to correctly model the booster?
Notes: To see which element is important to add in the booster model, we step back to take a look at the present booster.
However, we did not know much about how the present booster can work without instabilities even though its impedance is not at all optimized.
So we wanted to gather its data and use it the previously shown tracking model with energy ramp that I designed.
By doing this, I would know if there was something missing in my model if the results did not correspond the reality.
And also, this would help us know which element in the booster is crucial for fighting instabilities.

## Slide 12: Present booster model
Measured chromaticity along the ramp
Chromaticity
Positive chromaticity can:
Induce ‘head-tail damping’ which is favorable for coupled-bunch instabilities.
Decrease head-tail instability growth rate
ADTS coefficients along the ramp obtained from AT code
ADTS coefficients
Particle amplitude or Courant-Snyder (CS) invariant
Amplitude-Dependent Tune Shift (ADTS)
ADTS can prevent instabilities to build up since it induces incoherent tune spread in the beam which breaks the coherent behavior of the particles.
2nd order ADTS equation :
Re[]

## Slide 13: Present booster model
TCBI simulation results
It was found that the beam can indeed exhibit a large emittance blow-up along the ramp (blue line), but this behavior does not match the reality (green line)
Without ADTS, the blow-up gets even worse (orange line). So, the ADTS is necessary for the model.
This shows that the model was incomplete.
Vertical emittance along the ramp
Energy ramp
Chromaticity variation
RW impedance
Total charge = 3 nC (nominal multibunch charge)
ADTS
Model component
* All tracking simulations in this talk were by mbtrack2 [1,2]
[1] A. Gamelin, W. Foosang, and R. Nagaoka, Proc. IPAC’21 (2021), pp. 282–285,
https://doi.org/10.18429/JACoW-IPAC2021-MOPAB070
[2] mbtrack2, https://gitlab.synchrotron-soleil.fr/PA/collective-effects/mbtrack2

## Slide 14: Present booster model
To investigate this results, the ADTS was increased by a factor of 2 and 3 since it is possible that the ADTS in the model is underestimated.
A mock-up BBR was also added as an approximate impedance of all the special chambers whose model does not exist, so they were not taken into account in the model.
Only at ADTSx3 or when the nominal ADTS is present simultaneously with the BBR, the instability can be suppressed completely.
Vertical amplitude along the ramp with different combinations of ADTS and broadband resonator (BBR)
TCBI simulation results
Case study conclusion: essential elements for collective effect modeling
Broadband resonator parameters:
Energy ramp
Chromaticity variation
RW impedance
ADTS
Broadband impedance

## Slide 15: Moving back to the SOLEIL II booster

## Slide 16: SOLEIL II booster model
Coefficient | Value |  | C
 | SOLEIL (varied ) |  | SOLEIL II (
 | 1.73 GeV | At 2.75 GeV | 
 | -8.9 | 4.08 | -688
 | -18.0 | -23.25 | -491
 | -18.0 | -23.25 | -491
 | 26.54 | 14.05 | -604
Coefficient |  |  | C
 |  | At 2.75 GeV | 
 | -8.9 | 4.08 | -688
 | -18.0 | -23.25 | -491
 | -18.0 | -23.25 | -491
 | 26.54 | 14.05 | -604
Comparison of the ADTS coefficients in the two boosters computed from the AT code
Chromaticity
ADTS
* In reality, ADTS coefficients are different for each chromaticity since the sextupole strength is not equal. However, in this work, every chromaticity was estimated to have identical ADTS coefficients.
Constant throughout the ramp due to constant sextupole strength.
Also constant ADTS (for a given chromaticity*).
ADTS is much stronger in the new booster due to the stronger chromaticity correction.

## Slide 17: SOLEIL II booster model
Kicker chamber (3)
Existing elliptical chambers reused, 40 x 16 mm2
Ceramic chamber with 200 nm Ti coating, (amorphous structure from sputtering technique used for the deposition)
Tapers
Standard chambers
32 mm
22 mm
Elliptical chamber 32 x 22 mm2 (conservative H dim.)
Stainless steel 316LN ()
Present RF cavity reused.
Taper modeled as a frustum of a right cone, 300 mm long with an angle of 7.41°
RF cavity (2)
Present storage ring striplines reused
Stripline (2)
BPM (42)
New design Molybdenum ()
0.3 mm gap between the electrode and the BPM body.
Standard chamber
Preliminary impedance model

## Slide 18: SOLEIL II booster model
Total transverse impedance
The kicker chambers add a significant broadband impedance at around 450 MHz.
Vertical dipolar impedance (real part)
Vertical dipolar impedance (imaginary part)
Horizontal dipolar impedance (real part)
Horizontal dipolar impedance (imaginary part)
Zoom-in at low frequency part
Conclusion:
Sorted by max to min contribution (downward and L to R)
Overall, the kicker chambers contribute the most to the budget, but the resistive wall dominates the low frequency part which is important for multibunch instability.

## Slide 19: Energy-dependent collective effect study

## Slide 20: Single-bunch regime (without energy ramp)
TMCI Growth rate at 150 MeV at
Growth rate (s-1)
Bunch charge (nC)
Transverse mode-coupling instability (TMCI)
HTI Growth rate at 150 MeV at
Growth rate (s-1)
Bunch charge (nC)
Head-tail Instability (HTI)
ADTS does not have an impact on the threshold but does significatly reduce the growth rate
Growth rate reduces at higher chromaticity
ADTS also greatly reduce the growth rate.
This shows Landau damping effect in the booster

## Slide 21: Single-bunch regime (without energy ramp)
Stability diagram
Stability diagram of the SOLEIl II booster at 150 MeV
Growth rates in the low charge regime
Growth rate (s-1)
Growth rate (s-1)
Coherent tune shift ()
Landau damping cannot stabilize the beam with the nominal charge at the injection.
Emittance at injection :
The stability limit is approximately 75 – 200 pC which is lower than 500 pC (nominal charge) at every chromaticity.
75 – 200 pC
However, it cannot be concluded immediately if the beam will be stable throughout the ramp. Simulations with an energy ramp then needs to be pursued.
Nominal charge
Bunch charge (pC)
Landau damping limit

## Slide 22: Single-bunch regime (with energy ramp)
A beam with the nominal charge is in fact stable throughout the ramp.
Transverse single-bunch instabilities (TSBI) along the ramp
1.5 nC (maximum single-bunch charge) with ADTS
V emittance (m.rad)
Turns
V emittance (m.rad)
Turns
0.5 nC (nominal single-bunch charge) with ADTS
Conclusion:
Could be the loss of Landau damping due to the beam size reduction (reducing the tune spread for the same ADTS coefficients)
To be investigated
For the maximum charge, only chromaticity 5 can suppress the instability at low energy.
An unexpected sawtooth feature at high energy was discovered for chromaticities 3-5.

## Slide 23: Multibunch regime (with energy ramp)
Transverse coupled-bunch instability (TCBI) driven by RW impedance [1]
Conclusion:
Vertical emittance without ADTS
Vertical emittance with ADTS
  On the contrary, the beam withtout ADTS would not be stable at low chromaticity: for 3 nC and either or for 10 nC to be stable.
Simulations with energy ramp were also performed for TCBI to confirm the stability throughout the ramp at
3 nC (nominal multibunch charge)
10 nC (maximum achievable charge)
  The beam at both charges are indeed stable all along the ramp when ADTS is present.
[1] More about this topic: W. Foosang et al, J. Phys.: Conf. Ser. 2687 062017 (2024), https://doi.org/10.1088/1742-6596/2687/6/062017

## Slide 24: Conclusion

## Slide 25: Conclusion
It has been shown that
ADTS and broadband impedance are key elements for accurate modeling of collective effects in boosters.
Tracking with energy ramp is important to determine beam’s stability throughout the ramp.
Conclusion from the SOLEIL II project’s aspect
Single-bunch regime
  The beam is stable throughout the ramp at nominal charge (0.5 nC) for positive chromaticity.
  Possible stability issue for maximum charge (1.5 nC), to be investigated.
Multibunch regime
  The beam is stable up to 10 nC (maximum charge) for positive chromaticity.
Cost optimization: collective effect study can help optimize the construction cost of the machine by neglecting unneccessary impedance optimization (tapers, RF fingers, pumping grid etc.).
Bottom line:
SOLEIL II booster is safe from TMCI, HTI, and RW instability at the nominal charge.

## Slide 26: Thank you for your attention

## Slide 27: Back-up slides

## Slide 28: Outlook
Next steps
New impedance model following the advance of mechanical design.
Use of different ADTS coefficients according to the chromaticity​.
Investigate the sawtooth feature at the end of the ramp of the single-bunch simulation.
Add physical aperture in tracking.

## Slide 29: In the present booster
Energy deviation is adjusted via RF frequency :
Betatron tunes along the present booster’s ramp at various energy deviation
Horizontal tune
Vertical tune
Chromaticity
To obtain the chromaticity along the ramp in the present booster, a measurement of the betatron tune along the ramp at various energy deviation was conducted.

## Slide 30: In the present booster
However, due to the inconstant in the horizontal plane after 100 ms, the chromaticities vary by a large amount from this point until extraction.
Between 0-100 ms, the sextupole strength in both planes ramps up accordingly to the beam energy resulting in a constant normalized sextupole force and thus fairely constant chromaticities.
Chromaticity & ADTS

## Slide 31: In the present booster
ADTS
Present booster’s ADTS coefficients along the ramp calculated using the real chromaticity variation
As a consequence of the inconstant , the ADTS coefficients vary after 100 ms (1.73 GeV) in the present booster.
Coefficient | value | 
 | 1.73 GeV | At 2.75 GeV
 | -8.9 | 4.08
 | -18.0 | -23.25
 | -18.0 | -23.25
 | 26.54 | 14.05
Coefficient |  | 
 |  | At 2.75 GeV
 | -8.9 | 4.08
 | -18.0 | -23.25
 | -18.0 | -23.25
 | 26.54 | 14.05
The ADTS coefficients were then determined from element-by-element tracking in Accelerator Toolbox (AT) code.