## Slide 1: What can radars tell us about snowfall microphysics? Insights from a MCMC approach
Anne-Claire Billault-Roux1,2 and Alexis Berne1
1 Environmental remote sensing lab, EPFL, Lausanne, Switzerland
2Now at MeteoSwiss, Payerne, Switzerland
1st PrePEP conference, March 2025

## Slide 2: The radar Doppler spectrum
Doppler spectrum: radar reflectivity as a function of Doppler velocity
Vertically-pointing radar
Faster-falling particles
At a given time & height
Microphysical properties
￫ scattering, aerodynamics…
Radar properties
￫ wavelength, beam width…
Atm. dynamic processes
￫ turbulence, wind…
1

## Slide 3: Multi-frequency Doppler spectra
Rayleigh/non-Rayleigh scattering regimes: more info on PSD
  ‘Small’ particles: sZeX ≈ sZeKa ≈ sZeW
  ‘Large’ particles: sZeX > sZeKa > sZeW
2
Doppler velocity [m s-1]
Spectral Ze [dBsZ]
Faster-falling particles
W
Ka
X

## Slide 4: Question: how much microphysical info is contained in these data?
3
full PSD?
PSD parameters?
density?
mass-size relation?
orientation?
geometry?
aspect ratio?
area-size relation?
…
Doppler velocity [m s-1]
Spectral Ze [dBsZ]
Faster-falling particles
W
Ka
X

## Slide 5: Approach: retrieve posterior distributions using MCMC
Given a set of triple-freq. Doppler spectra, what is the underlying distribution of microphysical descriptors that can explain the observations (posterior distribution)?
  Uncertainty quantification
  Sensitivity tests (e.g., impact of atmospheric broadening, of modelling choices…)
  Assess reasonable assumptions for operational retrievals
4

## Slide 6: Approach: retrieve posterior distributions using MCMC
Given a set of triple-freq. Doppler spectra, what is the underlying distribution of microphysical descriptors that can explain the observations (posterior distribution)?
  Uncertainty quantification
  Sensitivity tests (e.g., impact of atmospheric broadening, of modelling choices…)
  Assess reasonable assumptions for operational retrievals
Markov chain Monte Carlo (MCMC): Bayesian retrieval framework
  Few mathematical assumptions on retrieval problem / error distributions
  Retrieval of full posterior distributions
  Too slow for use on large datasets
4

## Slide 7: Framework
MCMC, Metropolis-Hastings: iterative algorithm, based on a chain of accept/reject decisions; leading to sample full posterior distribution.
Specific choices:
  Adaptive proposal
  Parallel tempering needed in some settings
  Prior: uniform (bounds from literature)
5
Illustration: Tomic et al. 2019

## Slide 8: Framework
Simulations of radar spectra using PAMTRA (Mech et al, 2020)
  Frequencies: X + Ka + W bands
  Scattering: Self-similar Rayleigh-Gans approximation (SSRGA, Hogan and Westbrook 2014)
  Velocity-size: Heymsfield 2010
Microphysical descriptors retrieved:
  PSD shape: Gamma (prescribed through , µ, )
  Mass-size relation: , (correlated in prior)
  Area-size relation: , (correlated in prior)
  Turbulent broadening and radial wind shift: EDR, vr (ON/OFF)
Analysis conducted on 10 simulated examples of triple-freq. spectra (representative)
6

## Slide 9: Baseline retrieval: first outcomes
7
: narrow + ‘differentiated’ posterior
: same (but log…)
µ: wide / ‘flat’ posterior
: ‘non-specific’ posterior

## Slide 10: Sensitivity to retrieval parameters
Atmospheric effects (turbulence + radial wind): wider and biased posterior
Number of frequencies: single freq = uncertainty ++; dual-freq = worse if X+Ka only
Using ‘wrong’ SSRG coefficients: minor impact
Using ‘wrong’ mass/size relation: biased posterior
Using ‘wrong’ PSD shape (µ): wider and biased posterior
8

## Slide 11: Sensitivity tests: mass-size relation
9
Knowing true , reduces posterior width
  e.g., - 40% IQR0.1-0.9 in
Assuming wrong , (e.g., Brown and Francis 1995) leads to biased posterior
  e.g., +20% mean in , -100% mean in µ
  sometimes quasi-disjoint distributions
Ex S9

## Slide 12: The case of bimodal Doppler spectra
10
Bi-(multi-)modal spectra measured when different hydrometeor populations co-exist in radar volume
Using MCMC framework: retrieval of 2 ice populations and compare to baseline
Impact of bimodal “separation” on retrieval quality?

## Slide 13: The case of bimodal Doppler spectra
11
In some cases, distributions retrieved with similar accuracy than baseline
Peak separation plays a great role in retrieval ability
Jensen-Shannon distance w.r.t. baseline

## Slide 14: The case of bimodal Doppler spectra
12
Peak separation: quantified with prominence index (mean ratio of peak prominence) <-> related with mean JSD
=> shows information content accessible in multi-peaked spectrum

## Slide 15: Conclusion
MCMC framework on examples of simulated multi-frequency radar Doppler spectra
  Few mathematical assumptions
  Retrieval of full posterior distributions
  Too slow for operational use
13

## Slide 16: Conclusion
MCMC framework on examples of simulated multi-frequency radar Doppler spectra
  Few mathematical assumptions
  Retrieval of full posterior distributions
  Too slow for operational use
Insights gained
  Information content: different level of confidence depending on variable ( ≠ µ)
  Sensitivity tests: certain common assumptions can be misleading (e.g., a/b, PSD shape)
  Bimodal spectra: prominence index indicates possibility for accurate retrieval
13

## Slide 17: Conclusion
MCMC framework on examples of simulated multi-frequency radar Doppler spectra
  Few mathematical assumptions
  Retrieval of full posterior distributions
  Too slow for operational use
Insights gained
  Information content: different level of confidence depending on variable ( ≠ µ)
  Sensitivity tests: certain common assumptions can be misleading (e.g., a/b, PSD shape)
  Bimodal spectra: prominence index indicates possibility for accurate retrieval
Perspectives
  Sheds light on intrinsic uncertainties
  Using statistical emulators in view of applications on larger datasets
13

## Slide 18
Thank you!

## Slide 19: Baseline retrieval: bivariate analyses
Certain correlations come from prior (a/b, /)
/: expected
Others to be explored

## Slide 20: Sensitivity tests: SSRG example
Assuming a set of SSRG coefficients different than the true one (i.e., used for original simulation): only minor impact on retrieved posterior
Depending on SSRG coefs, bias in and
Ex S6

## Slide 21: Sensitivity tests: PSD shape
Knowing true µ reduces posterior width (but not drastically)
Assuming wrong µ (e.g., exp. PSD) leads to wider and biased posterior
  e.g., +80% IQR0.1-0.9 , -10% mean , on average
  sometimes quasi-disjoint distributions
Ex S10

## Slide 22: Sensitivity tests: atmospheric effects
Turbulent broadening: leads to wider posterior and bias
  e.g. +30% in IQR0.1-0.9 for on average
But if turbulence is known: no impact on posterior (no intrinsic loss of information in spectra)
Turb known
Turb unknown
Turb known
Turb unknown
Turb known
Turb unknown
Turb known
Turb unknown
Turb known
Turb unknown
Ex S3

## Slide 23: Sensitivity tests: atmospheric effects
Radial wind: leads to wider posterior and bias
  e.g. +40% in IQR0.1-0.9 for on average
Similar effect if uniform vertical wind (same for 3 radars) or radar misalignment (differential radial wind)
Ex S1