## Slide 1: Reinforcement Learning for Laser Alignment
RL4AA Workshop 2025, DESY
Matthew B. Schwab
April 4th, 2025

## Slide 2
Helmholtz-Institute Jena
JETi200
Target Area Fraunhofer (TAF)
POLARIS
Lots of opportunity for optimization and automation!
Notes: At the HI Jena, we are currently upgrading our Polaris laser and building the infrastructure to combine it with another several 100 TW laser, the Jeti 200, in a new and larger target area. My project is to look into how we can automate some of the alignment procedures on the Polaris laser

## Slide 3
Polaris Laser
I. Tamer, Diss. 2020
Laser plasma acceleration
Nonlinear interactions
  LWFA, TNSA, etc.
Stable laser parameters save:
  Time
  Data
  Money
  Frustration
A. Sävert, Diss. 2016; G. Becker, Diss. 2021
Notes: This is a block diagram of the Polaris laser, a double CPA system
Just like large high energy particle accelerators, high power lasers consist of several amplifiers in a chain.
The experiments we perform with such lasers, like LWFA and TNSA, are highly nonlinear, so stable laser parameters save a lot of time, data, money, frustration

## Slide 4
Polaris Laser
I. Tamer, Diss. 2020
Variation in laser energy
Long-term drift
Shot-to-shot
Causes
Temperature
Humidity
Vibration noise
Who aligns the laser
Notes: Unfortunately, if we look at one of our first amplifiers as an example, there is both a long-term drift and a shot-to-shot variation of the amplifier’s output energy. Caused by…
Drift can be so significant, that the previous references for optimal laser energy no longer give an optimal laser energy, nonstationary problem
Process of manual realignment in an experiment takes time (radiation safety)

## Slide 5
Agent performs Mirror Tip/Tilt Alignment
Two Main Objectives
  Control of Input Alignment (Input)
  Control of Cavity Alignment (EM)
Easy
  Align to the previous beam position references
Hard
  Find new optimal alignment for laser energy
Extra Hard
  Use inferior stepper motors….
Reinforcement Learning: Goal
Notes: Schematic of a regenerative amplifier on which the agent will perform mirror alignment
Ability to automate the realignment/optimization of optical systems has potential to save a lot of time, both in operation of the laser and in analysis of experimental results (due to improvement in laser stability)
System should use existing stepper motor control and normal NF, FF diagnostics (CCDs)
Pilot-laser + Quadrant detectors is standard, but not wanted here because of timing with Pockel’s cell/ Polarization system

## Slide 6
Motivation/Background
Reinforcement Learning Basics
Gymnasium Environment
NF/FF and NF/FF + Energy
Hyperparameter Tuning
Real2Sim Gap
Simulation Methods
NF/FF Results
Next Steps
Outline

## Slide 7
Map Two Mirror System to RL Scheme
x
y
z
M1
M2
NF
FF
P
D
Agent
Environment
State
Actions
Observables & Reward
At
St
Rt
St+1
Rt+1
Un/Observables
Simulation necessary for training
1 Hz and 1/50 Hz rep. rates of laser
Notes: Necessary then to map the tip/tilt-based optical systems of our laser onto the Markov Decision Process Framework
Need to use a simulation of the optical setup, because the actual laser runs at 1Hz repetition rate, which is slow for training

## Slide 8
Python: Gymnasium Environment
Unobservables
  Reset at start of each episode (Domain Randomization)
  P = [Px,Py,Pz], start position of ray
  D = [Dx,Dy,Dz], start direction of ray
  Absolute mirror orientations
  Optimal energy axis
Observables
  Near-field position of laser [NFx, NFy]
  Far-Field position of laser [FFx,FFy]
  Normalized time
  Motors’ change of direction
Actions
  S = [S1x,S1y,S2x,S2y], relative # of steps to be driven by each motor
Reward
  Various schemes
  Measure of distance from NF and FF references
  Measure of laser energy
Truncation
  Terminal state for condition outside of MDP
Termination
  Terminal state for condition inside of MDP
  # of laser shots = episode_length
  Optimal Energy found and kept
Extra code for calculating the ray tracing
x
y
z
M1
M2
NF
FF
P
D
Optimal
Energy

## Slide 9
Reward Scheme: NF/FF
For alignment to NF/FF references
Metric: Tx = (1-RNF,norm )N * (1-RFF,norm)N
Continuous Reward [0,1]
RL solves this easily (without Backlash)
  Even with domain randomization of
    Input ray position
    Input ray direction
    Mirrors’ starting orientations
NF
FF
Tx
Notes: Summation instead of product?

## Slide 10
Reward Scheme: NF/FF + Energy
For finding optimal laser energy
Metric: Tx = (1-RNF,norm )N * (1-RFF,norm)N
  Now scaled with maximum < 1
On reset(), optimal energy’s position shifts relative to NF/FF reference
  Mimics long-term drift
  Max energy 1.0
  Gaussian (FWHM based on lab)
  Position shift (based on lab)
NF
FF
Optimal
Energy
Notes: Talk about ray tracing later because we need to know about the Sim2Real gap

## Slide 11
Hyperparameter Search
Hyperparameters (non-learned parameters in PPO algorithm)
  Number of neurons per hidden layer in Agent’s NN
  Number of neurons per hidden layer in State Value’s NN
  Number of hidden layers in Agent’s NN
  Number of hidden layers in State Value’s NN
  Optimization function
  Activation function in Agent’s NN
  Activation function in State Value’s NN
  Base Learning Rate
  Multiplier
  Sub-batch size
  Max gradient norm
  Number of epochs
  PPO loss clip
  Entropy epsilon
  Episode length
  Reward discount
  Trajectory discount
  Total training iterations
18 Parameters: 318 = 387 million combinations to test!
DO NOT USE GRID SEARCH!, use Tuning software

## Slide 12
Hyperparameter Search: Optuna
Hyperparameter Importance

## Slide 13
Hyperparameter Search: Optuna
Parallel Coordinates Plot

## Slide 14
Hyperparameter Search: Optuna
Parallel Coordinates Plot

## Slide 15
Test Bench
Trained agents first tested here before use on actual laser amplifier
M1
M2
NF
FF
Laser
~500 mm

## Slide 16
Sim2Real Gap
Shot-to-Shot variation (pointing + energy)
  Simulation – values constant over episode
  Real – everything varies (take averages)
Accurate motion of mirrors and motors
  Rotation or Rotation + Translation
  “Cross-talk”, drive motor in x, beam moves in y
  Backlash/Hysteresis of motor + mirror mount
    Add direction change to observables
Measurement noise
  Mechanical Vibration
  CCD Noise
  Dirt on CCD/Filters
  Non-Gaussian Laser Profile
  Pulse energy measurement
Synchronization of Data
NF/FF
Notes: Except for last bullet point, all of these things could be included in the simulation to improve Agent‘s performance, but you can‘t always accurately simulate everything

## Slide 17
Backlash Calibration
Calibrated all four motor/mount pairs
Not ideal for back and forth alignment in small step size range….
Env(): Normal distribution created for every step size
  Sampled in simulation to simulation real motor/mount

## Slide 18
Ray Tracing vs. Ray Transfer Matrix
Ray Tracing
Pros
  Flexibility
  Domain Randomization
  Avoid nonlinear set point
Cons
  Slow for complicated system
  Hard to model real world
    Motor/Mirror-mounts
    Optical layout
    Manufacturing errors
Ray Transfer Matrix
Pros
  Uses real data to calibrate
    Rotation + Translation
    Motor cross talk
    Geometry “built-in”
Cons
  Nonlinear system, need set point
  Can’t model laser cavity properly

## Slide 19
Results on Test Bench: NF/FF
Evaluation During Training
Notes: 241115

## Slide 20
Results on Test Bench: NF/FF
NF
FF
Notes: 241115
1% error is 2.5 pixel

## Slide 21
Results on Test Bench: NF/FF
New reward scheme (max Return = 100)
Terminate for Tx > Threshold over 4 consecutive shots
A few other changes…
Evaluation During Training
Notes: 250201 r036

## Slide 22
Results on Test Bench : NF/FF
NF
FF
Notes: 250201 r036
1% error is 2.5 pixel

## Slide 23
Regenerative Amplifier
Currently installing, calibrating and testing…
Input FF
Input NF
Input
Cavity
Cavity NF
Cavity FF
EM
EM
M1
M2
Output

## Slide 24
Next Steps
Currently calibrating/testing on regenerative amplifier
Prevent oscillatory behavior
Simulation of laser cavity
Other Improvements
Thank you for your time!
Me
Audience’s
State
Presentation
Observables & Reward
At
St
Rt
St+1
Rt+1
Applause, Boos,
Questions, Sleeping