## Slide 1: Do citizen science data improve the reconstruction of heavy rainfall events?
Opportunistic Sensing of Precipitation
Offenbach, 26.06.2025
H. Müller-Thomy, F. Meyer, K. Schröter
Leichtweiß-Institute for Hydraulic Engineering and Water Resources
Div. Hydrology and River Basin Management

## Slide 2
Data
Studied rainfall event
Storm Lambert (single rainfall event)
Braunschweig, Germany (205 km²)
Start: 22.06.2023, 18:00 CET
End: 23.06.2023, 18:00 CET
Notes: DWD German Weather Service
BS Municipal Wastewater management
Quality checks: Double sum analysis, number of missing values

## Slide 3
Data
Studied rainfall event
Storm Lambert (single rainfall event)
Braunschweig, Germany (205 km²)
Start: 22.06.2023, 18:00 CET
End: 23.06.2023, 18:00 CET
Station data
DWD: 1 station
Citizen Science: 8 stations
BS (incl. LWI): 9 stations
Radar data:
  YW data set (downscaled RADOLAN)
4 stations
8 stations
Simple quality checks
Notes: DWD German Weather Service
BS Municipal Wastewater management / NOT accessible
CS / accessible
Quality checks: Double sum analysis, number of missing values

## Slide 4
Methods
Regionalization Rainfall amount 22.06., 19:00-19:10
DWD
Radar
All Stat - NN
All Stat – IDW-Q
All Stat – OK
Regionalization | Event rainfall amount [mm/24h] |  |  |  |  | 
 | DWD | Radar | BS | BS+DWD | CS | ALL_Stat
NN | 72 | 69 | 133 | 132 | 98 | 125
IDW |  |  | 130 | 126 | 90 | 115
IDW_Q |  |  | 133 | 131 | 98 | 127
OK |  |  | 128 | 121 | 91 | 113
OK_Q |  |  | 130 | 129 | 98 | 124
Data set choice is more important than regionalization technic!
Notes: Cross-validation: The data set validated is assumed as truth and by leave-one-out evaluated

## Slide 5
Return period [yrs]
Rainfall amount [mm]
Extreme value analysis based on KOSTRA2020
Raster-based extreme value analysis for Germany
Durations: D={5, 10, 15, 20, 30, 45, 60, 90 [min], 2, 3, 4, 6, 9, 12, 18, 24 [h]}
Return periods: T={1, 2, 3, 5, 10, 20, 30, 50, 100 [a]}
Methods
Return period
(Junghähnel et al., 2022; Shehu et al., 2023)
→ For all durations D the maximum value for each raster field was classified.
→ 12 KOSTRA raster cells for Braunschweig enable spatial return period estimation
Notes: national extreme value catalogue
Example OK-BS

## Slide 6
Results
Return period
Fraction [%]
Fraction [%]
Raster-based extreme value within the event
Spatial return period estimation
Notes: national extreme value catalogue

## Slide 7
Results
Return period
DWD & YW:
TG(10min) = 1 yr & <1 yr
TG(1440 min) = 20 yrs
Fraction [%]
Fraction [%]
Fraction [%]
Duration [min]
Duration [min]
BS & BS+DWD (‘conventional measurements’):
TG(10min) = 30 yrs
TG(1440 min) = 100 yrs
CS :
TG(10min) = 5 yrs
TG(1440 min) = 50 yrs
Notes: national extreme value catalogue

## Slide 8
Conclusions
Citizen science data:
Enrich rainfall information and are easily accessible
Add spatial detail which outweighs limited measuring accuracy
With simple quality checks only slightly less accurate than conventional measurements
@hydriv@mas.to
  @HydroHannes
@hydriv-lwi
Thank you for your attention!

## Slide 9
DO IT! Digitization of analogue records in time
doit-lwi.tu-bs.de
Opportunistic sensors will improve
the precipitation data situation…
…in the meanwhile in the archives:
Help us to digitize historical records - only a few minutes by everyone will add centuries of records to our precipitation data!
Questions & feedback?
h.mueller-thomy@tu-bs.de

## Slide 10
Methods
Regionalization Rainfall amount 22.06., 19:00-19:10
Cross-validation via RMSE:
(truth := data set studied)
DWD
Radar
All Stat - NN
All Stat – IDW-Q
All Stat – OK
Method
Data set
CS less peaky than ALL_Stat
Notes: Cross-validation: The data set All_Stat is assumed as truth and by leave-one-out evaluated
Bias is smallest for all data sets using OK

## Slide 11
Shehu, B., Willems, W., Stockel, H., Thiele, L.-B., Haberlandt, U. (2023): Regionalisation of rainfall-dept-duration-frequency curves with different data types in Germany, Hydrol. Earth Syt. Sci. 27, 1109-1132, doi.org/10.5194/hess-27-1109-2023.
Junghänel, T., Bär, F. , Deutschländer, T., Haberlandt, U., Otte, I., Shehu, B., Stockel, H., Stricker, K., Thiele, L.-B., Willems, W. (2022): Methodische Untersuchungen zur Novellierung der Starkregenstatistik für Deutschland (MUNSTAR), Synthesebericht. 95 pp.
References
Notes: Transition probabilities extended by position and volume dependencies