## Slide 1: Beam-based girder alignment in PETRA-IV
Sajjad H. Mirza for the PETRA IV WP2.08 team
Karlsruhe, 19.03.2025
Conceptual simulations

## Slide 2: PETRA III is one of the core facilities at DESY
Each year ~5000h users operation serve more than 2000 users
Max von Laue Hall
Paul P. Ewald Hall
Extension Hall North
Ada Yonath Hall
Extension Hall East
Parameter | PETRA III
Energy [GeV] | 6
Circumference [m] | 2304
Emittance (hor./vert.) [nm] | 1.3 / 0.013
Total current [mA] | 100
PETRA IV project:
replacing PIII with an ultra-low emittance ring (20 pm), adding a new Experimental Hall in two more octants,
replacing DESY II with a new low emittance booster
PETRA III emittance 1300 pm
PETRA IV emittance 20 pm
65 times smaller
enabling 500 times larger
X-ray beams brightness

## Slide 3: FOFB parameters
FOFB: Machine Parameters & Beam Stability Requirements
Parameter | Value
Circumference | 2.3km
Number of BPMs (x/y) | 790
Number of fast correctors | 560 (244H, 316V)
Betatron freq. (fx / fy) | 23.4 kHz / 35.2 kHz
Synchrotron oscillation | 100 Hz for 3rd harmonic cavity
at ID, standard cell (29) | 2.2 m, 2.2 m
at ID, flagship IDs (7) | 4 m, 4 m
Natural emittance | 20 pm rad, 4 pm rad
Beam size at ID, standard cell | 6.6 µm, 2.97 µm
Beam size at ID, flagship IDs | 8.9 µm, 3.98 µm
Beam divergence at ID, standard cell | 3.02 µrad, 1.34 µrad
Beam divergence at ID, flagship IDs | 2.23 µrad, 1.0 µrad
Parameter | Value
Circumference | 2.3km
Number of BPMs (x/y) | 790
Number of fast correctors | 560 (244H, 316V)
Betatron freq. (fx / fy) | 23.4 kHz / 35.2 kHz
Synchrotron oscillation | 100 Hz for 3rd harmonic cavity
 | 2.2 m, 2.2 m
 | 4 m, 4 m
 | 20 pm rad, 4 pm rad
 | 6.6 µm, 2.97 µm
 | 8.9 µm, 3.98 µm
 | 3.02 µrad, 1.34 µrad
 | 2.23 µrad, 1.0 µrad
Beam stability requirements:
Typically 10% of beam size and divergence at the IDs.
Remark: Some beamlines may require even 5%, 3%, … in future?

## Slide 4: Slow and fast correctors in lattice
Fast corrector magnets = 244 in X-plane
Fast corrector magnets = 316 in Y-plane
Slow corrector magnets = 618 in X-plane
Slow corrector magnets = 618 in Y-plane
Overlap of slow and fast magnets
Higher net corrector strengths for the fast magnets due to combined slow/fast action – space constrains
based upon commissioning simulations
FOFB regime
SOFB regime
Planned strategy: Single FOFB system (Quasi-DC to high frequency)
Slow correctors for machine setup and large static correction
DC download from fast correctors to slow correctors
Slow and fast correctors have overlapped locations in lattice
Expected corrector strength budget
Notes: First we see the distribution of corrector magnets in the lattice. One cell is shown here alongwith beta function and phase advance.
We see less number of corrector magnets in horizontal plane  based upon machine physics simulations for optimal phase advance.
Although from our side, 30 urad maximum corrector strengths looks enough, but there are certain locations where slow/fast magnets are identical.
So a maximum of 600 urad corrector magnets are required.

## Slide 5: Why higher slow corrector strengths
Overlap of slow and fast magnets
Courtesy to T. Hellert (MPY)
Fast corrector magnets = 244 in X-plane
Fast corrector magnets = 316 in Y-plane
Slow corrector magnets = 618 in X-plane
Slow corrector magnets = 618 in Y-plane
No. of Girders = 288
Below shown the corrector strengths required for girder misalignment
One major contributor to large slow corrector strengths is
large girder misalignment  Heritage from PETRA I
Slow and fast correctors have overlapped locations in lattice
33 % reduction
For Girder offsets
For Girder offsets
Talk: Normann Koldrack
Notes: First we see the distribution of corrector magnets in the lattice. One cell is shown here alongwith beta function and phase advance.
We see less number of corrector magnets in horizontal plane  based upon machine physics simulations for optimal phase advance.
Although from our side, 30 urad maximum corrector strengths looks enough, but there are certain locations where slow/fast magnets are identical.
So a maximum of 600 urad corrector magnets are required.

## Slide 6: Heritage from PETRA I
PETRA I tunnel reused for PETRA IV
PETRA IV Tunnel
Outside the experimental halls the old PETRA I tunnel will be reused
5 old sections, 100 – 300m long, in total ~800m.
The old sections of the tunnel are below streets and buildings.
The tunnel is covered by 3 – 10 m of soil.
Tunnel access at the halls, every 300m.
Tunnel between PXW and RF building will be rebuild (part of a construction package).
DESY
West
Ost
NW
SO
SW
NO
NL
NR
OL
OR
NWR
NOR
SOL
NOL
SOR
SL
SR
Süd
SWL
SWR
WL
WR
NWL
Nord
FLASH
Linac II
PIA
L-Weg
E-Weg
P-Weg
e-
PXW*
RF hall*
Tunnel NW-N*

## Slide 7: PETRA III Tunnel segment movements: Temperature effects
Relative movement of neighboring Tunnel segments (only one example of many possible scenarios)
Mechanical measurements at cracks (2020)
Typical temperature changes 23º – 36º C
Typical movements over one year (2020):
Units: Micro meter
x, horiz.: 50 - 100 µm, black, blue, red curve, temp. stabilized
x, horiz.: 150 µm, green curve, not temperature stabilized (this is above the alignment tolerances of PETRA IV!)
Long term transvers movements are dominated by the outside temperature.
Assumption: Reducing the temperature changes by a factor of 10 would reduce the short term movements by a factor of ~10 and make them tolerable.
Variation ~ 150µm,
not temperature stabilized
50 – 100 µm,
temperature stabilized
Temperature variation in 2020
Relative movement of horizontal
tunnel segment in 2020
OR59
OR59
SOR85
Notes: Tunnel segments experience significant movement (up to 150 µm) driven by temperature changes.
Mitigation via improved temperature stabilization could reduce movements to acceptable levels.

## Slide 8: Slow/fast combined corrector parameters
Based upon APS-U design
Overlap of slow and fast correctors lead us (FOFB system) to interfere in
Optimization of fast corrector magnet design (Sven’s talk)
DC current downloading from slow magnets to Girder alignment (this talk)
Baseline parameters:
  Main/aux coil is 65/27 turns (2.4074)
  Coil current 15 A
  Self-inductance 23 mH
Main coils
Auxiliary coils
WP2.02
First prototype
Notes: First we see the distribution of corrector magnets in the lattice. One cell is shown here alongwith beta function and phase advance.
We see less number of corrector magnets in horizontal plane  based upon machine physics simulations for optimal phase advance.
Although from our side, 30 urad maximum corrector strengths looks enough, but there are certain locations where slow/fast magnets are identical.
So a maximum of 600 urad corrector magnets are required.

## Slide 9: Beam-based girder alignment
What is the concept?
First download 
Fast correctors strengths fast ORM BPM space
BPM space slow ORM  Slow corrector strengths
Second download 
Slow correctors strengths slow ORM BPM space
BPM space Girder ORM  Girder alignments
Hard to measure, we have to rely on model!
Girder ORM is calculated by misaligning the start and end of each girder separately and recording the orbit deviation at all BPMs.
For 288 Girders and 790 BPMs, the Girder ORM has a size of per plane.

## Slide 10: Assumed misalignments
Girder misalignments  corrector relaxation to Girder movements
Errors | 1 σ (cut at 2σ)
Random Girder misalignments of start and end points | 
Random Magnet misalignments | 
Random BPM offset | after BBA
BPM calibration errors | 
Corrector calibration errors | 
Errors | 1 σ (cut at 2σ)
Random Girder misalignments of start and end points | 
Random Magnet misalignments | 
Random BPM offset | 
BPM calibration errors | 
Corrector calibration errors | 
Such large alignment errors cannot be applied directly to PETRA IV lattice  commissioning simulations
For this study, the errors were ramped in small steps and orbit correction was performed for each step (work around)

## Slide 11: Slow corrector relaxation to Girders
Girder misalignments
Required corrector strengths
Achieved orbit correction at BPMs
Predict Girder
alignmnets

## Slide 12: Slow corrector relaxation to Girders
Girder correction applied
Reduced corrector strengths
Tikhonov regularization for Girder ORM inverse
Achieved orbit correction at BPMs

## Slide 13: Rolling the dice many times: simulation for 72 machines
Simulations extended to 72 random misalignment patterns of girders and magnets etc.
Cumulative distribution function (CFD) is calculated for girder misalignment, slow corrector strengths and BPM values for all machines!  and compared before and after girder alignment
Don’t ask please about
this Golden Number of 72 
CDF =
CDF calculation:
1- Combine all data points of one variable from different machines into a single dataset
2- Sort the data in ascending order
3- CDF of a given value in the data e.g. for girder misalignment is:
Example 

## Slide 14: Slow corrector relaxation to Girders  for 68 of 72 random machines, 4 failed
Tikhonov regularization for Girder ORM inverse

## Slide 15: Girder movement histogram
Tikhonov regularization for Girder ORM inverse
Single machine
68 machines
The net movement required for each Girder end is plotted here
Left: for one machine Right: for 68 machines as histogram

## Slide 16: Girder alignment in feedback fashion
With aggressive correction, the girder correction diverges
RMS of girder alignment, corrector strengths and BPM values are plotted below at different iteration of feedback. (no information about controller type etc. )

## Slide 17: Girder alignment in feedback fashion
Let us include only Girder misalignment as source of errors, for comparison.
After certain iterations, magnet misalignment dominates as main source of errros

## Slide 18: Summary
Reuse of PETRA I tunnel for PETRA IV (with some improvements) comes with challenges of relatively large tunnel segment movements.
Space constrains require combined slow and fast corrector magnets.
Large slow corrector strengths are required to cope with accepted girder misalignments for PETRA IV.
Simulations are performed to demonstrate the possibility of beam-based girder alignment of the PETRA IV.

## Slide 19
Sajjad H. Mirza
WP 2.08 - Feedback
sajjad.hussain.mirza@desy.de
+49 40 8998 - 1991
Thank you