## Slide 1: Introduction of KARA Storage Ring
Akira Mochihashi, 19.03.2025

## Slide 2: Karlsruhe Research Accelerator (KARA)
          KIT synchrotron light source & accelerator test facility
Parameters | Values
Circumference | 110.4 m
Energy range | 0.5 – 2.5 GeV
RF frequency | 499.7 MHz
Revolution frequency | 2.715 MHz
Harmonic number | 184
Beam current | up to 200 mA
r.m.s. bunch length | 45 ps (2.5 GeV) a few ps (1.3 GeV, low-alpha)
Lattice structure | DBA
Injection at 500 MeV
User Operation at 2.5 GeV
Non-Top-Up Machine

## Slide 3: Lattice Functions at KARA
Results by OPA
One superperiod = 1 long straight + 1 short straight + 2 gaps of separated bends
KARA … four-folded structure

## Slide 4: Quadupole Families at KARA
          Quadrupoles: Five-Family Configuration
Family name | Main function | Location and total number
Q1 | Horizontal-quads | The first-Q at long straight: 8
Q2 | Vertical-quads | The second-Q at long straight: 8 (up- and downstream of the first bend)
Q3 | Horizontal-quads, dispersion control | In the gap of separated bends: 8
Q4 | Vertical-quads | The first-Q at short straight: 8 (up- and downstream of the second bend)
Q5 | Horizontal-quads | The second-Q at short straight. 8
Q1
Q2
Q3
Q4
Q5
Q3
Q5
Q4
Q2
Q1

## Slide 5: BPMs at KARA
          Basic configuration … located at
          up- and downstream of every separated bend
          upstream of the Q1-Q2 doublet in the long straights
          39 of 40 are integrated into the closed orbit measurement system now.
          (1 BPM at the downstream of the second bend in sector-4 is not in operation)
          BPM modules:
          Libera Brilliance (i-Tech)

## Slide 6: Corrector (Steering) Magnets at KARA
          Location and total number: horizontal correctors
          One upstream of the Q1-Q2 doublet
          Two in one gap of the separated bends
          One in the short straight
          In total … 28 horizontal correctors
          Location and total number: vertical correctors
          One between the Q1-Q2 doublet
          Two in the short straight
          In total … 16 vertical correctors

## Slide 7: Available Operation Energy at KARA
          Available operation energy range: 0.5 – 2.5 GeV
          Several typical operation beam energies:
0.5 GeV for injection
1.3 GeV for low-alpha & short bunch experiment (for CSR generation, etc.)
2.2 and 2.3 GeV for power-saving operation
2.5 GeV for normal user operation
Power-saving operation at 2.2 and 2.3 GeV
... One of two RF stations (klystrons) can be switched off.
*Two RF stations are needed for the 2.5 GeV operation.

## Slide 8: Magnets at Energy-Saving Operation
Magnets | 2.2 GeV (A) | 2.3 GeV (A) | 2.5 GeV (A)
Q1 | 295 | 311 | 343
Q2 | 298 | 323 | 374
Q3 | 256 | 267 | 288
Q4 | 278 | 285 | 309
Q5 | 283 | 296 | 330
Bend | 551 | 583 | 664
Output current for each power supply of quadrupole families and bending magnet
A fascinating point:
Can the spatial offset of quadrupole magnets change in different operating energy modes?

## Slide 9: Experiment 1: Beam-Based Alignment (BBA)
          The purposes:
          To measure special offsets of quadrupole magnets in different machine operation energy
          Ideas (Christian will present them in detail)
          BBA at 2.5 GeV operation in different beam currents (two klystrons)
          BBA at 2.2 and 2.3 GeV (one klystron)
          Measurement of lattice functions under the experimental conditions
          BBA at 2.5 GeV by changing the temperature of cooling water (technically possible?)
          Touch, disconnect and reconnect the BPM cables to see the effect on the measured beam position.
          BBA by deactivation of sextupole magnets
          BBA by change of the magnet-cycling procedure (ex. the number of cycling, warming-up time)

## Slide 10: Experiment 2: System identification of the corrector magnets system
          The purposes:
          To measure the time response of the entire corrector magnet system (power supply, magnet, vacuum chamber, control system). This is relevant for FOFB (fast orbit feedback system).
          Ideas (Günther will explain them in detail)
          Kick the beam with a chosen corrector magnet using a step-function change
          Observe the stored beam response using a fast (> 10 k Samples/sec) BPM.
          Synchronization between the corrector kick and the beam orbit recording is relevant
(The synchronisation system is not yet ready for KARA, so this time we can only do some basic tests)