## Slide 1: From backyard rain gauges to flood forecasts: using PWS in operational hydrology

## Slide 2: Waterschap Rijn en IJssel
Regional water authority in the east of the Netherlands
Mix of urban areas, agriculture, nature and higher sandy soils
Responsible for water levels, flood risk, drought, water quality and wastewater treatment
650,000
inhabitants
3,500 km
watercourses
Many !
controlled structures
Cross-border
catchments from Germany
Notes: Before I go into the Netatmo project, I want to briefly introduce the organisation and the area we manage.
My name is Eoin Burke, and I work as a hydrologist at Waterschap Rijn en IJssel. For those of you who are less familiar with the Dutch water-authority system: a waterschap is a regional water authority. We are responsible for water levels, flood risk, drought, water quality and wastewater treatment.
Our management area is in the east of the Netherlands, along the German border. It includes urban areas, agricultural land, nature areas and higher sandy soils. It is also a strongly managed water system, with thousands of kilometres of watercourses and many weirs and control structures.
A particular feature of our area is that several of our catchments are cross-border systems. A significant part of the water enters our area from Germany. That means that rainfall outside our own management area can still influence water levels and operational decisions inside our area.
This is why rainfall information is so important for us. We are not only interested in rainfall as a historical measurement. Rainfall tells us where runoff may develop, where water levels may rise, and where water managers may need to take action.
So when I talk about Netatmo today, I am not talking about a citizen-science project in isolation. I am talking about whether dense rainfall observations can help a regional water authority understand local rainfall extremes and make better operational decisions.

## Slide 3: Something did not add up
Notes: I want to start with a small story, because this project did not begin with a big strategic plan or a formal innovation programme.
It started with curiosity.
One of my colleagues from ICT, Ben Vermans, had his own weather station at home in the Winterswijk area. He was interested in weather data and was measuring rainfall locally. During intense summer showers, he started to notice something strange. What he measured in his own gauge did not always match what the official rainfall product suggested had fallen.
And these were not small differences. In one case, the local measurement was much higher than the radar-based rainfall estimate. From a water-management perspective, that matters. If the official rainfall product says 50 millimetres, but locally almost 90 millimetres has fallen, then the hydrological response in that area can be very different from what our systems expect.
At first, this sounds like a simple measurement problem. Maybe the private gauge is wrong. Maybe the radar is wrong. Maybe both are partly right. But for us it opened up a much more interesting question.
How well do we actually see local convective rainfall?
Summer storms can be very small, very intense, and very local. They can cause real problems in one village or one part of a catchment, while a few kilometres away almost nothing happens. If our observation network or rainfall product misses that local peak, then our models and operational decisions may also miss part of the event.
So this anecdote became the starting point for a bigger investigation. Could low-cost citizen rain gauges help us see rainfall that the existing network or radar product might miss?
The key question for the rest of the presentation is:
Can many imperfect local measurements help us build a better operational picture of extreme rainfall?

## Slide 4: Why good rainfall measurements matter
Rainfall data is used throughout water management:
understanding local flooding and field reports
operating weirs, pumps and retention areas
Antisipating high water levels for seawage treatmentand and urban systems
In ydrological models
Antisipating and evaluating management strategies
Notes: Rainfall may sound like a simple measurement: how many millimetres fell? But for water management, the details matter much more than the total alone.
We need to know where the rain actually fell, how intense it was, and over what period of time. That is especially important for summer convective storms. These storms can be very local. One village can receive a large amount of rain, while a few kilometres away almost nothing happens.
For a regional water authority, that difference matters. It determines which ditches, streams, urban areas and retention areas respond. It helps explain why one part of the catchment has high water levels, while another part does not. It can also help us understand field reports, local flooding, high inflow at a RWZI, or why a retention area filled up during an event.
Rainfall data also supports the management of structures. If we operate weirs, pumps or retention areas, we need to understand whether the system is responding to a real rainfall event, where that response is coming from, and how local it is.
And of course, rainfall is also essential for our models. Models are often judged by their water levels or discharges, but the model can only respond to the rainfall we put into it. Bad rainfall data in means bad model information out — and often bad understanding out as well.
So good rainfall measurements are not only useful for forecasting. They are fundamental for understanding the water system. Without them, we do not really know what input the catchment has received. And if we do not know the input, it becomes much harder to explain the response, manage structures, validate models and learn from what happened.

## Slide 5: Convective storms are small, intense and local.
Doetinchem, 2 September 2024
One local storm. Different rainfall estimates. Real operational impact.
Radar: ±30 mm Manual gauge: ±60 mm Local reports: 70 mm+
Water entered Slingeland Hospital and the fire brigade had to pump water away.
Notes: This is the type of event that makes convective rainfall so difficult for a water authority.
On 2 September 2024, a heavy convective storm passed over parts of the Achterhoek. In Doetinchem, public reports mention around 67 to 68 millimetres of rainfall in only a few hours. That is a large amount of rain, but what is important here is not only the total. It is the combination of intensity, location and impact.
One of the places affected was Slingeland Hospital. Water entered the hospital, the emergency plan was activated, and water had to be pumped away to prevent further damage. For a short period, the emergency department was affected. So this was not just an interesting rainfall measurement. It became an operational and societal issue.
And this is exactly the challenge with convective storms. They are small, intense and local. A few kilometres can make a big difference. One part of the town or catchment may receive a very intense shower, while nearby areas receive much less. For hydrological models and operational systems, this is difficult, because the response depends on where the rain actually fell.
In this case, we could see the event in the daily manual measurement in Doetinchem, which was around 60 millimetres. Local reports also spoke of more than 70 millimetres. But the real-time radar product we were looking at gave a lower daily accumulation, around 30 millimetres. That difference matters. If the rainfall input is too low, the model response will also be too low.
I do not want to use this example to say that one product is always right and another is always wrong. The point is that during local convective events, different rainfall sources can tell different stories. And when the impact is this local, we need observations that help us understand what actually happened on the ground.
So the message of this slide is simple: convective storms do not need to be large to be important. They need to be seen clearly, because small local rainfall errors can become large operational errors.
field response.

## Slide 6: Radar gives coverage, but not certainty
Source: Overeem et al. (2025), The Dutch real-time gauge-adjusted radar precipitation product, Earth System Science Data, 17, 4715–4736. DOI: 10.5194/essd-17-4715-2025. Figures 1 and 4.
Radar rainfall is still an estimate.
distance from the radar
beam blockage
vertical structure of rainfall
attenuation during heavy rain
limited ground correction
rainfall measured aloft vs. at the surface
Notes: essd-17-4715-2025.pdf essd-17-4715-2025.pdf Radar is absolutely essential for operational water management. It gives us something that rain gauges alone cannot give: spatial coverage. We can see rainfall patterns across the whole area, every few minutes, at a resolution that is very useful for hydrological models and decision-support systems.
The Dutch real-time gauge-adjusted radar product is a good example of this. It provides 5-minute precipitation accumulations every 5 minutes on roughly a 1 km² grid, and it is specifically used for hydrological decision support and nowcasting.
But this slide is about an important nuance: radar coverage does not mean radar certainty.
A radar does not directly measure rainfall at the ground. It measures reflectivity in the atmosphere, and that signal has to be processed, corrected and translated into rainfall intensity. That processing is very advanced, but there are still several sources of uncertainty.
One issue for our area is distance. In Figure 1 of the Overeem paper, you can see the radar locations and the distance to the nearest radar. The paper notes that the Dutch–German border region has longer distances to the nearest radar. That is relevant for us, because WRIJ is in the east of the Netherlands along that border.
Another issue is beam blockage. In Figure 4c, you can see what looks like a spatial artefact running across part of the east and northeast of the Netherlands. The paper identifies severe beam blockage in the easterly direction from the Herwijnen radar, mainly caused by a line of trees. That matters because beam blockage can lead to systematic underestimation in a specific direction.
There are also other uncertainties: attenuation during heavy rain, the vertical structure of rainfall, the use of a fixed relationship between reflectivity and rainfall, and the limited number of ground gauges available for real-time adjustment. And especially for short-duration, local convective events, there is also a representativeness problem: the radar samples a volume of air aloft, while a rain gauge measures a very small point at the surface.
So the point of this slide is not that radar is unreliable. The point is that radar is an essential estimate. It gives us the pattern, but not absolute certainty. And that is why additional ground observations can be valuable, especially in areas where local radar uncertainties may still exist.

## Slide 7: The idea: many low-cost ground sensors
What if we could make the ground network much denser?
many more rainfall points
direct measurements at the surface
better chance of capturing local storm cells
low-cost expansion of the observation network
extra information where radar and official stations are uncertain
Notes: Speaker notes — approximately 2 minutes
After seeing the limitations of both the official gauge network and radar rainfall products, the next question was: could we make the ground observation network much denser?
Official rainfall stations are reliable. They are well maintained, properly installed and professionally managed. But there are not enough of them to capture every local convective storm. A small summer shower can easily fall between official stations.
At the same time, more and more people have private weather stations in their gardens. These stations are not professional instruments, and they are not always perfectly placed or maintained. But they do offer something very interesting: density. There are many more of them, and they measure rainfall directly at the surface.
So the idea was not to replace the official network. The idea was to complement it. Radar gives spatial coverage. Official stations give high-quality reference measurements. Netatmo could add many extra ground observations in between.
The strength of this type of network is not that every individual sensor is perfect. The strength is that many sensors together can reveal patterns that a sparse network may miss. If several stations in the same area respond during a local storm, that gives us extra information about where rainfall actually occurred.
The project therefore developed step by step. We started with limited funding and looked at different possible products. Then we built an internal system to retrieve and manage the data. Sensors were distributed, first in a controlled pilot phase, especially in areas where we wanted to fill gaps in the network. After that came testing, validation and quality control, before thinking about wider operational use.
For me, this slide is the turning point from the problem to the opportunity. We know radar is essential but uncertain. We know official gauges are reliable but sparse. Netatmo offered a possible third layer: a dense, low-cost ground network that could help us see local rainfall more clearly.

## Slide 8: Raw citizen data is not automatically useful
Things can go wrong:
sensors too close to houses or trees
gauges placed near sprinklers, roofs or obstacles
blocked funnels, leaves, dirt or poor maintenance
Wi-Fi failures or missing data
consumer sensors not designed as an operational public network
Notes: Slide 9 — Raw citizen data is not automatically useful
Slide title
Citizen data only becomes useful after verification
Text on slide
Publicly shared data is not automatically trustworthy.
Things can go wrong:
sensors too close to houses or trees
gauges placed near sprinklers, roofs or obstacles
blocked funnels, leaves, dirt or poor maintenance
Wi-Fi failures or missing data
consumer sensors not designed as an operational public network
So before using the data operationally, we needed quality control.
Visual idea
Left side: Raw Netatmo data Messy cloud of green dots, with some warning icons: house, tree, sprinkler, blocked funnel, Wi-Fi.
Middle: Verification / quality control A filter or funnel.
Right side: Useful rainfall information Cleaned station points, maybe overlaid on a map or rainfall field.
Small footer text: Sensor test + siting rules + WUR knowledge + operational validation
At this point in the project, an important question was: can we actually trust this data?
These are not professional stations installed in standard locations by trained field staff. They are consumer sensors, often placed by private owners. And many things can go wrong. A gauge can be too close to a house, under a tree, near a sprinkler, on the edge of a roof, or it may simply not be cleaned or maintained. A small leaf in the funnel can already change the measurement. So the first lesson is that publicly shared sensor data is not automatically useful data.
We therefore started in a controlled way. My colleague first distributed sensors to colleagues within the water authority, especially in areas where we needed more rainfall information. Not everyone simply got a sensor. The location had to be useful for filling gaps in the network, and the sensors could be installed and maintained in a more controlled way. This made the first phase much more manageable.
We also had the Netatmo rain gauges tested independently. The test looked at the performance of the sensors under different rainfall intensities and calibration settings. The conclusion was that the gauges were reasonably consistent, especially with the factory calibration factor of 1.25. The recommendation was also not to let individual owners calibrate the sensors themselves, because that could introduce more errors than it solves.
But sensor performance is only one part of the story. The report also emphasised placement and maintenance: distance from obstacles, a standard measurement height, keeping the gauge level, and cleaning the tipping bucket and funnel. In other words, the data quality depends not only on the instrument, but also on the location and the behaviour of the person hosting it.
At the same time, Lotte de Vos and Wageningen University were publishing important work on crowdsourced rainfall data and quality control for personal weather stations. That created a valuable knowledge source for us. It helped us think beyond just collecting more observations, towards validating and filtering the data properly.
So this slide is really the turning point in the story: Netatmo gave us density, but verification is what made the data potentially useful for operational water management.

## Slide 9: Historical verification
After the event, the full pattern is visible.
before / during / after
neighbouring stations
spatial pattern
timing of the storm
Hindsight gives context
Notes: Once we started looking seriously at the Netatmo data, we saw that there is a big difference between historical validation and real-time validation.
When we analyse an event afterwards, we have the full context. We can look at what happened before the rain started, how the storm moved through the area, which stations responded first, which stations responded later, and whether the radar showed a similar spatial pattern. We can also check whether the rainfall totals make sense compared with neighbouring stations and with the general movement of the storm.
This is very useful, because at the beginning of a convective event the signal can look strange. Maybe only one Netatmo station measures heavy rainfall while all the surrounding stations are still dry. If you only see that single moment, it can look like a sensor error. But if you look back after the event, you may see that this station was simply the first one hit by a small intense storm cell. Ten or twenty minutes later, other stations may confirm the pattern.
So historical validation gives us the whole movie. We can see the rainfall before, during and after the event. We can check the spatial pattern and the timing. We can compare Netatmo with radar and with official gauges. That makes it much easier to distinguish between a bad measurement and a real local extreme.
This is important because it teaches us what kind of behaviour we should expect from the network. It helps us improve the validation rules and understand which signals are trustworthy. But it also shows the main operational problem: in real time we do not have the whole movie. We only have the first few frames.
And that is where the difficulty begins.

## Slide 10: Real-time verification
Notes: This is where the problem becomes operational.
When we analyse an event afterwards, we can use the full spatial and temporal pattern. But in real time, we only see the current moment. The system has to decide whether a measurement is trustworthy before we know what happens next.
Imagine that one Netatmo station suddenly measures heavy rainfall, while the surrounding stations still show zero. There are two possible explanations. It could be a real convective cell that is only just starting to hit that part of the catchment. But it could also be a bad measurement: a blocked funnel, a maintenance issue, a sensor problem, or an unrealistic spike.
For an automatic validation system, that is difficult. If the rules are too strict, the system may reject the very events we want to capture: small, intense, local convective storms. But if the rules are too relaxed, we risk allowing bad citizen-sensor data into an operational system.
This is different from professional station data. With professional stations, we have more control over siting, maintenance and instrumentation. With citizen or consumer sensors, the network is much denser, but also much less controlled. So the real-time validation has to deal with uncertainty.
That is why this step is so important. The challenge is not only collecting more observations. The challenge is deciding, quickly enough for operational use, which observations are believable.
So the key message is: in real time, a real local extreme and a bad sensor can look almost the same.

## Slide 11: The quality-control paradox
The challenge is to remove false outliers without removing real extremes.
Notes: Speaker notes — approximately 2 minutes
This is one of the key quality-control challenges in the project.
If we look at a frontal rainfall system, the pattern is usually relatively smooth. The rainfall covers a larger area, and nearby stations tend to behave in a similar way. One station may measure 8 millimetres, another 9, another 7 or 10. There is variation, but the variation is limited. For a quality-control system this is useful, because a very unusual value stands out clearly. In this situation, a standard deviation check works quite well.
But convective rainfall is different. A summer shower can be very local and very intense. One station may be directly under the core of the storm, while another station only one or two kilometres away measures almost nothing. So values like 0, 2, 28, 0 and 6 millimetres may look strange, but they may also be a realistic description of the rainfall field.
That creates the paradox. We use quality-control rules to remove bad data: false zeros, blocked gauges, unrealistic spikes, or sensors that are poorly placed or badly maintained. But the rainfall events we most want to capture are also the events that naturally produce irregular patterns and high standard deviations.
So a high standard deviation can mean two very different things. It can mean that something is wrong with the data. But it can also mean that the network has captured a real local cloudburst.
This is why we need to be careful with automatic validation. If the rules are too strict, we risk removing the extremes. If the rules are too loose, we risk accepting bad citizen-sensor data. The challenge is not simply to remove outliers. The challenge is to distinguish between false outliers and real extremes.
For me, this is the heart of the Netatmo challenge: the value of the network is precisely in seeing local extremes, but those same extremes are the hardest signals to validate automatically.

## Slide 12: Radar and Netatmo should verify each other
0
4
3
3
8
3
1
3
1
0.1
0
Notes: Speaker notes — approximately 2 minutes
This brings us to what I think is the most interesting direction for the future.
The question should not be whether radar is better than Netatmo, or whether Netatmo is better than radar. They have different strengths and different weaknesses.
Radar gives us spatial coverage. It shows the wider rainfall field and the movement of a storm across the area. That is extremely valuable, especially because rainfall is spatially variable. But radar is still an estimate of rainfall at the ground. It can underestimate rainfall, and local convective showers can be difficult to capture correctly.
Netatmo gives us something different. It gives us dense ground observations. These are real measurements at the surface, often in places where we do not have official stations. That is exactly why the network is interesting. But the individual observations are less controlled. Stations may be badly placed, poorly maintained, or affected by local errors.
So the real opportunity is to combine them.
If a single Netatmo station reports a high value, radar can help provide context. Is there a storm cell nearby? Is the rainfall pattern moving in that direction? Does the spatial pattern make the observation plausible? In that case, what first looked like an outlier may actually be a valid local extreme.
At the same time, Netatmo can help us question the radar. If several ground stations measure high rainfall in an area where radar shows much less, that may indicate radar underestimation. This is especially useful during local convective events.
So for me, the ideal future is a dual verification system. Radar helps verify Netatmo, and Netatmo helps verify radar. Neither source is perfect on its own, but together they can give us a more reliable picture of what is happening.
The key message is: the value is not in choosing one data source. The value is in intelligently combining imperfect observations.

## Slide 13: Rainfall observations feed operational decisions
Rainfall observations
Radar Official gauges Netatmo
→
Hydrological models
updated every hour
7-day forecast
water levels and discharges
→
Operational decisions
weirs, reservoirs warnings, response
August 2010: wet period followed by <100 mm in a few hours
→
The model is only as good as the rainfall data we put into it.
→
Notes: To understand why this matters operationally, it helps to look at the decision-support system we use at the water authority.
After an extreme summer rainfall event in August 2010, WRIJ reassessed how prepared we were for this type of local flood event. The situation was difficult because a wet two-week period was followed by a very intense storm, with almost 100 millimetres of rainfall in only a few hours. That combination — already wet conditions followed by intense convective rainfall — is exactly the type of situation that can create local flooding problems.
One of the systems we now have in place is our Flood Early Warning System. This system runs hydrological models for the whole catchment area. The models are updated every hour and produce forecasts of water levels and discharges for the next seven days.
The purpose of the system is not simply to make model runs. It is a decision-support system. It helps water managers with structure and weir operation, reservoir management, local flood response, evacuation procedures and communication with other authorities. It also helps prevent false positives, because unnecessary warnings also have consequences. In addition, some of our forecast data is used as input for national river modelling by Rijkswaterstaat.
But there was a key limitation. In the past, one of the weakest parts of the forecasting chain was the rainfall input. Before the IRC product came online, we were mainly dependent on the available radar precipitation product, and in our area this could underestimate rainfall. When that happened, the hydrological model started too dry, produced too little runoff, and underestimated forecast water levels.
At that time, Netatmo was not just an interesting extra dataset. It was one of the main practical ways we could improve the rainfall information going into the system. By adding dense ground observations, Netatmo gave us an additional view of where rainfall had actually occurred, especially during local summer storms.
Now the situation has changed. With the IRC product, we have a stronger radar-based rainfall product available. It seems to reduce some of the underestimation problems we saw before. But that does not mean the question is closed. There still appears to be a beam-blocking issue in parts of our area, and we need to understand how much this affects both the precipitation estimates and the model forecasts.
So the next step is not simply to choose between Netatmo and IRC. The next step is to compare the products properly: what rainfall do they estimate, what does that do to the hydrological model, and which product gives the best operational performance during the events that matter most?
That is why Netatmo remains relevant. Before IRC, it was a rainfall-input improvement. After IRC, it becomes a valuable source for validation, comparison and understanding local extremes.
The key message is: rainfall observations are not just measurements. In an operational forecasting system, they influence model results, warnings and real water-management decisions.

## Slide 14: Measurements in the model
RR
CF
Forecast
Q
Q/H
Notes: This slide shows how rainfall observations become part of the forecasting system.
The model chain is built in two main steps. First, rainfall is used in a rainfall-runoff model. This part of the model represents how the catchment responds to precipitation: how much water infiltrates, how much is stored, and how much becomes runoff towards the streams and rivers.
That runoff then becomes input for the channel-flow model. This part calculates how water moves through the watercourses and what this means for discharges and water levels at important locations in the catchment.
The forecast is therefore not only controlled by the weather forecast for the coming days. It is also strongly influenced by the starting condition of the model. The model needs to know how wet the catchment already is, how much water is already stored in the system, and whether the rivers are already responding to recent rainfall.
But there was a key limitation. In the past, one of the weakest parts of the forecasting chain was the rainfall input. Before the IRC product came online, we were mainly dependent on the available radar precipitation product, and in our area this could underestimate rainfall. When that happened, the hydrological model started too dry. It thought that less water had entered the catchment than actually did. As a result, it produced too little runoff and underestimated forecast water levels.
At that time, Netatmo was not just an interesting extra dataset. It was one of the main practical ways we could improve the rainfall information going into the system. By adding dense ground observations, Netatmo gave us an additional view of where rainfall had actually occurred, especially during local summer storms.
Now the situation has changed. With the IRC product, we have a stronger radar-based rainfall product available. It seems to reduce some of the underestimation problems we saw before. But that does not mean the question is closed. There still appears to be a beam-blocking issue in parts of our area, and we need to understand how much this affects both the precipitation estimates and the model forecasts.
So the next step is not simply to choose between Netatmo and IRC. The next step is to compare the products properly: what rainfall do they estimate, what does that do to the hydrological model, and which product gives the best operational performance during the events that matter most?
That is why Netatmo remains relevant. Before IRC, it was a rainfall-input improvement. After IRC, it becomes a valuable source for validation, comparison and understanding local extremes.
So the simple message is: rainfall observations do not just improve a map. They improve the starting condition of the hydrological model, and that influences the reliability of the forecast.

## Slide 15: Keeping our models close to reality
Data assimilation can correct the model, but better rainfall input gives the model a better start.
Notes: This figure shows another part of the forecasting system. The blue lines are the ensemble forecasts, the red line is the observed discharge, and the blue historical line is the model without the same level of correction. What you can see is that the system is constantly trying to keep the model aligned with reality. Data assimilation helps by adjusting the model state when observations show that the model is drifting away.
But this is also why rainfall input matters so much. If the rainfall entering the model is too low, the catchment state becomes too dry and the forecast response will be too low. Assimilation can partly correct this, but it is essentially fixing the symptoms. Better rainfall observations help improve the cause: the model receives a more realistic input from the start.

## Slide 16
The hidden work behind the network
What people see: rain gauges + dashboard
What keeps it alive:
Wi‑Fi changes
API connections
database
quality control
cleaning & maintenance
participant contact
selecting useful locations
documentation
detecting sensor failures
sensors installation
replacing or relocating stations
Keeping our knowledge up to date
Buying sensors is easy. Keeping the network alive is the real work.
Notes: A big lesson from this project is that the sensor is only the visible part of the system.
Buying a Netatmo rain gauge is relatively easy. But keeping a regional network useful over several years is a very different challenge. Sensors lose Wi-Fi connection, people move house, devices stop reporting, funnels become blocked, stations are placed in poor locations, and the data access has to keep working through a consumer API that was not designed for a public operational network.
So the real work is behind the scenes. We need to select good locations, keep track of station metadata, detect failures, contact participants, replace or relocate sensors, manage the database, build dashboards, document the system and maintain quality-control rules.
But this is also one of the positive outcomes of the project. It was not only a rainfall project. It helped us build knowledge inside the organisation: how to work with sensor networks, APIs, dashboards, databases and real-time data flows. That knowledge is useful beyond Netatmo alone.
So the message is: citizen data may look cheap, but operational citizen data is not free. The value comes when the organisation treats it as a real data system, with ownership, maintenance and quality control.

## Slide 17
From more data to better decisions
1
Density adds visibility
2
Verification creates value
3
Combination is the future
A sensor network is not built by buying sensors.
Notes: To close, I want to bring the story back to where it started.
This project began with a simple observation: local rainfall measurements sometimes told a different story than the operational rainfall product. That raised an important question for us as a water authority: are we seeing local convective rainfall clearly enough?
Netatmo gave us something valuable. It gave us density. It added many more ground observations in places where we did not have official stations. That helped us see local storm cells more clearly, especially during intense summer showers. Before the IRC product became available, Netatmo was also one of the main practical ways we could improve the rainfall input to our operational system.
But the project also taught us to be careful. Citizen sensors are not professional stations. They can be badly placed, poorly maintained, blocked by leaves, affected by Wi-Fi problems, or influenced by local conditions such as trees, roofs or sprinklers. And in real time, it is not always easy to distinguish between a bad measurement and a real local cloudburst.
So the lesson is not simply that more data is better. More data only becomes useful when it becomes trusted information. That requires verification, maintenance, good metadata, infrastructure, dashboards, quality-control rules and continuous learning.
For me, the most important insight is that each rainfall source answers a different part of the question. Radar gives us the spatial pattern. Official gauges give us reliable reference measurements. Netatmo gives us density and local ground observations.
None of these sources is perfect on its own. But together they can help us build a better picture of what actually happened on the ground, and that is what we need for operational water management.
So my final message is this: the future is not one perfect rainfall product. The future is intelligent combinations of imperfect observations.

## Slide 18
References and sources
Overeem, A., Leijnse, H., Veldhuizen, M. and Anker, B. (2025). The Dutch real-time gauge-adjusted radar precipitation product. Earth System Science Data, 17, 4715–4736. https://doi.org/10.5194/essd-17-4715-2025
AMO-meteo (2021). Onderzoek NETATMO neerslagmeter. Rapportage in opdracht van Waterschap Rijn en IJssel.

## Slide 19
Thank you