## Slide 1
Particle therapy beam monitoring with HV-CMOS sensors
Matthias Balzer, Alexander Dierlamm, Felix Ehrler, Horacio Mateos, Andreas NürnbergETP, Ivan Peric, Rudolf Schimassek, Alena Weber
Picture from https://www.klinikum.uni-heidelberg.de/interdisziplinaere-zentren/heidelberger-ionenstrahl-therapiezentrum-hit/leistungsspektrum

## Slide 2: Introduction
Radiotherapy is an important pillar in the therapy of cancers and is prescribed to ~50% of cancer patients.
Standard radiotherapy uses photon radiation, whereas particle therapy uses
  high energy protons (50−220MeV; flux<~2x109p/s; FWHM 8−30mm) and
  carbon ions (90−430MeV/u; flux<~108p/s; FWHM 3.5−12mm)
  [HL-LHC, R~25cm: 107p/(cm²s)]
to destroy tumor cells in the body of patients.
To achieve local tumor control, a well-controlled particle beam in terms of position and dose is of utmost importance for the success of the therapy and the patient’s health.
  gas-based wire chambers used so far
We want to develop an HV-CMOS based monitoring system for clinical use
  beam position resolution ~200µm
  response time ~ 100µs
  low mass (<2mm water eq.) and large size (25x25cm²)
  radiation hard (<1.5x1015p/cm² per year at central spot)
  magnetic field tolerance ( o(100mT) )

## Slide 3: HeiKa Project
We managed to get funding for a first test chip submission from HeiKa
  22k/58k to be shared between HIT (Heidelberger Ionenstrahl-Therapiezentrum) and IPE
Project extends over 2020
Goal is to prepare for a larger application likely at DFG
Charac. and design (1,2)
Task 4: Conceptual development of a dedicated data acquisition system
  Extend readout with FPGA evaluation boards to high-performance DAQ system
Task 5: Characterization of the test sensor
  Main task during summer
Task 6: Evaluation of possible modification in the beam monitoring system
Task 7: Design of the demonstrator sensor and the full-size system
  The demonstrator sensors will follow the test chip design with best performance in the summer test beams scaled to the full reticle size (~100k€)
  Conceptual extension towards the final system as basis for next funding application
Task 1: Characterization of pixel response to the therapeutic particle beam
  Current HV-CMOS chips are used to check their performance in these harsh beams and learn for test chip design
  Next beam test on 14/15.3.2020
Task 2: Design and submission of beam monitor test sensor
  3-4 approaches are being implemented on an engineering run to be submitted by end of March
Task 3: Development of an in-beam magnetic field test bench
  Task for HIT
Q1’20
Q2’20
Q3’20
Q4’20
Concept of scaled DAQ (4)
Test-chip evaluation (5)
Design of demonstrator (7)
Modifications of mon. system? (6)

## Slide 4: Test beam and currently evaluated chips
Beam test in June‘19 with MuPix8 and ATLASPix1 telescope
Irradiation of ATLASPix3 at beam dump from Monday on
Next beam test with MuPix8 and ATLASPix3 on 14./15.3.
Beam dump
Cluster size distribution for MuPix8
Partial beam profile on MuPix8
20mm
3mm
MuPix8:
~1 cm x 2 cm
128 x 200 pixels
Pixel size: 80 μm x 81 μm
Triggerless column drain readout
Analog information: 6 bit
Timestamp: 10 bit
Three readout links: 3x 1hit / 25 ns
soon: MuPix10
~2.1 cm x 2.1 cm
250 x 256 pixels
Pixel size: 80 μm x 80 μm
Triggerless column drain readout
Analog information: 5 bit
Timestamp: 11 bit
Three readout links: 3x 1hit / 25 ns
ATLASPix3:
2 cm x 2 cm
Pixel size: 50µm x 150µm
Radiation hard; will be irradiated at beam stop
It supports hit driven untriggered and triggered readout
~0.5 hits/cm²/25ns

## Slide 5: Test-chip concepts
General properties
  TSI 180nm process
  Charge sensitive amplifier, comparator and 8-bit counter with readout bus driver
  Pixel size: ~ 200µm x 200µm
  Matrix each 5mm x 5mm
Chip designs
  Simple counting design:
    counting hits
    radiation hard design
    90% electrode coverage
  Integrating design:
    counting hits and integrating signal (~dose)
    not radiation hard, yet
    ~80% electrode coverage
    eventually, not integrating each cell, but total signal of matrix to get scaling factor for profile
  Extended counting design
    counting hits
    radiation hard design
    100% electrode coverage; requires extra deep p-well, which is new to the company and has some risk
Counting cell
Counting matrix
Integrating cell