## Slide 1: Recent Progress in Polarimetric Radar QPE
Alexander Ryzhkov
University of Oklahoma, USA
With contributions from Jian Zhang, Pengfei Zhang, and Ju-Yu Chen
RealPEP meeting, 5 October 2020
Slide 1

## Slide 2
Layout
Polarimetric QPE based on specific attenuation – R(A)
Current status and challenges
QPE at longer distances from the radar
Polarimetric VPR
Slide 2

## Slide 3
Ryzhkov, A., M. Diederich, P. Zhang, and C. Simmer, 2014: Utilization of specific attenuation for rainfall estimation, mitigation of partial beam blockage, and radar networking. J. Atmos. Oceanic Technol., 31, 599 – 619.
Diederich, M., S. Troemel, A. Ryzhkov, P. Zhang, and C. Simmer, 2015: Use of specific attenuation for rainfall measurements at X-band radar wavelengths. Part II: Rainfall estimates and comparison with rain gauges. J. Hydrometeorology, 16, 503 - 516
Wang, Y., S. Cocks, L. Tang, A. Ryzhkov, P. Zhang, J. Zhang, and K. Howard, 2019: A prototype quantitative precipitation estimation algorithm for operational S-band polarimetric radar utilizing specific attenuation and specific differential phase: Part I – Algorithm description and initial results. J. Hydrometeorology, 20, 985 – 997.
Cocks, S., Y. Wang, L. Tang, A. Ryzhkov, P. Zhang, J. Zhang, and K. Howard, 2019: A prototype quantitative precipitation estimation algorithm for operational S-band polarimetric radar utilizing specific attenuation and specific differential phase: Part II – Case study analysis and performance verification. J. Hydrometeorology, 20, 999 – 1014.
Zhang, J., L. Tang, S. Cocks, P. Zhang, A. Ryzhkov, K. Howard, C. Langston, and B. Kaney, 2020: A dual-polarization radar synthetic QPE for operations. J. Hydrometeorology, 22, doi: 10.1175/JHM-D-19-0194.1
Basic publications on R(A)
Slide 3

## Slide 4
In this formulation, the A(r) estimate is immune to the Za biases caused by radar miscalibration, partial beam blockage, and wet radome
How to estimate specific attenuation A?
Za (r) is a radial profile of attenuated (and possibly biased) reflectivity
PIA is a two-way path-integrated attenuation
Slide 4

## Slide 5
How to measure PIA?
Range
PIA is estimated using total differential phase shift along the propagation path in rain
Reliable estimation of the radial profile of A is possible for
ΔΦDP as low as 1 - 3°
Slide 5

## Slide 6
Sensitivity to the radar wavelength and temperature
Specific attenuation A is a function of the radar wavelength λ and temperature T, therefore, the multiplier γ in the power-law R(A) relation and the factor α = A/KDP depend on λ and T as well
However, their product (and the R(A) estimate) is practically insensitive to the variability of temperature and radar wavelength (in a given frequency band: S, C, or X) if δ is close to 1
Therefore, a single R(A) relation can be used in a wide range of temperature and radar wavelength, e.g., R = 4120 A1.03 at S band
Slide 6

## Slide 7
Sensitivity of the factor α to the DSD variability (ZDR)
T = 0°C – black dots
T = 30°C – grey dots
In the current version of the R(A) algorithm employed at S band, the factor α is determined from a slope of the ZDR dependency on Z (“ZDR slope”)
The estimate of the ZDR slope is immune to calibration errors of Z and ZDR
Slide 7

## Slide 8
Continental MCS
Kansas
Hurricane Florence North Carolina
Zdr slope is high
Zdr slope is low
“ZDR slope” for continental and tropical rain
Black circles indicate the bottom of the ML
From Zhang et al. 2020
Slide 8

## Slide 9
Practical advantages of the R(A) method
Low sensitivity to the DSD variability
Immunity to radar miscalibration, partial beam blockage, attenuation, and impact of wet radome
High spatial resolution (similar to R(Z) )
Uniformly good performance for light and heavy rain
Ideal for networking and compositing (particularly for the radars operating at different wavelengths)
Caveats
Has to be complemented by R(Z) for ΔΦDP < 1 - 3° and by R(KDP) in hail cores
Parameter α is variable depending on rain type and needs real time optimization
Slide 9

## Slide 10
Distance R(A)+R(KDP) data available dependent upon bottom of ML
~ 175 km
Partial Blockage
R(A)
R(Z)
Partial blockage mitigation
230 km
R(A)+R(KDP)
Partial Blockage
mitigated
The impact of partial blockage of radar beam caused by trees is eliminated in a 24-hour rain total map obtained using a combination of the R(A) and R(KDP) relations
Slide 10

## Slide 11
Iowa Flood Center Area
Evaluation of the R(A) algorithm in the Iowa Flood Center area
Seo, B., A. Ryzhkov, and W. Krajewski, 2020: Evaluation of the specific attenuation method for radar-based quantitative precipitation estimation: Improvements and practical challenges. J. Hydrometeorol., 21, 1333 – 1347.
Slide 11

## Slide 12
IFC validation results
Grey circles – R(Z)
Red circles – R(A)
NMAE is reduced about two times if R(A) is utilized
Slide 12

## Slide 13
Limitation of using a single α for a whole radar coverage area
α vs ZDR from disdrometer simulations.
For S band, T = 20°C
Smaller Drops Larger Drops
Stratiform rain where α is larger due to lower ZDR
Convective line, α is smaller due to higher ZDR
In the current S-band R(A) algorithm, a single value of α is used for a whole radar coverage area and spatial variability of α is ignored
This inevitably causes underestimation of rain dominated by smaller drops and overestimation of rain dominated by larger drops
Slide 13

## Slide 14
S band
Alternative way to determine the factor α
Two possible relations
Pros: There is no need to estimate the ZDR slope. Azimuthal variability of α is captured
Cons: ZDR should be well calibrated; Z and ZDR have to be corrected for attenuaton
b = 0.62
d = 0.72
Slide 14

## Slide 15
KTLX 2015/05/24
00:46 UTC
Hurricane Irene
2011/08/27
12:26 UTC
El = 0.5°
Continental case
Tropical case
Z
Z
Continental MCS
ZDR
ZDR
Slide 15

## Slide 16
Continental
Tropical
α is generally higher for tropical rain
Slide 16

## Slide 17
20150524-00:26 UTC
20150524-05:59 UTC
Black star:
Red star:
Correlation between azimuthal patterns of α and average values of Z and ZDR
Obvious anti-correlation is observed
Slide 17

## Slide 18
Scatterplots of R vs Z, KDP, and A for very tropical (red dots) and very continental rain (blue dots)
R - Z
R - KDP
R - A
R - A
R(A) is less efficient at C band than at S band
The reason for this is resonance scattering on large raindrops at C band
Challenges at C band
At C band, the R(A) relation is expected to be efficient for rain dominated by small drops
For rain dominated by large drops, the R(KDP) relation is expected to work better
Slide 18

## Slide 19
QPE at longer distances from the radar
Polarimetric VPR
Slide 19

## Slide 20
Radial profiles of ΔZ for different heights and strengths of the ML at El = 0.5⁰
Hb = 1.0 km
2.0 km
3.0 km
The VPR correction schemes are designed to eliminate a positive Z bias due to the BB contamination and a negative bias caused by rain overshooting at longer distances
Hb = 2.0 km
Thick ML
Thin ML
Range interval of BB contamination depends on the height of the ML and its strength / thickness
Slide 20

## Slide 21
0.6
1.0
2.8
R = 0.6 R(Z) wet snow
R = 1.0 R(Z) dry snow and r < Rtt
R = 2.8 R(Z) dry snow / crystals and r > Rtt
The origin of discontinuities in the existing WSR-88D QPE
The use of a number of “fudge” factors in the R(Z) relations utilized in the existing WSR-88D QPE partially mitigates the bias but creates strong discontinuities in the retrieved rainfall fields. The QPE product is vulnerable to the hydrometeor misclassifcation
Slide 21

## Slide 22
Melting layer signatures in a composite PPI at El = 2.4°
Polarimetry offers possible solution because the areas of BB contamination are very well delineated in the fields of polarimetric radar variables such as differential reflectivity ZDR and cross-correlation coefficient ρhv (or CC)
The suggested methodology called “polarimetric VPR” or PVPR is based on the correlation of the radial profiles of Z and ρhv in the presence of the melting layer. Radial profiles of ρhv are used to detect the range intervals where contamination from BB occurs and to estimate the height of the ML. Therefore, MLDA and PVPR are closely linked in a new paradigm.
Slide 22

## Slide 23
Z
ZDR
ρhv
HFL is the height of the freezing level (Tw = 0°C)
Radial profiles of Z, ZDR, and ρhv at El = 0.5° for low-level, horizontally uniform melting layer
Impact of range and beam broadening
Zrain = 30 dBZ
Radial profiles of Z bias, ZDR, and ρhv are strongly correlated
Slide 23

## Slide 24
1
1
2
2
Model radial profiles of Z bias and ρhv
Radial profiles of Z bias and ρhv are correlated. Deeper minimum of ρhv corresponds to higher Z bias and one can quantify the Z bias using radial profile of ρhv.
The whole idea of PVPR is to examine a measured radial profile of ρhv at a given elevation and find its best match in the family of model radial profiles stored in the lookup tables
Slide 24

## Slide 25
New VPR concept (polarimetric VPR or PVPR)
Establish statistical correlations between intrinsic vertical profiles of Z and ρhv in the melting layer using the QVP methodology
Simulate a multitude of the model radial profiles of Z bias and ρhv at lowest antenna tilts for different heights and strengths of the melting layer and store them in lookup tables
Pick up an appropriate model profile of the Z bias at every azimuth by finding the best match between the model and observed radial profiles of ρhv and subtract this model profile of Z bias from the measured radial profile of Z
Slide 25

## Slide 26
Simplified model of the melting layer
Every radial profile of CC is labeled by two parameters (or indexes): (1) height of the ML bottom Hb and (2) strength of the ML
Hb = 0.2,0.4, ….3.0 km (15 values)
min(ρhv) = 0.80, 0.82, 0.84, 0.86, 0.88, 0.90, 0.92, 0.94 (8 values)
ΔH = 0.55, 0.53, 0.51, 0.49, 0.45, 0.40, 0.36, 0.32 km
In the current version of the algorithm, 120 radial profiles of CC and ΔZ are generated for a given antenna elevation
Slide 26

## Slide 27
There is no need to store full 120 radial profiles of CC
Each profile of CC (model or measured) can be characterized by two parameters which can be robustly estimated from observations
These are rb – the distance to the CC dip and the “strength” of the ML (S) defined as
The parameters rb and S are stored in the two lookup tables or matrices 15 x 8 for each antenna elevation
Such lookup tables have to be generated only once
Slide 27

## Slide 28
Lookup table for rb
El = 2.4°
True depth of the ML (km) |  |  |  |  |  |  |  | 
Hb (km) | 0.55 | 0.53 | 0.51 | 0.49 | 0.45 | 0.40 | 0.36 | 0.32
Range to the ML bottom (km) |  |  |  |  |  |  |  | 
0.2 | 5.0 | 5.0 | 5.25 | 5.25 | 5.25 | 5.25 | 5.5 | 5.5
0.4 | 9.25 | 9.25 | 9.25 | 9.5 | 9.5 | 9.5 | 9.75 | 10.0
0.6 | 13.0 | 13.25 | 13.25 | 13.5 | 13.5 | 13.75 | 13.75 | 14.0
0.8 | 17.0 | 17.0 | 17.25 | 17.25 | 17.5 | 17.75 | 17.75 | 18.25
1.0 | 20.5 | 20.75 | 21.0 | 21.25 | 21.25 | 21.5 | 21.75 | 22.25
1.2 | 24.25 | 24.25 | 24.5 | 25.0 | 25.0 | 25.25 | 25.75 | 26.25
1.4 | 27.75 | 28.0 | 28.25 | 28.5 | 28.75 | 29.25 | 29.75 | 30.5
1.6 | 31.25 | 31.5 | 31.75 | 32.25 | 32.5 | 33.0 | 33.5 | 34.5
1.8 | 34.5 | 35.0 | 35.25 | 35.75 | 36.25 | 36.75 | 37.5 | 38.75
2.0 | 38.0 | 38.5 | 38.75 | 39.25 | 39.75 | 40.5 | 41.25 | 42.75
2.2 | 41.25 | 41.75 | 42.25 | 42.75 | 43.5 | 44.25 | 45.25 | 47.0
2.4 | 44.5 | 45.25 | 45.75 | 46.5 | 47.0 | 47.75 | 49.0 | 51.0
2.6 | 48.0 | 48.5 | 49.25 | 49.75 | 50.5 | 51.5 | 52.75 | 55.25
2.8 | 51.25 | 51.75 | 52.5 | 53.25 | 54.25 | 55.25 | 56.75 | 59.5
3.0 | 54.5 | 55.25 | 56.0 | 56.75 | 57.75 | 58.75 | 60.5 | 63.75
Slide 28

## Slide 29
True depth of the ML (km) |  |  |  |  |  |  |  | 
Hb (km) | 0.55 | 0.53 | 0.51 | 0.49 | 0.45 | 0.40 | 0.36 | 0.32
Strength of the ML |  |  |  |  |  |  |  | 
0.2 | 4.66 | 3.94 | 3.24 | 2.63 | 1.97 | 1.31 | 0.84 | 0.46
0.4 | 4.93 | 4.13 | 3.35 | 2.69 | 1.99 | 1.31 | 0.82 | 0.43
0.6 | 5.30 | 4.39 | 3.52 | 2.79 | 2.05 | 1.32 | 0.81 | 0.40
0.8 | 5.72 | 4.71 | 3.72 | 2.92 | 2.12 | 1.34 | 0.80 | 0.37
1.0 | 6.17 | 5.04 | 3.94 | 3.06 | 2.19 | 1.36 | 0.79 | 0.34
1.2 | 6.62 | 5.37 | 4.16 | 3.21 | 2.27 | 1.39 | 0.78 | 0.31
1.4 | 7.08 | 5.71 | 4.38 | 3.35 | 2.34 | 1.41 | 0.76 | 0.28
1.6 | 7.52 | 6.03 | 4.60 | 3.48 | 2.41 | 1.42 | 0.75 | 0.26
1.8 | 7.96 | 6.35 | 4.81 | 3.61 | 2.47 | 1.43 | 0.73 | 0.23
2.0 | 8.39 | 6.11 | 5.01 | 3.74 | 2.53 | 1.44 | 0.71 | 0.20
2.2 | 8.80 | 6.96 | 5.21 | 3.85 | 2.59 | 1.45 | 0.69 | 0.18
2.4 | 9.21 | 7.25 | 5.39 | 3.96 | 2.64 | 1.45 | 0.67 | 0.15
2.6 | 9.60 | 7.53 | 5.57 | 4.07 | 2.68 | 1.45 | 0.65 | 0.13
2.8 | 9.98 | 7.81 | 5.74 | 4.17 | 2.72 | 1.45 | 0.63 | 0.11
3.0 | 10.4 | 8.07 | 5.91 | 4.26 | 2.76 | 1.45 | 0.61 | 0.09
Lookup table for S
El = 2.4°
Slide 29

## Slide 30
MLDA. Sloping melting layer, KTLX 2019/04/13
Z
CC
El = 0.9°
El = 0.9°
Z
ML bottom height
Slide 30

## Slide 31
ρhv
ρhv
El = 0.5°
El = 0.9°
MLDA. Sharp snow/rain frontal boundary. KTLX 2020/02/05
ML bottom height
Slide 31

## Slide 32
Polarimetric VPR QPE
It is just one small step from MLDA to PVPR QPE
In addition to the MLDA lookup tables, 120 radial profiles of Z bias (ΔZ) are generated and stored for different heights and strengths of the ML: ΔZ (r, ih, is)
For any given azimuth and elevation, the indexes ih and is of the ML height and strength are determined from the MLDA output
A corrected radial profile of Z is obtained as
Slide 32

## Slide 33
El = 0.5 deg
El = 1.45 deg
KBMX WSR-88D
2014/02/12
Slide 33

## Slide 34
Before PVPR correction
After PVPR correction
El = 0.5⁰
El = 1.45⁰
El = 0.5⁰
El = 1.45⁰
KBMX WSR-88D
2014/02/12
Slide 34

## Slide 35
KINX WSR-88D
2020/01/17
El = 1.3°
Slide 35

## Slide 36
KINX WSR-88D radar, 2020/01/17, El = 1.3°
Before correction
After correction
Slide 36

## Slide 37
Composite PPI at El = 1.5⁰
DWD
C band
Slide 37

## Slide 38
Composite PPI at El = 0.5⁰
DWD
C band
Slide 38

## Slide 39
Before PVPR correction
After PVPR correction
El = 1.5⁰
El = 1.5⁰
El = 0.5°
El = 0.5°
DWD
C band
Slide 39

## Slide 40
Courtesy of Ju-Yu Chen (UBonn)
Slide 40

## Slide 41
Taking into account evaporation
X band radar
(BoxPol)
Martinitis, S., H. Grams, C. Langston, J. Zhang, and K. Howard, 2018: A real-time evaporation correction scheme for radar-derived mosaicked precipitation estimations. J. Hydrometeorology, 19, 87 – 111.
The Martinitis et al. (2018) scheme takes into account vertical profiles of humidity but not DSD
Slide 41

## Slide 42
Taking into account evaporation
M. Kumjian and A. Ryzhkov, 2010: The impact of evaporation on polarimetric characteristics of rain. Theoretical model and practical implications. Journal of Applied Meteorology and Climatology, 49, 1247 – 1267.
For a given vertical profile of relative humidity, rain with lower ZDR evaporates faster
Slide 42

## Slide 43
Taking into account coalescence / breakup in warm (tropical) rain
Hurricane Irma, Florida, 10 September 2017
Strong vertical gradients of Z, ZDR, KDP, and corresponding rain rate indicate warm rain process
Slide 43

## Slide 44
Conclusions on R(A)
The R(A) methodology demonstrates success at S band and is ready for operational implementation on the US NEXRAD network
Several issues remain such as utilization of a single factor α for a whole radar coverage area although this factor is updated from scan to scan. Such a choice of α inevitably leads to some underestimation of rain dominated by small drops and mild overestimation of rain characterized by large drops
A novel technique for optimization of α is suggested and its testing is underway
The R(A) technique seems to be less efficient at C band and the use of the R(A) relation has to be complemented by more aggressive utilization of the R(KDP) relation
Slide 44

## Slide 45
Conclusions on PVPR
The suggested PVPR technique passed the feasibility test and is applicable at S and C bands
It shows good promise in the two challenging situations: (a) BB enhancement of Z is mixed with the increase of Z due to embedded convection and (b) Z at lower tilts is biased by partial beam blockage
This version of PVPR takes into account azimuthal and radial heterogeneity of the rain field and melting layer
It makes a good use of higher antenna elevations for QPE in situations when the data at lowest elevation are of poor quality due to ground clutter contamination or beam blockage
Slide 45