## Slide 1: Ultra-low mass silicon trackers for high-rate, high-multiplicity heavy-ion physics
Johann M. Heuser GSI Helmholtz Center for Heavy Ion Research, Darmstadt, Germany
607th Heraeus Seminar “Semiconductor detectors in astronomy, medicine,
particle physics and photon science”, Bad Honnef, 14-17 February 2016

## Slide 2: Overview
What is Heavy-Ion Physics?
Challenge: Charged-particle tracking at high multiplicities and high rates
Silicon Detectors: Microstrips and pixels
Technical approach of two modern applications:
  ALICE Inner Tracking System (Collider Experiment)
  CBM Silicon Tracking System (Fixed-Target Experiment)

## Slide 3: Heavy-ion physics
matter
crystal
atom
nucleus
proton/neutron
quarks
cell
(10-3 m)
(10-10 m)
(10-14 m)
(10–15 m)
(<10-18 m)
(10-5 m)
electron
Collective term for research with energetic heavy ions.
Heavy ions are the nuclei of heavy elements (ionized atoms, e.g. Gold, Lead).
As projectiles they are important probes to study matter.
Research fields
nuclear physics, atom and solid state physics
nuclear chemistry
astro physics
energy and material research
biology and medicine

## Slide 4: Nuclear matter
Hadrons: composite particles made of quarks held together by the strong force:
mesons (quark + anti-quark)
baryons (3 quarks)
neutron
proton
nucleus
Why are quarks confined in hadrons?
How is their mass generated?
Coupling strength between two quarks
Experimental approach: Measure the properties of hadrons inside nuclear matter under extreme conditions: heat, pressure.
wikipedia

## Slide 5: Exploring the QCD phase diagram
Courtesy of K. Fukushima & T. Hatsuda
At very high temperature:  highest-energy ion collisions
N of baryons  N of antibaryons Situation similar to early universe
Lattice-QCD finds crossover transition between hadronic matter and Quark-Gluon Plasma
Experiments: ALICE, ATLAS, CMS at LHC-Heavy-Ion program STAR, PHENIX at RHIC
Quark-Gluon Plasma

## Slide 6: Exploring the QCD phase diagram
Courtesy of K. Fukushima & T. Hatsuda
At high baryon density:  heavy-ion beams in range 7 to 45 GeV/nucleon
N of baryons  N of antibaryons Densities like in neutron star cores
L-QCD not (yet) applicable Models predict first order phase transition with mixed or exotic phases
Experiments: RHIC-BES, NA61 at CERN SPS,
CBM at FAIR, NICA at JINR
Compressed Baryonic Matter

## Slide 7
Heavy-ion collisions

## Slide 8
Diagnostic probes

## Slide 9
TPC detector
Charged-particle tracks, collider experiment

## Slide 10
Silicon pixel vertex tracker
Charged-particle tracks, fixed-target experiment

## Slide 11: Tracking challenge
high charged-particle multiplicities
  example LHC Pb+Pb @ 5.5 TeV: dnch /d | =0.5  1900
  track densities up to 100 cm-2
high collision rates:
  O(10 kHz) at LHC to 10 MHz at FAIR: due to rare probes
standalone tracking
  high detector segmentation
  low-mass detector  momentum resolution of O(1%)
  fast read-out electronics: little or no pile-up of collisions
  track-matching to other detectors
  in-detector decay topology
vertex detection
  particularly fine segmentation
  especially thin detector layers
  detection of short-lived decays
 typically with inner layers of a tracking detector, or a specialized add-on to it.

## Slide 12: Silicon detectors
Silicon Microstrip Detector:
thickness typ. 300 m
1 or 2-sided segmentation
fine sensor pitch, typ. 50 m
1-d native hit pattern, 2-d combinatorial points
electronics separated from sensor
Pixel Detectors:
thickness < 300 m
fine sensor pitch, typ. < 50 m
2-d native hit pattern
hybrid detector: electronics sandwiched with sensor, fast
monolithic detector: thin, ~50 m, electronics integrated in sensor, less fast

## Slide 13: Two tracking detector systems under construction:
ALICE Inner Tracker Upgrade
CBM Silicon Tracking System

## Slide 14: Large Hadron Collider @ CERN
largest and highest-energy particle accelerator,
27 km circumference
p+p,  s = 14 TeV Pb+Pb,  sNN = 5.5 TeV/nucleon

## Slide 15
ALICE Experiment

## Slide 16
Current ALICE ITS
ALICE ITS slides: from L. Musa, ref. 5

## Slide 17: ITS Upgrade Design Objectives
1. Improve impact parameter resolution by a factor of ~3
Get closer to IP (position of first layer): 39 mm  23 mm
Reduce x/X0 /layer: ~1.14%  ~ 0.3% (for inner layers)
Reduce pixel size: currently 50 μm x 425 μm  O(30 μm x 30 μm)
2. Increase granularity:
6 layers  7 layers
silicon drift and strips  (monolithic active) pixels
3. Increase readout speed (currently limited at 1 kHz with full ITS)
Pb+Pb interactions at > 100 kHz,
p+p interactions at ~ several 100 kHz
4. Fast insertion/removal for yearly maintenance
possibility to replace non-functioning detector modules during yearly shutdown

## Slide 18: ALICE ITS Upgrade

## Slide 19: ITS pixel detector

## Slide 20: Pixel detector requirements

## Slide 21: Pixel chip architecture

## Slide 22: ITS Layout

## Slide 23: Inner Barrel Staves

## Slide 24: Outer Barrel Staves

## Slide 25: Interconnection of pixel chip to flex PCB
Powering and Read-out
Cooling
power dissipation: 300/100 mW per ASIC in inner/outer barrel
total power dissipation: 15 kW
cooling duct embedded in a carbon structure, de-mineralized water flow
detector operation at room temperature, dry air-flow to control humidity
external thermal shield towards the TPC detector

## Slide 26: System Integration

## Slide 27: ITS Upgrade performance simulation

## Slide 28: FAIR - Facility for Anti-Proton and Ion Research, Darmstadt

## Slide 29: FAIR - Facility for Anti-Proton and Ion Research, Darmstadt
GSI Helmholtz Center for Heavy Ion Research GmbH, Darmstadt, Germany
p to U beams,
2 – 45 GeV/nucleon
highest intensities
1 km circumference
CBM

## Slide 30
Time-of-Flight Detector
Projectile
Spectator
Detector
DAQ/FLES HPC cluster
Dipole
Magnet
Silicon
Tracking
System
CBM Experiment
Ring
Imaging
Cherenkov Detector
Transition
Radiation
Detector
Muon
Detector
Micro
Vertex
Detector
beam
Beam Dump
HADES Detector

## Slide 31: Silicon Tracking in CBM
p+C, 30 GeV
few charged particles
STS task: track identification + momentum determination
    from few charged particles in p+A collisions at SIS100
    to hundreds of charged tracks in A+A collisions at SIS100 and SIS300
    at 105 to 107/s collisions per second
identification of decay topologies within its aperture
links to further detectors: MVD (upstream) and MUCH/RICH (downstream)
central Au+Au, 8 AGeV
~350 charged particles
central Au+Au, 25 AGeV
~700 charged particles
UrQMD + GEANT + CbmRoot

## Slide 32: CBM Micro-Vertex Detector
Customized FEE & DAQ:
TRB-based
Ultra-thin: CVD diamond, TPG
Sensors: CMOS MAPS
Radiation hard,
Thinned to 50 µm,
< 150 mW/cm2,
spatial resol. < 5 µm,
R/O several 10 µs/frame
Prototyping & test beam:
MVD prototype
PRESTO
MVD demonstrator
RVC foam
Thermal Pyrolytic Graphite

## Slide 33: STS design constraints
Coverage:
  from center-of mass to close to beam rapitidies
  aperture 2.5° <  < 25°
Momentum resolution
  δp/p  1%
  field integral 1 Tm, 8 tracking stations
  25 µm single-hit spatial resolution
  material budget per station 0.3 – max. ~1% X0
  No event pile-up
  interaction rates 0.1 - 10 MHz
  self-triggering read-out
  timestamp resolution < 5 ns
  signal shaping time < 20 ns
Efficient hit & track reconstruction
  close to 100% hit efficiency
  > 95% track eff. for p > 1GeV/c
Minimum granularity
  at hit rates < 20 MHz/cm2:
  maximum strip length compatible with hit occupancy and S/N performance
  largest read-out pitch compatible with the required spatial resolution
Radiation hard sensors
  compatible with CBM physics program:
  1 × 1013 neq/cm2 (SIS100)
  1 × 1014 neq/cm2 (SIS300)
Integration, operation, maintenance
  compatible with the confined space in the dipole magnet
  efficient cooling for electronics
  cooling of sensors
  system design including target chamber, MVD, beam pipe
  extraction possible for maintenance

## Slide 34: System concept
8 tracking stations in dipole magnet: between 0.3 m and 1 m from target.
Aperture: 2.5° <  < 25° (38° horizontal).
Double-sided micro-strip sensors in 3 sizes, arranged in modules on carbon-fiber supported ladders.
Readout electronics at periphery.
Target chamber/MVD/beam pipe.
Thermal enclosure, sensors at -5 ◦C.
STS
2.5°
25°
beam
target

## Slide 35: STS integration concept
8 stations, volume 2 m3, area 4 m2
896 detector modules
    1220 double-sided microstrip sensors
    ~ 1.8 million read-out channels
    ~ 16 000 r/o STS-XYTER ASICs
    ~ 16 000 ultra-thin r/o cables (à 5 components)
106 detector ladders with 4-5 modules
power dissipation: 42 kW (CO2 cooling)
building block: 4-5 modules per ladder
front-end board: 8 self-triggering r/o ASICs
sensor
8 tracking stations
ladder
mech. unit
x/X0 [%]
ultra-thin r/o cables
1 m
material budget per station

## Slide 36: Silicon microstrip sensors
300 µm thick, n-type silicon
double-sided segmentation
2nd metal routing lines
1024 strips of 58 µm pitch
strip length 2/4/6/12 cm
angle front/back: 7.5/0 deg
read-out from top edge
rad. tol. up to 1014 neq/cm2

## Slide 37: Silicon microstrip sensors
300 µm thick, n-type silicon
double-sided segmentation
2nd metal routing lines
1024 strips of 58 µm pitch
strip length 2/4/6/12 cm
angle front/back: 7.5/0 deg
read-out from top edge
rad. tol. up to 1014 neq/cm2
6.2 × 6.2 cm2
6.2 × 4.2 cm2
6.2 × 2.2 cm2
prototype sensors from CiS, Germany, and Hamamatsu Photonics, Japan
prototype read-out sector with two daisy-chained sensors
6.2 × 12.4 cm2

## Slide 38: Read-out cables
cable stack: thickness 0.230 % X0
spacer layer
signal layer: 64 Al lines of 116 µm pitch, 10 µm thick on 14 µm polyimide, lengths up to 55 cm

## Slide 39: Read-out ASIC “STS-XYTER”
STS-XYTER ASIC
purely data driven read-out
time-stamped data elements
channels | 128, polarity +/-
noise | 1000 e- under load
ADC range | 16 fC, 5 bit
clock | 250 MHz
power | < 10 mW/channel
timestamp | < 5 ns resolution
out interface | 4(5) × 500 Mbit/s LVDS
v1.0 produced (v2.0 under design) UMC 180 nm CMOS
every channel is divided into two sub-channels:
fast branch: time-stamp
slow branch: signal digitization
noise minimization in self-triggering system:
effective two-level discrimination
trigger to the timestamp latch is vetoed if ADC-LSB generated no signal
no transmission of data then
CBM-NET
(v1.0 )
GBT (V2.0)
LSB veto
ts = 30 ns
ts = 80 ns
r/o logic

## Slide 40: Detector module
integration of:
silicon sensors,
front-end electronics,
read-out cables
into the building block of the STS:
“module”
71 (+3) components/module
non-reworkable assembly
high-yield components essential
 most work-intensive and critical part of STS construction effort:
896 modules required

## Slide 41: Module assembly
TAB bonding of microcables to ASICs and sensors
dummy components (sensor, ASICs, FEBs)

## Slide 42: Carbon fiber ladders

## Slide 43: Engineering: units/cabling/cooling
Front-end Electronics Boards
Read-out Boards, Power Boards
FEB stack 200 W
bi-phase CO2 cooling system
STS electronics total: 42 kW
Cooling plate
ongoing activity

## Slide 44: Engineering: units/cabling/cooling
rail
slide bearing
C-frame
distance piece
ongoing activity

## Slide 45: STS performance simulation
track reconstruction efficiency
momentum resolution
detailed, realistic detector model based on tested prototype components
CbmRoot simulation framework
using Cellular Automaton / Kalman Filter algorithms

## Slide 46: Summary
Heavy-ion physics  nucleus-nucleus collision physics
  investigation of the properties of nuclear matter in collisions of nuclear beams
  high charged particle multiplicities, embedded in those: “rare probes”
    challenge: charged-particle tracking, decay topology recognition,
    additionally: micro vertex detection
Silicon detectors can meet the tracking requirements:
  fine segmentation, low material budget, read-out, radiation tolerance
  challenge: keep the sensor benefits in a realistic detector system
  examples of two upcoming systems overviewed: ALICE-ITS Upgrade, CBM-STS
Outlook: New technologies are emerging that will allow forthcoming projects to push system performance even closer to physical limits: thinner passive structures, innovative cooling, new electronics concepts etc ...

## Slide 47: References/further reading
Heavy –Ion physics
  J. Bartke, Introduction to Relativistic Heavy Ion Physics, World Scientific (2008)
  Compressed Baryonic Matter in Laboratory Experiments, Lecture Notes in Physics, Vol. 814 (2011), Electronic Authors version: http://www.gsi.de/documents/DOC-2009-Sep-120-1.pdf
Silicon Trackers
  ALICE ITS Upgrade, J. Phys. G: Nucl. Part. Phys. 41 (2014) 087002
  L. Musa, Upgrade of the ALICE Inner Tracking System, CERN Detector Seminar, 17 April 2015, http://indico.cern.ch/event/317211/
  CBM STS Technical Design Report, GSI Report 2013-4 (2013), http://repository.gsi.de/record/54798
  The STAR Heavy Flavor Tracker - Conceptual Design Report, STAR Note 0600 (2011), https://drupal.star.bnl.gov/STAR/starnotes/public/sn0600
Vertex Detectors
  J. Heuser, Experience with the NA60 silicon pixel vertex tracker in a harsh radiation environment, Nucl. Instr. Meth. Phys. A 560, Issue 1 (2006) , 9-13
  M. Koziel et al., The prototype of the Micro Vertex Detector of the CBM Experiment, Nucl. Instr. Meth. Phys. A 732 (2013), 515–518